## Slide 1: IPv6 Hop-by-Hop Options for DetNet
Author(s): Pascal Thubert

## Slide 2: DetNet Dataplane Operations
DetNet defines its domain where DetNet information is significant
At each hop: Forwarding sublayer operation
  Associates a path to the flow
  Selects one next hop along that path
  Signals lower layer processing
  Perfect fit for the HbH Extension Header
At some hops: Service sublayer operation
  PREOF
  HbH is suitable since HbH can be ignored
  DO + SRH also suitable if SRH signals Service-sublayer relays

## Slide 3: Can DetNet use the IPv6 HbH Extension Header?
Using EH’s has gained traction recently
  See success of SRH with SRv6
  RFC 8200 allows routers to ignore HbH options (removed a MUST)
  "IPv6 Hop-by-Hop Options Processing Procedures" to make it even simpler
Less Complexity in Dataplane
  6-tuple is a complex key to read and use, and may be lost in tunneling / crypto
  EH comes naturally with tunneling at PE if end-systems not service-aware
  The HbH EH is always first after the IPv6 Header: simpler P4 / ASIC processing
IPv6 Header
DOH
Transport
header
SRH
…
payload
HbH

## Slide 4: DetNet dataplane requirements for IPv6
Redundancy Information for service sublayer
  Think sequence information but that’s too limitative
  No POF: Anything unique within the upper bound on out-of-order packet delivery
  If POF: Anything strictly ordered for the duration of the path, e.g., time stamp
  Network Coding: multiple fragments that can be delivered in any order
Path Information for both forwarding and service sublayer
  Path Information provides a scope for redundancy information
  DetNet places flows on paths (water and pipe analogy), and forwards along paths
  Same path  same DetNet treatment and fate share for all flows and OAM
  A PREOF path is not a linear sequence of nodes (terminology issues in sight)

## Slide 5: A native IPv6 signaling for DetNet dataplane
The draft allows placing DetNet info in IPv6 Hop-By-Hop Extension Header
DetNet information available early in the packet and easy to grab
  No need to dig down to transport header to find port info
Signals the path and PHB independently of the transported flows
  Enables tunneling, OAM, and flow aggregation with common treatment
Fits IPv6 architecture to coexist with other IPv6 extensions e.g., SRv6
Fits DetNet architecture whereby edge nodes assign DetNet flows "to specific paths through a network“ [RFC 8655]

## Slide 6: Current version is 06
First personal submissions in quick sequence
  Early comments on applicability and option details
DetNet Redundancy Information Option
  Sequence but but not only (e.g., time, include Net coding)
  Could be placed in DO if/when SRH signals service sublayer
DetNet Strict Path Option
  DetNet forwarding layer is strict
DetNet Loose Path Option
  Relaxed to traverse non-service-aware
  Could/Should be fully replaced by SRH