## Slide 1: Announcing Prefixes
Pascal Thubert
RFC 8505 ++
IETF 113
Remote

## Slide 2: 6LoWPAN ND (IPv6 Stateful Address Autoconfiguration)
  RFC 6775 (original 6LoWPAN ND)
        Defines ARO for registration and DAD operations for stateful AAC
  RFC 8505 (extended 6LoWPAN ND)
        Extends ARO, updates the registration procedure
        Allows registering to network services inc. proxy
  RFC 8928 (Address Protection for ND)
        Secures ownership and enables SAVI
  RFC 8929 (Backbone Router – proxy ND)
        Defines a proxy ND operation. Updates EDAR to transport ND options such as SLLAO.
  draft-thubert-6lo-unicast-lookup (Unicast Address lookup on backbone)
        Allows the 6LBR to respond to lookups and saves broadcasts
  draft-ietf-6lo-multicast-registration (Anycast and Multicast Address Registration)
        Registers anycast and multicast addresses (in addition to unicast per RFC 8505

## Slide 3: Redistributing RFC 8505 in routing ?
Already done for host routes with the “R” flag
  e.g., RFC 9010 into RPL, or even RFC 8929 into IPv6 ND
  Also draft-thubert-bess-secure-evpn-mac-signaling using BGP, or RIFT
  Provides a host / router interface that is agnostic to the IGP beyond the router

## Slide 4: Multi-link Subnet Routing (non-storing mode)
A
B
C
D
Parent is default GW, propagates root PIO (L-bit off)
Parent Address in the PIO (with R bit)
RPL Router autoconfigures Address from parent PIO
RPL Router advertises Address via Parent to Root
Root recursively builds a Routing Header back
B:
::/0 via A::A
A::A connected
A::B self
A:: ~onlink
C:
::/0 via A::B
A::B connected
A::C self
A:: ~onlink
D:
::/0 via A::B
A::B connected
A::D self
A:: ~onlink
Target A::C via
Transit A::B
A::B
A::C
A::D
A::A
A: (root)
A::A self
A::B connected
A::C via A::B
A::D via A::B
A:: ~onlink
A::C via A::B connected

## Slide 5: RFC 9010 (RUL)
A
B
C
D
6LR advertises A:: in RAs
6LN autoconfigures A::L
6LN registers A::L with « R » flag set
6LR injects the address as external host route in RPL
C:
::/0 via A::B
A::B connected
A::C self
A:: ~onlink
Target A::L via
Transit A::C (Ext)
A::B
A::C
A::D
A::A
A: (root)
A::A self
A::B connected
A::C via A::B
A::L via A::C
A::D via A::B
A:: ~onlink
A::C via A::B connected
A::L
RPL
RPL
RFC 8505
A::L via

## Slide 6: But… prefixes?
  Hosts may own prefixes
    Network in Node / recursive networking
    Kubernetes / Private IPv4 realms

## Slide 7: Owned prefix routing (non-storing mode)
A
B
C
D
Parent is default GW, advertizes owned PIO (L bit on)
RPL Router autoconfigures Address from parent PIO
RPL Router advertises Prefix via Address to Root
Root recursively builds a Routing Header back
B:
::/0 via A::A
A:: connected
B:: connected
C:
::/0 via B::B
B:: connected
C:: connected
A: (root)
A:: connected
B:: via A::B
C:: via B::C
D:: via B::D
D:
::/0 via B::B
B:: connected
D:: connected
Target C::/ via
Transit B::C
D::3 via B::D via A::B connected
A::B
B::C
B::D
B::B
A::A
D::3

## Slide 8: Owned prefix routing (non-storing mode)
A
B
C
D
C:
::/0 via B::B
B:: connected
C:: connected
A: (root)
A:: connected
B:: via A::B
C:: via B::C
D:: via B::D
Target C::/ via
Transit B::C
C::L via B::C via A::B connected
A::B
B::C
B::D
B::B
A::A
D::3
L::
????
C::L is reachable but L:: is not
Missing equivalent of RFC 8505/9010 for prefixes
C::L
L:: unreachable

## Slide 9: What becomes of DAD?
  Need to consider prefix aggregation and nesting
    Provisioned Mobile Networks should be unique
    Auto-allocation?

## Slide 10: How would that work?
RS replaces NS
Stub registration option replaces EARO

## Slide 11
6LR
LP Node
RS (SRO, CIPO*, Nonce and NDPSO**)
ToR
Calico
Challenge round trip
RA (SRO(status=0))
RS (target = IPv6 address, SRO (ROVR=Crypto-ID PoO))
RA (SRO(status=Validation Requested), Nonce)
* Crypto-ID Parameters Option
** NDP Signature Option
EDPR
EDPC
MS/MR
LB DNS
vSwitch
Fabric
RS replaces NS
Stub Registration Option
Duplicate Prefix R/C replaces DAR / DAC

## Slide 12
ToR (leaf)
Server
6LBR
6LR
IPAM
Container
MS/MR
L-B DNS
Provision IPv6 prefix 2001:db8:1::/96 for subnet 10.1.0.0/28 in tenant VRF
Provision IPv4 tenant-global subnet 10.1.0.0/28
RS (StubRegOption, R=1 lifetime, sequence, PoO)
RA(SRO, status = 0)
vSwitch
Ethernet
Fabric
Advertise (IGP, eVPN)
EDPC
EDPR

## Slide 13: Sorry, getting gory…
Adding stub prefix advertisement vs. host today
  Indicate prefix type e.g., a /96 to embed an IPv4 address
  Proof of ownership (PoO) per RFC 8928
Adding policy / ACLs
  Signal partial micro-segmentation (offload), who can talk to me
Adding metrics to influence load balancing
  worker capacity (clusters / containers)
  Access bandwidth /
  multihoming / preferred interface / anycast
Tenant ID / VRF ID / RPL instanceID
  Route tags, RH

## Slide 14: Go? No-Go?

## Slide 15: Ask
Should we go for it
  Indicate prefix type e.g., a /96 to embed an IPv4 address
  Proof of ownership (PoO) per RFC 8928