## Slide 1: Reliable and Available Wireless Architecture
Presenter: Pascal Thubert
Authors: P. Thubert, G.Z. Papadopoulos, (+ contributors)

## Slide 2: Reliability & Availability vs. Energy & Bandwidth
Due to uncontrolled interferences, including the self-induced multipath fading, deterministic networking can only be approached on wireless links.
The radio conditions may change -way- faster than a centralized PCE can adapt and reprogram, in particular when the controller is distant and connectivity is slow and limited.
RAW separates the path computation time scale at which a complex path is recomputed from the path selection time scale at which the forwarding decision is taken for one or a few packets.
RAW operates at the path selection time scale. The RAW problem is to decide, within the redundant solutions that are proposed by the PCE, which will be used for each packet to provide a Reliable and Available service while minimizing the waste of resources.
Controller
Wireless
network
FAST
SLOW
LARGE
SMALL
SLOW

## Slide 3: RAW Architecture / Framework Split
Architecture: what we will do, the broad picture before the work
  Terminology
  Reliability and availability in the context of the IETF
  Conceptual Model with OODA Loop,
  Introducing the Path Selection Engine (PSE)
Framework: How we did it, selected building blocks and their interaction
  Use cases and requirements served
  Scope of the work / applicability
  Identifying Tracks, Paths, and Flows
  Source Routing vs distributed PSE
  OAM and metrics

## Slide 4: Path and Complex Path (the experience)
  The general acceptance of a path is a linear sequence of nodes, as opposed to a multi-dimensional graph, defined by the experience of the packet that went from a node A to a node B (see the definition of "path" in section 1.1 of [RFC9049]).
  With DetNet and RAW, a packet may be duplicated, fragmented and network-coded, and the various byproducts may travel different paths that are not necessarily end-to-end between A and B; we refer to that experience as a complex path.
  The complex path does not fit the traditional description of a path; it is subject to change from a packet to the next.
  This is why we introduce below the term of a Track as the overall topology where the possible complex paths are all contained.

## Slide 5: Track (the piping)
  A networking graph that can be followed to transport packets with equivalent treatment; as opposed to the definition of a path above, a Track represents not an experience but a potential, is not necessarily a linear sequence, and is not necessarily fully traversed (flooded) by all packets of a flow. It may contain multiple paths that may overlap, fork and rejoin, for instance to enable the RAW PAREO operations
  In DetNet [RFC8655] terms, a Track has the following properties:
  A Track is a layer-3 abstraction built upon P2P IP links between routers. A router may form multiple P2P IP links over a single radio interface.
  A Track has one Ingress and one Egress nodes, which operate as DetNet Edge nodes.
  A Track is reversible, meaning that packets can be routed against the flow of data packets, e.g., to carry OAM measurements or control messages back to the Ingress.
  The vertices of the Track are DetNet Relay nodes that operate at the DetNet Service sublayer and provide the PAREO functions.
  The topological edges of the graph are serial sequences of DetNet Transit nodes that operate at the DetNet Forwarding sublayer.

## Slide 6: Flow (the water)
  A collection of consecutive IP packets defined by the upper layers and signaled by the same 5 or 6-tuple.
  Packets of the same flow must be placed on the same Track to receive an equivalent treatment within the Track.
  Multiple flows may be transported along the same Track.
  The subTrack that is selected for the flow may change over time under the control of the PSE.

## Slide 7: OODA Loop
The OODA Loop Enables Continuous Adaptation to Continuously Changing Situations:
Observation: the collection of data by means of the senses
Orientation the analysis and synthesis of data to form one’s current mental perspective
Decision the determination of a course of action based on one’s current mental perspective
Action the physical playing-out of decisions
Source: https://imarcai.com/ooda-loop-new

## Slide 8: The Conceptual Model
OODA loop with 3 new steps:
  Observe (OAM), Orient (PCE),
  Decide (PSE), Act (PAREO)
PSE:
  DetNet to signal Flow information
  RAW-SRv6 to hint/control DetNet Service Layer
  PSE operate at Track Ingress only (control)
  PSE may be partially distributed (hint)
  PSE may be fully distributed (No SRv6 signaling)
DetNet Service Plane
  Enrich DetNet (PAREO, timing, SR hint/control)
Redundant Radio Access
Packet flow / SR, IPPM
Feedback / DLEP, OAM
PSE at Ingress (headend)
(PSE) DetNet Service Layer

## Slide 9: RAW within (and vs.) DetNet
RAW operates at the DetNet Service Layer in the Network Plane
Controller Plane Functions compute complex Tracks
RAW observes a selection of L2 Links (the others are “infinite”)
RAW observes the L3 end-to-end operation
CPF CPF CPF CPF
Southbound API
_-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-
_-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-._-
RAW --z RAW --z RAW --z RAW
z-- Node z-- Node z-- Node z-- Node --z
Ingress --z / / z-- Egress
End \ \ .. . End
Node ---z / / .. .. . z-- Node
z-- RAW --z RAW ( non-RAW ) -- RAW --z
Node z-- Node --- ( Nodes ) Node
... .
--z wireless wired
z-- link --- link
Notes: RAW inherits the conceptual model described in section 4 of the DetNet Architecture [RFC8655]. RAW extends the DetNet service layer to provide additional agility against transmission loss. A Controller Plane Function (CPF) called the Path Computation Element (PCE) [RFC4655] interacts with RAW Nodes over a Southbound API. The RAW Nodes are DetNet relays that are capable of additional diversity mechanisms and measurement functions related to the radio interface, in particular the PAREO diversity mechanisms. The PCE defines a complex Track between an Ingress End System and an Egress End System, and indicates to the RAW Nodes where the PAREO operations may be actionned in the Network Plane. The Track may be expressed loosely to enable traversing a non-RAW subnetwork. In that case, the expectation is that the non-RAW subnetwork can be neglected in the RAW computation, that is, considered infinitely fast, reliable and/or available in comparison with the links between RAW nodes.

## Slide 10: RAW Architecture: the PSE
RAW defines the path selection engine (PSE) that performs rapid local adjustments of the forwarding tables to avoid excessive use of the resource diversity that the PCE proposes
Exploiting richer forwarding capabilities with PAREO and scheduled transmissions
 | PCE (not in scope) | PSE (in scope)
Operation | Centralized | Source-Routed or Distributed
Communication | Slow, expensive | Fast, local
Time Scale | Long (hours, days) | Short (sub-second)
Network size | Large, many Tracks to compute | Small, within one Track
Metrics | Averaged, Statistical, Shade of grey | Instant values / boolean state

## Slide 11: The PSE “Stack”
|
packet | going
down the | stack
+==========v==========+=====================+=====================+
| (iOAM + iCTRL) | (L2 Triggers, DLEP) | (oOAM) |
+==========v==========+=====================+=====================+
| Learn from Learn from |
| packet tagging end-to-end |
+----------v----------+ OAM packets |
| Forwarding decision < +---------^-----------|
+----------v----------+ | Enrich or |
+ Retag Packet | Learn abstracted > Regenerate |
| and Forward | metrics about Links | OAM packets |
+..........v..........+..........^..........+.........^.v.........+
| Lower layers |
+..........v.....................^....................^..v........+
frame | sent Frame | L2 Ack oOAM | | packet
over | wireless In | In | | and out
v | |
Notes: The PSE sits in the DetNet Service sub-Layer of Edge and Relay Nodes. On the one hand, it operates on the packet flow, learning the Track and path selection information from the packet, possibly making local decision and retagging the packet to indicate so. On the other hand, the PSE interacts with the lower layers and with its peers to obtain up-to-date information about its radio links and the quality of the overall Track, respectively.

## Slide 12: Status
02: split architecture / framework after IETF 112
03: Fabrice’s review
  Clarification and reformulations (e.g., short range radios)
  Forward references between sections 1 and 4
  Promiscuous vs. multicast
04: Dave’s pre-WGLC review
  Why @ L3 ? (technology diversity, increased spatial and spectrum diversity)
  Positioning vs. DetNet (add DetNet Service Sublayer services)
  Scope, clarify that multiple wireless access(es) is in scope
Editor’s view: Ready for WGLC

## Slide 13: Questions ?