## Slide 1: Mobility Capability Negotiation as a 5G Mobility Pattern draft-yan-dmm-man-10
Presenters: Jianfeng Guan and Zhiwei Yan
@IETF 116
Notes: Actually, this draft was discussed about twice or three times in the past. But with the development of 5G and the related mobility function extensions, we think it can be a part of the 5G mobility management information.

## Slide 2: Categories
PMIPv66
F-PMIPv66
DMM-PMIPv66
GTP6
HIP 6
MIPv66
FMIPv66
DS-MIPv66
DMM-MIPv66
DS-PMIPv66
HMIPv66
NEMOv66
PMIPv6 MIPv66
PMIPv6 Suite
MIPv6
Suite
Network based
Host
based
MOBIKE 6
PMIPv6: the network-based mobility management protocol specified by RFC5213
PMIPv6 Suite Protocols: extensions based on PMIPv6
Network-based mobility management protocols: L3 mobility management protocols which have no functional requirements on the mobile node
MIPv6: the host-based mobility management protocol specified by RFC6275
MIPv6 Suite Protocols: extensions based on MIPv6
Host-based mobility management protocols: L3 mobility management protocols which have functional requirements on the mobile node
Notes: In order to clearly analyze the possible cases and actual requirements, the mobility management protocols are classified as the figure shows. From the large aspect, they can be classified into network-based and host-based. In each category, there are two classes. For example, in the network-based class, they are PMIPv6 and its extensions, the other type is other kinds of network-based protocols. Similar as in host-based class.

## Slide 3: Possible Cases
Host |  |  | Scenarios |  |  |  |  |  |  |  |  |  |  |  | Network |  | 
Network based | PMIPv6 suit | PMIPv6 |  |  |  |  |  |  |  |  |  |  |  |  | PMIPv6 | PMIPv6 suit | Network based
 |  | DS-PMIPv6 |  |  |  |  |  |  |  |  |  |  |  |  | DS-PMIPv6 |  | 
 |  | F-PMIPv6 |  |  |  |  |  |  |  |  |  |  |  |  | F-PMIPv6 |  | 
 |  | DMM-PMIPv6 |  |  |  |  |  |  |  |  |  |  |  |  | DMM-PMIPv6 |  | 
 | Others | GTP |  |  |  |  |  |  |  |  |  |  |  |  | GTP | Others | 
Host based | MIPv6 suit | MIPv6 |  |  |  |  |  |  |  |  |  |  |  |  | MIPv6 | MIPv6 suit | Host based
 |  | DS-MIPv6 |  |  |  |  |  |  |  |  |  |  |  |  | DS-MIPv6 |  | 
 |  | FMIPv6 |  |  |  |  |  |  |  |  |  |  |  |  | FMIPv6 |  | 
 |  | HMIPv6 |  |  |  |  |  |  |  |  |  |  |  |  | HMIPv6 |  | 
 |  | DMM-MIPv6 |  |  |  |  |  |  |  |  |  |  |  |  | DMM-MIPv6 |  | 
 |  | NEMOv6 |  |  |  |  |  |  |  |  |  |  |  |  | NEMOv6 |  | 
 | Others | HIP, MOBIKE |  |  |  |  |  |  |  |  |  |  |  |  | HIP, MOBIKE | Others | 
X
Y
Which protocol will be used?
Notes: Then there are many possible cases based on different capability and preference between host and the network. Then the question is a protocol should be selected when the host accesses the network initially or during handover.

## Slide 4: Principles
Priority 1: Follow network ability
Priority 2: Follow host preference
Priority 3: Support the functional extensions
Priority 4: Support the performance enhancements
In default: network based scheme if it can be supported
If the host prefers host-based protocols, a negotiation is executed to handover from network-based protocol to host-based protocol.
After initial attachment, a profile will be generated in the management store to record the selected or preferred protocol of this host.
When the handover happens, the network will check the selected or preferred protocol. But the network also needs to notify the host if the selected protocol cannot be supported herein.
Notes: We simply list some principles for the protocol selection, for example, in order to improve the efficiency and reduce the load on the terminal, the network based protocol should have higher priority. And besides, a scheme is needed in order to negotiate the capability and preference between terminal and network.

## Slide 5: Solution: as a part of 5G Mobility Pattern
The Mobility Pattern is a concept used by the AMF (Access and Mobility Management Function) to characterise and optimise the UE mobility with the aid of NWDAF (Network Data Analytics Function)
Intelligent mobility support
General mobility support
5G Mobility Pattern (TS 23.501)
Subscription of UE
Statistics of UE mobility
Network local policy
UE assisted information
Historical attachment
Moving trajectory
NWDAF (TS 23.288)
Statistics
predictions
Mobility capacity？
Notes: Mobility Pattern: . Due to the uneven space-time distribution of mobile data traffic and frequent user switching in the 5G system, the 5G core network function still has the problem of unbalanced load. Especially, when the UE accesses the 5G communication system or the UE moves between 5G base stations, the access network needs to allocate the access and handover requests of the UE to the AMF to carry and process them. To characterise and optimise the mobility pattern of UE, the subscription of the UE, statistics of the UE mobility, network local policy, and UE assisted information, or any combination of them should be analyzed according to 5G specification.
The AMF determines and updates Mobility Pattern of the UE based on subscription of the UE, statistics of the UE mobility, network local policy, and the UE assisted information, or any combination of them. The statistics of the UE mobility can be historical or expected UE moving trajectory. If NWDAF(Network Data Analytics Function) is deployed, the statistics of the UE mobility can also be analytics (i.e. statistics or predictions) provided by the NWDAF

## Slide 6
UE related analytics
3GPP TS 23.288
UE mobility analytics
UE Communication analyticas
Expected UE behavioural parameters
Related network data analytics
Abnormal behavior related network data analytics
NWDAF supporting UE mobility statistics or predictions shall be able to collect UE mobility related information from NF, OAM, and to perform data analytics to provide UE mobility statistics or predictions
In order to support some optimized operations, e.g. customized mobility management, traffic routing handling, RFSP Index Management, QoS improvement or Inactivity Timer optimization, in 5GS, an NWDAF may perform data analytics on UE communication pattern and user plane traffic, and provide the analytics results (i.e. UE communication statistics or prediction) to NFs in the 5GC.
Defines how a service consumer learns from the NWDAF the expected UE behaviour parameters as defined in clause 4.15.6.3 of TS 23.502 for a group of UEs or a specific UE
defines how to identify a group of UEs or a specific UE with abnormal behaviour, e.g. being misused or hijacked, with the help of NWDAF.

## Slide 7
Information | Source | Description
UE ID | AMF | SUPI
UE locations (1..max) | AMF | UE positions
>UE location |  | TA or cells that the UE enters (NOTE)
>Timestamp |  | A time stamp when the AMF detects the UE enters this location
Type Allocation code (TAC) | AMF | To indicate the terminal model and vendor information of the UE. The UEs with the same TAC may have similar mobility behaviour. The UE whose mobility behaviour is unlike other UEs with the same TAC may be an abnormal one.
Frequent Mobility Registration Update | AMF | A UE (e.g. a stationary UE) may re-select between neighbour cells due to radio coverage fluctuations. This may lead to multiple Mobility Registration Updates if the cells belong to different registration areas. The number of Mobility Registration Updates N within a period M may be an indication for abnormal ping-pong behaviour, where N and M are operator's configurable parameters.
UE access behaviour trends | AMF | Metrics on UE state transitions (e.g., access, RM and CM states, handover).
UE location trends | AMF | Metrics on UE locations.
UE Mobility information collected from 5GC
Service Data from AF related to UE mobility
Information | Description
UE ID | Could be external UE ID (i.e. GPSI)
Application ID | Identifying the application providing this information
UE trajectory (1..max) | Timestamped UE positions
>UE location | Geographical area that the UE enters
>Timestamp | A time stamp when UE enters this area
NOTE: The application ID is optional. If the application ID is omitted, the collected UE mobility information can be applicable to all the applications for the UE. | 
UE mobility analytics—Input Data
3GPP TS 23.288
Notes: Then we think the mobility capability should be considered as a kind of parameter during the UE mobility information collection. And furthermore, the more suitable and preferred mobility management protocol can be selected for the specific UE.
I know many of the guys are experts of 5G and we hope we can cooperate to design the details of this function.

## Slide 8
Thank you for your attention~
WG Adoption?
Notes: So, that’s all and thank you very much. And we also want to know is it possible for a WG adoption of this draft?