## Slide 1: Some refinements to RFC8345 OPSAWG, IETF117 draft-davis-opsawg-some-refinements-to-rfc8345
Authors:
Nigel Davis (ndavis@ciena.com)
Olga Havel (olga.havel@huawei.com)
Benoit Claise (benoit.claise@huawei.com)

## Slide 2: Summary of proposal in draft
To improve capability to support multipoint structures (both unidirectional and bidirectional (uni-bi))
  RFC8345 focusses on point to point unidirectional
  RFC8345 suggest use of a pseudo-node to deal with multipoint
There are many cases of both symmetric and asymmetric multipoint bidirectional and multipoint unidirectional network structures
  Practical experience with both service and network solutions has led to extensive use of multipoint uni/bi structures
  The digital map work has also led to a recognition of the need for multi-point uni/bi
The new draft proposes enhancements to the YANG and provides a sketch of the YANG (two alternatives)
  Considered to be backward compatible (needs validation)
  Multipoint uni/bi covers all unidirectional and bidirectional cases

## Slide 3: Experience and insight
Services are very often bidirectional even if asymmetric in flow rates
  Directional differences carried via properties of point and/or point pairs
Many transport technologies are bidirectional between termination
  There is often a return path or handshaking etc.
Device, management and controller models from other bodies and within implementations take advantage of multipoint uni/bi
  TMF MTNM, TL1, ONF TAPI, proprietary management solutions etc.
Multipoint uni/bi emphasises atomic units and provides an efficient instance model

## Slide 4: Basic enhancement (simple addition)
Yang tree with additions shown in red
Assumes two modes of operation
  Unidirectional using source/destination
  Multipoint uni/bi using point-list
When using point-list
  link-type references a spec
  Link-direction provides summary of points
In point-list
  point-id is unique and references the spec
  linked-node & linked-tp provides the same reference style as source/destination approach
  point-role provides a summary of spec pattern detail
  point-name may clarify role
  point-direction indicates direction of use
Note that a bidirectional tp may be connected to a unidirectional point (where half is used)
  In this model, bidirectional usage of a unidirectional TP pair would require two points
+--rw link* [link-id]
+--rw link-id link-id
+--rw source
| +--rw source-node? -> ../../../nw:node/node-id
| +--rw source-tp? leafref
+--rw destination
| +--rw dest-node? -> ../../../nw:node/node-id
| +--rw dest-tp? leafref
+--rw point-list
| +--rw points* [point-id]
| +--rw point-id string
| +--rw linked-node? -> ../../../nw:node/node-id
| +--rw linked-tp? leafref
| +--rw point-role? role-of-point
| +--rw point-name? string
| +--rw point-direction? direction-of-point
+--rw link-type? type-of-link
+--rw link-direction? direction-of-link
+--rw supporting-link* [network-ref link-ref]
+--rw network-ref
| -> ../../../nw:supporting-network/network-ref
+--rw link-ref leafref
Note that the YANG tree is not in the draft (the corresponding YANG is)

## Slide 5: Multi-point Uni/Bi compared to Pseudo Node
Link
TP
TP
TP
TP
TP
TP
TP
TP
Instances
Spec – showing 10 legal flows
Pseudo
Node
Pseudo node still needs spec to explain flows (this is not discussed in RFC8345).
Alternative is to overlay 10 unidirectional links.
BUT this does not explain contention at TPs
Spec can explain protection and sharing.
Instances

## Slide 6: Other areas for improvement mentioned but not covered by the draft
Termination direction (simple addition of optional direction property)
Specification of capability (complex challenging area, but insight from other work)
Links between networks (relatively simple with insights from other work)
Richness of navigation (requires refinement of statement of purpose)
Relationship roles (complex area, but insight from other work)
Generalized model of flow (challenging area, but insights from other work)
Layering and sub-layering (complex area, but insight from other work)

## Slide 7: Next Steps
Seek support for the draft and understand how to progress to making the adjustment to RFC8345
Consider the other areas for improvement mentioned in the draft and develop further drafts etc.

## Slide 8: Thank you!

## Slide 9: Abstract https://datatracker.ietf.org/doc/draft-davis-opsawg-some-refinements-to-rfc8345/
This draft provides a brief analysis of the current unidirectional
point-to-point approach to modeling of the link in RFC8345,
highlights why this is not sufficient and makes a proposal to enhance
RFC8345 YANG to support multipoint uni/bi links. The two alternative
enhancement approaches proposed are backward compatible. The
enhancement is such that it provides a uniform solution to modeling
all links that could, over time, replace the current unidirectional
point-to-point approach. The rationale for the change is based on
many years of practical experience, including challenges using
RFC8345 in actual solution development, and insight gained through
other standardisation efforts and deployments.