## Slide 1
Export of Energy Consumption Information in IPFIX
draft-yan-opsawg-ipfix-energy-consumption-01
PRESENTER
Jinjie Yan
ZTE Corporation
CO-AUTHOR
Jinming Li
China Mobile
WORKING GROUP
OPSAWG | IETF 125

## Slide 2
BACKGROUND
Global Drivers
Rising ConsumptionEnergy consumption has become a critical operational metric in modern data centers and networks, driven by:
sustainability requirements
cost efficiency demands
regulatory compliance
Operator Needs
Network operators need accurate, traffic-correlated power information to support:
energy-aware routing decisions
per-service energy cost accounting
fine-grained power optimization.
THE GAP: EXISTING PROTOCOLS
Current protocols (SNMP, NETCONF) rely on periodic polling
↓
Critical Flaw: Loss of causality between traffic events & energy consumption
↓
Impact: Delayed insights, unable to correlate power spikes with traffic bursts

## Slide 3
MOTIVATION: WHY IPFIX?
Limitations of Existing Approaches
SNMP & NETCONF
Request-response model with fixed polling intervals. Cannot establish causal binding between traffic events and power consumption.
YANG Push
Still fail to track traffic-induced power changes.
Data sampling is decoupled from data plane load dynamics.
IPFIX Advantages
Event-Driven
Binds metering directly to traffic events (e.g., flow expiration). Ensures timely and causal reporting.
Traffic-Correlated
Triggered by packet counts or active/inactive timeouts.
Extensible
Easy to add new Information Elements without protocol stack changes.
Core Insight: IPFIX’s event-driven architecture is naturally suited for traffic-correlated energy telemetry.

## Slide 4
OVERVIEW
Core Proposal
Defines six new IPFIX Information Elements to export energy consumption for physical entities in network devices.
Granularity & Metrics
Three levels: Device, Line Card, Port. Two types: Realtime (instantaneous) & Average (interval-based).
Key Characteristic
Traffic-driven export preserves causality between traffic events and energy consumption.
Target Applications
Energy-aware routing, per-flow energy auditing, and fine-grained power management.
Device Level
Line Card Level
Port Level

## Slide 5
NEW INFORMATION ELEMENTS
LEVEL
REALTIME (INSTANTANEOUS)
AVERAGE (INTERVAL)
Device
deviceRealtimePower
deviceAveragePower
Line Card
lineCardRealtimePower
lineCardAveragePower
Port
portRealtimePower
portAveragePower
EXPORT TRIGGERS
Packet Count
Export when N packets
are processed.
Active Timeout
Periodic export for sustained
low-rate traffic
Inactive Timeout
Export when flow ends.

## Slide 6
USE CASE 1: ENERGY-AWARE ROUTING
THE GOAL
Compute network paths that minimize total energy cost, not just latency or bandwidth.
THE PROBLEM
Traditional metrics are poor proxies for power. Polling is too slow to capture the power spikes caused by micro-bursts.
THE SOLUTION
Export RealtimePower triggered by traffic thresholds. This provides instantaneous power draw data directly correlated with specific traffic loads.
Traffic Burst
IPFIX Export
Controller Action
Result: Optimized "Green" Path Selection

## Slide 7
USE CASE 2: PER-FLOW ENERGY AUDITING
THE GOAL
Attribute energy costs to specific services or customers
THE PROBLEM
"Elephant flows" consume significant resources across multiple components, but traditional metering is only device-wide.
THE SOLUTION
Correlate 5-tuple flow keys with linecard and port energy IEs. Synchronized export ensures data alignment.
Traffic Flow (5-Tuple)
Port Power/Card Power
GRANULAR ACCOUNTING
Precise Billing & Carbon Auditing

## Slide 8
KEY INNOVATIONS
Traffic-Aware Collection
MECHANISM
Uses traffic events as the core triggering mechanism.
BENEFIT
Solves the asynchronous collection problem of polling; enables precise causal attribution.
Composite Templates
MECHANISM
Combines multi-level energy IEs (Device, Card, Port) with their identifiers.
BENEFIT
Synchronized collection of all relevant energy data in a single export event.
TECHNICAL BREAKTHROUGH
Bridges the gap between IPFIX’s event-driven capabilities and physical-layer telemetry, creating a standardized mechanism for traffic-correlated energy monitoring.

## Slide 9
Thank You
Questions and feedback are welcome
Jinjie Yan
yan.jinjie@zte.com.cn
Jinming Li
lijinming@chinamobile.com.cn