## Slide 1: SIDR Approach
SBGP and SoBGP represented different tradeoffs between processing load and levels of assurance
  A new WG (RPSEC) was formed to list set of functional requirements that a secured routing framework should address
  Working reached an agreement on using signed credentials to validate the function of route origination
  WG also stalled on the topic of path validation
  WG could not get to considering adherence to policy constraints
In 2005, SIDR was created
  IDR was pretty busy
  Had lots of BGP extensions in form of WG documents
  BGP Changes were time consuming and complicated
  WG Mandate for multiple implementations slowed the publication process
  New WG would be an easier approach as the design and prototypes for early RPKI and origin validation were done

## Slide 2: SIDR Approach
RPKI, ROV, and BGPSec work had something in common
  Separate Data outside BGP that can be used to validate (inband data of) BGP
  As opposed to, e.g. SO-BGP with in-band data, remember telco SS5 and Blue Boxes?
  Quick to deploy and get deployment experience
  Allowed this work to be developed in SIDR (outside IDR)

## Slide 3: Solutions
RPKI, ROV
  Separate Resource Public Key Infrastructure (RPKI)
    Managed by (IANA and) RIRs by acting as a Trust Anchors (TAs) and Certificate Authorities (CA)
  Used for verification of Origin AS authorization of a given prefix
  Backward compatible
  Incremental Deployment trivial
  Quick to deploy and get deployment experience

## Slide 4: Solutions
BGPSec
  Performs Path validation by using cryptographic signatures
    Stronger: Path Validation as well as Origin Validation
  Replaces standard AS_PATH with BGPsec_Path attribute
  Relies on RPKI to manage Keys and validate signatures
  Reasonably secure solution that is computationally expensive and results in creation of larger update messages

## Slide 5: Solutions
ASPA
  Validates the authenticity of the AS_Path information
  Differs from BGPSec which provides cryptographic proof of the path integrity
    Instead checks path integrity based on the AS relationships by leveraging RPKI infrastructure
  Computationally less expensive than BGPSec when performing path validation

## Slide 6: Alternatives
IRR
  Set of distributed public databases (maintained by RIRs) where network operators register their:
    Routing policies
    IP address ownership
  Policy is stored in the Routing Policy Specification Language (RPSL)
    Operators can query (whois) and access the data
  Used to generate automatic filters for the routers to ensure only valid routing data is accepted
  Helps in preventing route hijacking

## Slide 7: Alternatives
Peerlock
  Operates on a list of Tier-1 ASNs
  Filtering policy that rejects any routes with those Tier-1 ASNs coming from a customer session
  Manual mechanism that requires updates to the List periodically (out-of-band co-ordination)
ARIN’s Origin AS
  Opional ARIN directory that allowed IP address owners to list Authorised ASNs
  Allowed ISPs to validate Letter of Authority (LOA)
  Implemented as a Filtering Policy

## Slide 8
Thank you