## Slide 1: Use Cases and Requirements for Network Admission of AI Agent Instances
July 2026
IETF 126, Vienna
Chao Shang, et al.
Huawei / BUPT
Notes: This presentation introduces draft-shang-agent-network-admission-01.
The document is an individual Informational Internet-Draft.
The focus is not a new Agent-ID or a new authentication protocol. The focus is a deployment gap: how to bind a specific running Agent Instance to network traffic that an enforcement point can control.

## Slide 2
Agents call internal resources, tools, external models, and peers
Application proofs are checked after reachability exists
Legacy and non-HTTP services may not understand Agent identity
Many instances may share a host, IP, or gateway
Why agent admission is a network problem
Agent
Agent
Service
MCP Server
Enterprise APP
Home Device
Network
Agent
Agent
Gateway
Network admission adds an earlier control boundary; application authorization remains.
Notes: Agents increasingly create network connections across campus, cloud, enterprise, and Internet boundaries.
Application authentication remains necessary, but it is normally evaluated only after a path already exists and it depends on each destination understanding the credential.
The draft asks what the network must know before granting general reachability, while keeping application authorization as a separate layer.

## Slide 3
Implications
Device admission does not authenticate each Agent Instance
Source IP, source port, or a self-asserted Agent-ID is not proof
Different agents need different reachability policy
One IP address can represent multiple security subjects
Agent C
The network cannot attribute traffic to a specific Agent Instance
Agent A
Agent B
Gateway
Approved agents, unapproved agents, ordinary applications, and the user may share one attachment.
Other
Process
One device / one IP / many subjects
Notes: This is the first core problem.
Traditional admission binds authorization to a device, user, interface, tunnel, or address.
But a single device can run several approved and unapproved agents alongside ordinary processes.
Therefore the source IP cannot be treated as the agent identity. A trusted per-Agent Network Context is required.

## Slide 4
Why application-only is insufficient
Reachability exists before credential verification
Every destination must understand Agent identity
Scanning and bypass remain possible
Network EPs do not receive the result
Admission must precede general reachability
Current model
1. Network
reachability
2. Agent
Authentication
3. Service
Authorization
The network is already exposed before the application decides.
Notes: The second gap is timing.
An agent needs limited connectivity to identity, credential, attestation, remediation, and admission services.
It should not receive unrestricted enterprise or Internet reachability before admission completes.
The desired transition is from a constrained pre-admission state to Agent-specific reachability after the binding is installed.

## Slide 5
Shared Gateway
NAT / Proxy / Mesh
Shared gateways can erase the originating Agent Instance
Agent
Agent
Agent
Per-Agent origin becomes unclear
Only the gateway connection is visible
External Service
Pooling and multiplexing
HTTP/2
HTTP/3
NAT
Proxy
The gateway must preserve protected per-Agent context for every request.
Notes: The third gap appears at shared egress gateways.
Several agents may share one public address, a connection pool, or a multiplexed HTTP/2 or HTTP/3 connection.
Authenticating the gateway does not prove which Agent Instance caused a request.
The gateway must isolate per-Agent credentials and policy state, preserve the request-to-agent binding, and prevent bypass through another path.

## Slide 6
The missing function:
A verifiable Agent Binding
Authenticated Agent Instance
A particular running instance or continuity domain
Credential-key possession
Fresh proof bound to the admission session
Optional runtime evidence
Bound to the same instance key and context
Enforceable Network Context
Protected from reuse by another process
Finite lifetime
Renewal, revocation, migration, and termination
Result: Agent Binding
Identity and traffic attribution become enforceable
Notes: This is the central definition in the draft.
An Agent-ID is only an assertion until it is cryptographically bound to an authenticated key.
The admission result must then be bound to a Network Context that another local process cannot reuse.
Optional runtime evidence can be included, but it must bind to the same key and admission context. The result is finite-lived Agent Binding state.

## Slide 7
Functional model: verify, bind, enforce
1. Agent Instance
+ Evidence
2. Network Admission
Function
3. Network
Enforcement Point
Proves possession of the instance key and supplies optional runtime evidence
Verifies credential, freshness, evidence, and policy; then installs an Agent Binding
Maps Agent-ID, key, and attributes to an enforceable Network Context
The security property depends on the integrity of the complete path from authenticated key to Network Context.
Notes: The model has three logical roles.
The Agent Instance presents a fresh proof and optional evidence.
The Network Admission Function validates the material and decides whether to install a binding.
The Enforcement Point applies reachability policy using the Network Context.
These functions may be distributed across endpoint, controller, network device, and gateway; their physical location is not the defining property.

## Slide 8
Six core requirements derived from the use cases
1
Agent Instance authentication
Authenticate a particular running instance with fresh proof of possession—not only its user, host, image, or platform.
2
Binding to enforceable traffic
Bind the successful result to protected Network Context and distinguish traffic when agents share an attachment.
3
Shared-gateway attribution
Isolate per-Agent state and preserve the originating instance across pooled connections and multiplexed streams.
4
Admission, lifetime, revocation
Use constrained pre-admission connectivity, finite lifetimes, renewal, and prompt removal on change or termination.
5
Non-bypass and layered authorization
Prevent alternate paths; network admission constrains reachability but never implies unrestricted application authority.
6
Evidence, audit, privacy
Bind evidence to the same key and context; record lifecycle events while minimizing identifier scope and retention.
A secure architecture must protect both the cryptographic proof and the local mechanism that creates and uses the binding.
Source: draft-shang-agent-network-admission-01, Sections 5–8
Notes: The draft groups the requirements into six areas.
The key points are instance-level authentication, enforceable traffic binding, correct attribution through shared gateways, independent lifecycle, non-bypassability, and evidence with privacy-aware audit.
Importantly, successful admission means authenticated and constrained reachability. It does not grant broad application authority or automatically inherit all authority of the human principal.

## Slide 9
Security depends on the complete binding path
Who acts
Agent Instance
Agent-ID / instance key
fresh proof of possession
What is verified
Admission session
credential validity
freshness / anti-replay
What can be trusted
Optional evidence
same instance key
same admission context
What is enforced
Network Context
anti-reuse / anti-spoofing
policy and reachability
When it ends
Lifecycle + audit
expiry / renewal / revoke
terminate / migrate
Primary risk
A false association between an authenticated Agent-ID and traffic generated by another process, host, request, or stream.
Binding rule
Protect the complete path from instance key to Network Context; proof-of-possession helps only when the key and context are protected.
Privacy rule
Minimize identifier scope and retention; disclose only policy-required attributes and avoid unnecessary export of runtime evidence.
Source: draft-shang-agent-network-admission-01, Sections 7–8
Notes: The primary failure is false attribution: authenticated identity on one side, but traffic from a different entity on the other.
Proof-of-possession is insufficient if the private key can be copied or the Network Context can be reused.
The same binding discipline applies to attestation and to shared gateways.
Privacy also matters because stable identifiers can reveal relationships among a principal, agent, device, runtime, and destinations.

## Slide 10
This draft defines requirements—not a new protocol
IN SCOPE
1. Define the problem
Operational use cases
Agent Instance terminology
Admission and attribution gaps
Clarifies why application authorization and network admission are complementary.
IN SCOPE
2. State requirements
Authentication and binding
Lifetime and revocation
Non-bypass, audit, and privacy
Creates criteria for evaluating future architectures and protocol profiles.
OPEN DESIGN SPACE
3. Realize the binding
Network Context choices
Distributed NAF / EP placement
Reuse of existing IETF mechanisms
No new Agent-ID format, authentication protocol, OAuth grant, or routing extension is defined.
Discussion: Are the requirements complete, and which existing mechanisms can realize the binding?
Source: draft-shang-agent-network-admission-01, version -01, 6 July 2026
Notes: To close, the draft is deliberately requirements-focused.
It defines use cases, terminology, the missing binding function, requirements, and a functional model.
It does not define a new identity format, authentication protocol, OAuth grant, or routing extension.
The discussion questions are whether the requirement set is complete and how existing IETF mechanisms can be composed to realize a non-bypassable, privacy-aware Agent Binding.