## Slide 1
© 2009 Wichorus Inc. All rights reserved.
© 2009 Wichorus Inc. All rights reserved.
Address autoconfiguration for legacy hosts in a MANET
[autoconf] WG
IETF 79 / November, 2010
charliep@wichorus.com
thomas@thomasclausen.org

## Slide 2: Problem statement
It should be possible to configure addresses for IPv6 end-hosts in an ad-hoc network
This can be done even for “legacy hosts” running DHCPv6 or Stateless Address Autoconfiguration (SLAAC)
Enabling this does not by any means “solve” the address autoconfiguration problem for MANETs, but it does allow MANETs to include existing IPv6 hosts as viable participants
<number>
© 2009 Wichorus Inc. All rights reserved.

## Slide 3: DHCP legacy hosts
If node broadcasts a DHCP Solicit message, a MANET router can intercept it and “pretend” to be a DHCP server.
The router can then allocate an address from its “pool” of addresses, but with a very short prefix.
What goes on behind the scenes to make this work consistently does not have to be made visible to the legacy host.
Alternatively, MANET router can broadcast DHCP Advertise, etc.
<number>
© 2009 Wichorus Inc. All rights reserved.

## Slide 4: Legacy hosts running SLAAC
A legacy host can transmit a Router Solicitation
Any MANET router receiving the Router Solicitation can supply the appropriate routing prefix in a unicast Router Advertisement.
As before, the legacy host does not have to be involved with transactions “behind the scene”.
The router would presumably invoke the [autoconf] address configuration solution before responding with the Router Advertisement.
<number>
© 2009 Wichorus Inc. All rights reserved.