## Slide 1: ARP Traffic Study
Jim Rees, Manish Karir
Research and Development
Merit Network Inc.

## Slide 2: Outline
Goals
Experiment Setup and Architecture
Experiments
  Scanning
  Number of hosts
  Traffic load/patterns
  Host failures
  VM Migrations
  Emulator
Conclusions

## Slide 3: ARP/ND Traffic Study
Attempt to understand ARP behavior under various conditions
Recreate various environments and observe ARP/ND traffic
Build a model of ARP/ND based on experiments and collected data
Build scalable ARP/ND emulator for large scale experiments which can mimic various environments for evaluating software/protocol impact, and perhaps proposed solutions

## Slide 4: Network Topology

## Slide 5: Experiment Setup
VMWare Cloud Director
  Resource Pool – 100GHz, 200GB RAM, 3TB Disk
  60 Vapps with 10 VMs each
  Each VM 4G disk 256MB RAM – Centos 5.5
  Single flat network topology /22 network block
  Roughly 500 VMs used in tests
Herding the bot
  Write command/control agent/controller software
  Allows us to issue commands to all bots to start/stop services
  Write traffic generator software to generate internal and external traffic load via a traffic matrix

## Slide 6: Traffic Generator
Runs on up to 500 hosts
Each host listens for commands from controller and also runs web server
Bot controller sends UDP broadcast message hosts to start/stop (no ARP traffic)
Each host has list of other hosts to contact
For each host on list:
  wget https://host (v4/v6)
  sleep(n seconds - configurable)
Host list updated on each host prior to experiment

## Slide 7: Initial Experiments
Effect of external scans
Effect of number of hosts and relative traffic load
Effect of machine failures
Effect of traffic load with same number of hosts
Effect of VM migrations
IPv6 neighbor discovery behavior (for all above)

## Slide 8: I: Effect of External Scans
nmap scans from outside the network
Measure ARP/ND traffic spikes
Monitor CPU load on access switch
Possible to cause transient spikes in ARP/ND traffic
Effect on CPU load is greater for ARP than ND
IPv4
IPv6
CPU Load:
Normal: 10, Peak: 20
CPU Load:
Normal: 10, Peak: 30

## Slide 9: I: Effect of External Scans (single)
CPU Load
Combined ARP/ND Traffic Rate

## Slide 10: II: Effect of Number of Hosts
Starting up up to 500 hosts 100,200,300,400,500
Stop all hosts in between batch starts
Measure startup ARP/ND traffic and CPU Load
Increase overall traffic load roughly 5x from 100 – 500 hosts
Initial spike in CPU load similar for both v4/v6
Roughly linear increase in ARP/ND traffic
Higher ARP traffic rate as compared with ND
IPv4
IPv6
100
200
300
400
500
100
200
300
400
500
CPU Load ~ 40
200 pps
200 pps
CPU Load ~ 40

## Slide 11: IIb: Effect of Traffic
Starting up 500 hosts
Hosts attempt to contact varying number of active/inactive hosts (500/0, 400/100, 300/200, 200/300, 100/400)
Highest possible rate zero sleep
Stop all hosts in between changes to traffic pattern
Measure startup ARP/ND traffic and CPU Load
Initial spike in CPU load slightly higher for both ARP
CPU load spike roughly same across traffic patterns
Roughly linear increase in ARP/ND traffic
Higher ARP traffic rate as compared with ND
500/0
100/400
300/200
500/0
100/400
300/200

## Slide 12: IIc: Effect of Number of Hosts/Traffic
Starting up all 500 hosts
Contact list includes all 500 hosts plus a varying number of inactive hosts(0, 100, 200, 300, 400)
Sleep 2 seconds between connects
Stop all hosts in between experiments
Measure startup ARP/ND traffic and CPU Load
Initial spike in CPU load similar for both v4/v6
Roughly linear increase in ARP/ND traffic
Slight increase in CPU load for v6
Higher ARP traffic rate as compared with ND
500+0
500+400
500+200
500+0
500+400
500+200

## Slide 13: IId: Effect of Traffic Load
Start Traffic generator on 500 hosts
Vary the amount of load by reducing time between communication events (50, 20, 10, 5, 2, 1 seconds)
Measure ARP/ND Traffic and CPU load on switch
ARP/ND increases roughly linearly across experiments
50 20, 10, 5, 2, 1
50 20, 10, 5, 2, 1

## Slide 14: III: Effect of Machine Failures
Start Traffic generator on 400 hosts, 80 targets
Shutdown targets in groups of 10
Measure ARP traffic and CPU Load
ARP traffic increases as number of failed machines increases
10, 20, 30 , 40 , 50 , 60, 70

## Slide 15: IV: Effect of VM Migrations
Start Traffic generator on 500 hosts
Roughly 36 VMs on 1 blade
Place blade into maintenance mode forcing all VMs on that blade to migrate to other blades
Measure ARP Traffic

## Slide 16: V: Highest possible Load
Start traffic generator on 500 hosts
All hosts communicate with all other hosts as fast as possible (sleep interval = 0)
30 second test
Maximum 4K pps of ARP pkts and a CPU load of 65

## Slide 17: Emulator Topology
Emulator has two parts, a sender and a responder

## Slide 18: Emulator Validation
Real (top) vs emulator (bottom)

## Slide 19: High Emulator Load
8000 pps for 30 minutes
Equivalent to several thousand real hosts depending on traffic profile
Sustained 70% switch cpu load

## Slide 20: Conclusion and Next Steps
There appears to be roughly linear relationship between ARP traffic and number of hosts and traffic
There can be scenarios where machine failures in a data center can lead to higher ARP traffic rates
Overall ND appears to be lower impact than ARP in terms of traffic volume, number of hosts, and CPU load on access switch as compared with ARP
Detailed analysis of collected ARP/ND traffic
Build model of ARP/ND traffic behavior based on experimental data
Build ARP/ND traffic emulator software to scale up the experiments
Move away from limitations of managing real VM hosts
Repeat measurements for live production environment and compare with our experimental setup