## Slide 1: Address Resolution Issues Induced by VPN-oriented Data Center Service http://tools.ietf.org/html/draft-so-armd-vdcs-ar-00 http://datatracker.ietf.org/doc/draft-so-vdcs/
Ning So ning.so@verizonbusiness.com
Linda Dunbar linda.dunbar@huawei.com

## Slide 2: What Is VDCS
VPN-oriented Data Center Services (VDCS) are the extensions to the existing L2 and L3 VPN services into data centers and to control the virtual resources sharing functions
  Strictly maintaining the secure, reliable, and logical isolation characteristics of VPN
  Making the data center resources as additional attributes to VPNs
  Allowing end-to-end VPN-based service management
  VPN having the control on how and what data center resources to be associated with the VPN

## Slide 3: Address Issues Induced by VPN-o-DS
Address scalability
Address conflict
Notes: Traditional VPN’s end points are Access routers at customer premises. All the hosts belonging to a VPN are behind the access routers.  VPN hosts are hidden from VPN service providers
When VMs in Data Centers are attached to a VPN, VMs belonging to the VPN will be instantiated to the VMs in Data Center(s).  VPN attached hosts/VMs, especially the ones hosted in the provider’s data center, are exposed to VPN service providers.
  There can be a lot of those hosts associated with various VPNs.
  For any given VPN, the associated VMs could belong to one or multiple subnets, and their IP addresses could be pre-configured or dynamically assigned.
Address Resolution for those VPN hosts is critical to VPN-oriented Cloud Services

## Slide 4: VPN-o-DCS Logical View
Data Center
LAN Switch
VM
User
Desktops
LAN
Switch
CE
Router
VPN Edge Router
User
Desktops
LAN
Switch
CE
Router
VPN Edge Router
User
Desktops
LAN
Switch
CE
Router
VPN Edge Router
User
Desktops
LAN
Switch
CE
Router
VPN Edge Router
IP/MPLS network
Data Center VPN GW Router
Data Center
10.1.x
20.2.x
100.3.x
200.4.x
The number of address to manage is very large

## Slide 5: Scalability issues L2VPN’s VMs offload to data center
L2VPN’s PEs and VSIs have to learn and maintain the MAC &VLAN for all the hosts/VMs associated with this L2VPN.
When there are 100’s (1000’s) VPNs offload VMs to provider data center(s), the amount of MAC&VLAN <-> IP mapping for the PE is extremely large.

## Slide 6: Scalability issues L3VPN’s VMs offload to data center(s)
Scenario 1: offloaded VMs in DC are in different subnets than customer subnets
Scenario 2: offloaded VMs in DC are in same subnet as customer subnet.
  the traditional “subnet” concept is broken.
  the ARP/ND messages from the VMs in the data center have to be flooded to the corresponding sites to which those VMs belonging.
The data center gateway routers (CEs or PEs) have to handle both customer and data center IP/MAC addresses

## Slide 7: But the routing tables at PEs become more complicated - If Data Center hosts VMs for thousands of VPNs, gateway router has to maintain thousands of VRF tables.
VM
User
Desktops
VPN Edge Router
User
Desktops
VPN Edge Router
User
Desktops
VPN Edge Router
User
Desktops
VPN Edge Router
IP/MPLS network
DC VPN GW Router
Data Center
?.1.200.x
?.2.40.x
?.3.20.x
?.4.100.x
1
3
2
4
10.1.x
100.3.x
200.4.x
20.2.x
IP Address | Next Hop
10.1.200.x | DC VPN GW
10.1.x | VPN ER 1
10.2.20.x | DC VPN GW
10.2.x | VPN ER 2
10.3.20.x | DC VPN GW
10.3.x | VPN ER 3
10.4.100.x | DC VPN GW
10.4.x | VPN ER 4
IP Address | Next Hop
10.1.200.x | DC VPN GW
10.1.x | VPN ER 1
10.2.20.x | DC VPN GW
10.2.x | VPN ER 2
10.3.20.x | DC VPN GW
10.3.x | VPN ER 3
10.4.100.x | DC VPN GW
10.4.x | VPN ER 4
IP Address | Next Hop
10.1.200.x | DC VPN GW
10.1.x | VPN ER 1
10.2.20.x | DC VPN GW
10.2.x | VPN ER 2
10.3.20.x | DC VPN GW
10.3.x | VPN ER 3
10.4.100.x | DC VPN GW
10.4.x | VPN ER 4
IP Address | Next Hop
10.1.200.x | DC VPN GW
10.1.x | VPN ER 1
10.2.20.x | DC VPN GW
10.2.x | VPN ER 2
10.3.20.x | DC VPN GW
10.3.x | VPN ER 3
10.4.100.x | DC VPN GW
10.4.x | VPN ER 4
IP Address | Next Hop
10.1.200.x | DC VPN GW
10.1.x | VPN ER 1
10.2.20.x | DC VPN GW
10.2.x | VPN ER 2
10.3.20.x | DC VPN GW
10.3.x | VPN ER 3
10.4.100.x | DC VPN GW
10.4.x | VPN ER 4
IP Address | Next Hop
10.1.200.x | DC VPN GW
10.1.x | VPN ER 1
10.2.20.x | DC VPN GW
10.2.x | VPN ER 2
10.3.20.x | DC VPN GW
10.3.x | VPN ER 3
10.4.100.x | DC VPN GW
10.4.x | VPN ER 4
IP Address | Next Hop
10.1.200.x | DC VPN GW
10.1.x | VPN ER 1
10.2.20.x | DC VPN GW
10.2.x | VPN ER 2
10.3.20.x | DC VPN GW
10.3.x | VPN ER 3
10.4.100.x | DC VPN GW
10.4.x | VPN ER 4
IP Address | Next Hop
10.1.200.x | DC VPN GW
10.1.x | VPN ER 1
10.2.20.x | DC VPN GW
10.2.x | VPN ER 2
10.3.20.x | DC VPN GW
10.3.x | VPN ER 3
10.4.100.x | DC VPN GW
10.4.x | VPN ER 4
The DC GW Router has to keep 1000’s of VRFs

## Slide 8
Address Conflict:
  Addresses used by different VPN clients clash
  Clients require their own IP Addresses in Data Center

## Slide 9: Address conflict in L3VDCS
User
Desktops
LAN
Switch
CE
Router
VPN Edge Router
User
Desktops
LAN
Switch
CE
Router
VPN Edge Router
User
Desktops
LAN
Switch
CE
Router
VPN Edge Router
User
Desktops
LAN
Switch
CE
Router
VPN Edge Router
IP/MPLS network
10.1.x
10.2.200.x
100.12.x
10.120.4.x
10.130.x
101.3.20.x
170.4.x
170.4.100.x
Address conflict