## Slide 1: Content Splicing for RTP Sessions draft-xia-avtext-splicing-for-rtp-00
26/7/30
IETF#81, July 2011, Quebec City
Jinwei Xia xiajinwei@huawei.com

## Slide 2: Discussion on Maillist
26/7/30
In clearly user detectable case on RTP level
  Mixer includes the CSRC list in outgoing packets, which facilitates the system debugging.
  Majority of WG prefers the RTP mixer approach.
In likely user non-detectable case on RTP level
  Bring more complexity compared to detectable case whatever using mixer or translator.
  Mixer (not include CSRC list)
    Pros: straightforward on RTCP processing
    Cons: more overhead (regenerating timing model and its own RTCP even during non-splicing time), as well as has loop detection issue.
  Translator
    Pros: less overhead (simply rewrite the RTP sequence number after splicing has taken place and timing of original content unchanged).
    Cons: complex on RTCP processing, especially on bitrate adaptation.
  No clear preference on mailing list.

## Slide 3: Next Steps
26/7/30
Decide to use mixer in user detectable case.
Decide the final direction in user non-detectable case.
  Mixer, translator or both based solutions?
  Mixer seems to be more easily specified to realize this case because it is similar to user detectable case.
Submit single mixer based draft for both cases.