## Slide 1: BGP Data-Plane Benchmarking Applicable to Modern Routers
28 July 2011
BMWG@IETF81
<number>
Ilya Varlashkin
Rajiv Papneja
Bhavani Parise
presented by Grégory CAUCHIE
Notes: <number>

## Slide 2: Background/ Current Status
28 July 2011
BMWG@IETF81
<number>
Terminology for Benchmarking BGP Device Convergence in the (RFC 4098) / June 2005
Methodology draft focusing on the BGP Data Plane convergence was posted prior IETF 80
  http://tools.ietf.org/html/draft-papneja-bgp-basic-dp-convergence-01
  Not addressed (Missing item): Data-plane convergence on modern routers, which have local restoration capability
  Probable solution to address missing item: Proposing additional draft (may merge later) to be submitted prior to IETF 82
Notes: <number>

## Slide 3: Elaborating Missing Item
28 July 2011
BMWG@IETF81
<number>
Assumption was: packet flow restored – protocol converged
  This may NO LONGER be true – modern routers can restore traffic before protocols converge
  May not be applicable when mapped to modern routers
Notes: <number>

## Slide 4: Proposed Solution!
28 July 2011
BMWG@IETF81
<number>
Measure data-plane convergence at DUT (not behind) and do NOT call it BGP convergence
  Relevant to modern world
  By definition can be measured at data-plane
Measure BGP convergence only behind DUT, not at
  Still relevant even today
  Capture protocol packets rather than data-plane
  Use same reference clock for all timestamps
Notes: <number>

## Slide 5: Key points of methodology
28 July 2011
BMWG@IETF81
<number>
Eliminate or minimize dependence on non-DUT
DUT Detection time
DUT Reaction time
DUT Propagation time
Notes: <number>

## Slide 6: Two drafts
28 July 2011
BMWG@IETF81
<number>
DUT ability to tell routers, which depend on it, about new network topology
  Revised draft-papneja-bgp-basic-dp-convergence
  Either exact but in control plane,
  Or leveraging results from the new draft
DUT ability to send packets that already arrived to it
  New draft (pending upload to ietf.org)
  Strictly data-plane
Notes: <number>

## Slide 7: Current Draft Summary (draft-papneja-bgp-basic-dp-convergence-01)
BGP Data plane FIB convergence for both IPv4 and IPv6
Limited to Basic BGP convergence (RFC 4271 functionality with Multi-Protocol BGP (MP-BGP) for IPv6)
BGP Failure/Convergence Events
Considers dependencies on factors impacting convergence:
  Number of peers,
  Number of routes/peers
  Policy Processing/Reconfiguration
Data Traffic characterization – offered load
Various test cases that covers iBGP, eBGP and failure convergence events
Topologies – Several 3 node, and 4 node setups
Notes: <number>

## Slide 8: New draft summary
28 July 2011
BMWG@IETF81
<number>
Metrics derived from packets, not from clock
Single test procedure, 5 failure scenarios
  Loss of Signal on the link attached to DUT
  Attached link failure without LoS
  Non-direct link failure
  Best route withdrawal
  BGP next-hop failure
Background topological noise for realistic result
Large topology scenario
Notes: <number>

## Slide 9: Next Steps
28 July 2011
BMWG@IETF81
<number>
Current draft will be revised to focus only on “behind DUT”
Probably NOT data-plane
  Metrics obtained directly, not derived
Still data-plane
  Use results from new draft
Notes: <number>

## Slide 10: Action Items
28 July 2011
BMWG@IETF81
<number>
Can we agree on approach?
Post revised old draft and new draft before IETF82
Aim for WG-item readiness by IETF82
Inputs welcome!
Notes: <number>