## Slide 1: IMIX Genome
Al Morton
July 2011
draft-morton-bmwg-imix-genome-02

## Slide 2: Additional Tests with Variable Packet Sizes
Fixed Packet/Frame Size tests are currently required in RFC 2544, etc.
IF variable size testing is needed,
  Fully Specified
  Repeatability? How Important?
  Generally Specified if repeating sequence is too long for human comprehension (fraction, or number of frames@size for each size)

## Slide 3: Scope and Spec
Exact Sequence specification method
No Standard IMIX!!!
IMIX-aaafg has:
64,64,64,1280,1518
Also, frequency of a size
Size, bytes | Code Letter
64 | a
128 | b
256 | c
512 | d
1024 | e
1280 | f
1518 | g
MTU | h

## Slide 4: Feedback
Draft is useful, MTU size is useful
Previously Added Specification of fully Custom IMIX with sequence
Tester can specify IMIX Genome between any two entities in test
  Example with Blade configuration added
Jumbo Frame sizes added, with note about FCS issues

## Slide 5: Comments on the Genome Table
Added Jumbo sizes
No Standard IMIX!!!
What about PROTOCOL???
Size, bytes | Code Letter
64 | a
128 | b
256 | c
512 | d
1024 | e
1280 | f
1518 | g
2112 | h
9000 | i
16000 | j
MTU | z