## Slide 1: GMPLS RSVP-TE extensions for OAM Configuration
IETF-81 Quebec

## Slide 2: Background, Motivation and Objectives
Extend GMPLS CP to configure OAM entities
  Useful for any GMPLS controlled transport network
  Also a requirement for MPLS-TP LSPs
Avoid two separate management/configuration steps: connection setup followed by OAM configuration
  Additional delay and processing
  Prune to missconfiguration errors
Need to extend RSVP-TE signaling
  Maintenance entity identification parameters
  Configure OAM parameters (e.g., monitoring frequency)
  OAM control (e.g., admin down, disable/enable)

## Slide 3: CCAMP Documents
draft-ietf-ccamp-oam-configuration-fwk
draft-ietf-ccamp-rsvp-te-eth-oam-ext
draft-ietf-ccamp-rsvp-te-sdh-otn-oam-ext
draft-ietf-ccamp-rsvp-te-mpls-tp-oam-ext
4 CCAMP WG
documents
Base protocol spec (1)
Ethernet OAM (2)
MPLS-TP OAM (4)
SDH and OTN OAM (3)

## Slide 4: Next Steps
draft-ietf-ccamp-oam-configuration-fwk
  Stable, minor updates and two new OAM Function flags added
    FMS, PM/Throughput Measurement
  Ready for WG LC
draft-ietf-ccamp-rsvp-te-eth-oam-ext
  Ready for WG LC
draft-ietf-ccamp-rsvp-te-sdh-otn-oam-ext
  Ready for WG LC
draft-ietf-ccamp-rsvp-te-mpls-tp-oam-ext
  Stable, minor updates to increase the readability and to align to:
    draft-ietf-mpls-loss-delay
    draft-ietf-mpls-tp-cc-cv-rdi
  Ready for WG LC

## Slide 5: Changes on MPLS-TP OAM configuration draft [1]
Major changes in the following sections in order to de-emphasize BFD and have the same visibility for the whole set of tools:
  Section 1 – Introduction
  Section 2 – Overview of MPLS OAM
  Section 3 - Theory of Operations
Changes in BFD configuration:
  CC&CV functions are now part of the same functionality, it is not possible anymore to activate them separately
  Detect Multiplier has been deleted from the configurable parameters because it has been fixed to value 3 in draft-ietf-mpls-tp-cc-cv-rdi-05
  Encapsulation capability flags: allow to set either G-ACh encapsulation or UDP encapsulation
  Bidirectional/Unidirectional flag

## Slide 6: Changes on MPLS-TP OAM configuration draft [2]
New “Performance Monitoring TLV” in order to allow configuration flags for Loss, Delay and Throughput Measurements that can’t be handled in the corresponding sub-TLVs. Such flags are aligned with draft-ietf-mpls-loss-delay-04
D: Delay Inferred/Direct
L: Loss Inferred/Direct
J: Delay variation/jitter
Y: Dyadic
K: Loopback
C: Combined
Loss and Delay TLV are now sub-TLV of the new Performance monitoring TLV
Loss and Delay sub-TLVs have been updated in order to conform to the new version of draft-ietf-mpls-loss-delay-04