## Slide 1: Usage of The RSVP Association Object draft-ietf-ccamp-assoc-ext-00
Lou Berger <lberger@labn.net>
Francois Le Faucheur <flefauch@cisco.com>
Ashok Narayanan <ashokn@cisco.com>

## Slide 2: Question from last IETF: One draft or two?
draft-ietf-ccamp-assoc-info-01 covered:
  Informational usage for GMPLS recovery
  Standards track extensions for non-GMPLS recovery usage and Extended association
Discussed at IETF 80: Should Information and Standards track sections be separated? E.g.:
  “Usage of The RSVP Association Object”
  “RSVP Association Object Extensions ”
Consensus to separate
This presentation covers #2

## Slide 3: First sections moved from draft-ietf-ccamp-assoc-info-01
No Change
Non-Recovery Usage (Per IETF 76, 77)
  Standards Track
    But don’t modify usage for Recovery
    Provides informational guidance for Recovery
  Non-Recovery Usage
    Reuse recovery rules
      Match LSPs with identical ASSOCIATION objects
        All fields: Type, ID, & Source
      Multiple associations are possible all association objects need to examined.
    Applies to LSP and non-LSP forms of RSVP
  Allow for association based on Path or Resv messages
      Upstream Initiated Association (Path state matching)
      Downstream Initiated Association (Resv state matching)
      No cross-direction association

## Slide 4: Second sections moved from draft-ietf-ccamp-assoc-info-01
No Change
IPv4 and IPv6 Extended ASSOCIATION Objects
  Revised per plan discussed at IETF 79 (no changes since)
  Supports
    Association identifiers > 16 bits
    MPLS TP identifiers – ICC and Global ID
  Format:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Length | Class-Num(199)| C-Type (TBA) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Association Type | Association ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IPv4 Association Source |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Global Association Source |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
: . :
: Extended Association ID :
: . :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Global ID: <0> |
<2|4-byte ASN>
[<ICC> <0x00>] [<data>]
Per RFC 4872
>= 0 bytes,
32-bit
aligned
4 bytes

## Slide 5: Next steps
Draft is now stable
  Split resolved final open issue
Ready to move forward / LC
Comments?