## Slide 1: RSVP-TE Extensions to Establish Associated Bidirectional LSP
CCAMP/MPLS WG, IETF 81th, Quebec
draft-ietf-ccamp-mpls-tp-rsvpte-ext-associated-lsp-01
Fei Zhang Ruiquan Jing
Fan Yang Weilian Jiang

## Slide 2: Update
Describe the signaling procedure more clearly
Revision of asymmetric bandwidth LSPs
Revision of recovery scenario

## Slide 3: Single Sided VS Double Sided
 | One sided provisioning LSP1 triggers LSP2 | Double sided provisioning
Both LSPs do not exist | 2Tp | 2Tp
LSP1 exists, LSP2 needs to be established | 2Tp | 1Tp
LSP1 does not exist, LSP2 has been established | 2Tp | 1Tp
Both LSP1 and LSP2 exist | 2Tp | 1Tp
The associated time comparison of two solutions
  Tp are the time costs of path messages processing
Double sided provisioning is more efficient

## Slide 4: Asymmetric bandwidth LSP
 | One sided LSP1 triggers LSP2 | Double sided
Both LSPs do not exist | REVERSE_TSPEC object in LSP1’s Path Message | REVERSE_TSPEC object in LSP1 and LSP2’s Path messages
LSP1 exists, LSP2 needs to be established | REVERSE_TSPEC object in LSP1’s Path Message | REVERSE_TSPEC object in LSP1’s Path Message
LSP1 does not exist, LSP2 has been established | REVERSE_TSPEC object not needed | REVERSE_TSPEC object in LSP2’s Path Message
Both LSP1 and LSP2 exist | REVERSE_TSPEC object not needed | REVERSE_TSPEC object not needed
The complexity brought by asymmetric bandwidth
  The associated time is not changed
Single sided provisioning is more simple

## Slide 5: Recovery
LSP1 and LSP2 are associated together by LSP1’s identifier
  LSP3 is rerouted/refreshed with LSP2’s identifier
  LSP2 is refreshed with LSP2’s identifier
LSP1 and LSP2 are associated together by LSP2’s identifier
  LSP3 is rerouted/refreshed with LSP2’s identifier

## Slide 6: Next Steps
Updated based on discussion
  One sided provisioning or double sided provisioning?
Comments/Feedback?
