## Slide 1: RSVP-TE Extensions to Notification for Shared Mesh Protection
CCAMP WG, IETF 81th
draft-he-ccamp-notification-shared-mesh-protection-00
Wenjuan He (he.wenjuan1@zte.com.cn)
Fei Zhang (zhang.fei3@zte.com.cn)

## Slide 2: Motivation
Requirements
  R66/67/68/69 [RFC5654]
Benefits
  Reducing the number of network resources[tp-survive]
Solution gaps
  The processing of Shared Mesh Restoration was descried in [RFC4872], but Shared Mesh Protection was not covered.

## Slide 3: Shared Mesh Protection Planning
Operator plans the Shared Mesh Protection Group (SMPG)
  assign a group ID and a virtual address for the shared mesh protection group.
Association Object
  Association Type:Resource Sharing
  Association Source: SMPG virtual address
  Association ID :SMPG group ID
Protection Object
  Unchanged

## Slide 4: Protection Switching Notification
Node A/B switch the traffic from working path to protection
  Data plane Switching [linear-protection]
  Control Plane Switching [section-7 of RFC4872]
Node E send notify message to node C with error "notify error/resource occupied by the high priority" or "notify error/resource occupied by the low priority"
Node C MAY reroute or lock the protecting LSP.

## Slide 5: Reversion
Node A switches the traffic to W1 and refreshes the Path message
Upon receiving the Path message with the O bit clear, node E will send notify message with new error code/sub-code "notify error/ resource available" to node C
Node C May unlock the protection path
When the fault of the working LSP disappears:

## Slide 6: Resource Preemption
A failure occurs on W2 while W1 is still in failure state
  if P2’s priority is lower; the node C will not switch the traffic
  if P2’s priority is higher; the above figure indicates the signaling procedure

## Slide 7: Next Steps
Update RFC4872?
Comments/Feedback?
