## Slide 1: OSPF-TE Extensions for WSON-specific Network Element Constraints draft-peloso-ccamp-wson-ospf-oeo-04
Cyril Margaria, Giovanni Martinelli, Julien Meuric, Pierre Peloso

## Slide 2: 3 main changes proposed by current draft
<number> | OSPF-TE extensions for WSON | IETF 81st
  INTRODUCTION of RESOURCE POOL: atomic group of devices, for which properties share identical dynamicity.
    Rationale: a/ to formalize information aggregation, b/ to formalize flooding processes upon LSP updates.
  USE of node’s CONNECTIVITY MATRIX TLV: to describe OEO devices connectivity constraints.
    Rationale: a/ Gather more static information inside node LSA, b/ Limit number of new TLVs.
  Enhance the Resource Block Strength: took “NUMBER of DEVICES” off the Resource Block Information TLV.
    Rationale: a/ Use Resource Blocks compactness, while sharing
    resource descriptions for all identical devices, b/ Create independent flooding entity for all resource
    descriptions (static).

## Slide 3: Modification 1 – Introduction of Resource Pool High-Level view of change
  Makes the resource pool an independently floodable entity
  => needs dedicated local ID
Resource Block: a group of n OEOs introduced by draft-ietf-ccamp-rwa-info as a compacting entity
  same accessibility constraints
  same features
Resource Pool: a group of m Resource Blocks introduced by draft-peloso
  Same accessibility constraints
<number> | OSPF-TE extensions for WSON | IETF 81st
RB1: 5x10Gbit/s
RB2: 7x40Gbit/s
RB3: 3x43Gbit/s
RB4: 11x10Gbit/s
RB5: 5x40Gbit/s
RB6: 3x43Gbit/s
RB7: 9x10Gbit/s
RB8: 1x43Gbit/s
<ResourcePool> ::= <ResourcePoolID> <ResourceBlockState>... (SharedAccessWavelengths>...)
A
C
D
A
C
D

## Slide 4: Modification 1 – Introduction of Resource Pool Detailed view of change
<number> | OSPF-TE extensions for WSON | IETF 81st
RBPoolState
Current WG draft ----> draft-peloso
Res Pool ID
Shared Access Wavelengths
Resource
Pools
Resource
Description
Container
ResourceBlockInfo
ResourceBlockInfo
ResourceBlockInfo
ResourceBlockInfo
R_B_Accessibility
R_B_Accessibility
R_B_Accessibility
R_B_Accessibility
R_WaveConstrain
R_WaveConstrain
R_WaveConstrain
Shared Access Wavelengths
RBState
RBState
ResourceBlockInfo
ResourceBlockInfo
ResourceBlockInfo
ResourceDescription
Merged into already existing connectivity Matrix
Node Attribute
Modification 1
Modification 2
Modifications
1+3

## Slide 5: Modification 1 – Introduction of Resource Pool Example with current WG drafts
<number> | OSPF-TE extensions for WSON | IETF 81st
  Have LSAs for WDM links with availability of wavelength (dynamic)
  Have 1 LSA for switching constraints of nodes (static)
  Have 1 LSA for Resource Pools (dynamic & static), could be with multiple instances of TE-LSA:
    Shared Access Wavelengths
    Resource Pool State
    Resource Block Accessibility
    Resource Block Info
A
B
C
D
OEO pool
Shared Wvl
Pool State
Block Access
Block Info
OEO pool
LSP set-up

## Slide 6: Modification 1 – Introduction of Resource Pool Example with draft-peloso
<number> | OSPF-TE extensions for WSON | IETF 81st
A
B
C
D
Provide an OSPF-TE layout that intrinsically separates some static info from some dynamic ones, exploiting the concept of OEO pools
  Have LSAs for WDM links with availability of wavelength (dynamic)
  Have 1 LSA for switching constraints of nodes (static)
  Have LSAs for Resource Pools (dynamic: usage of wavelength & devices)
  Have 1 LSA for OEO features (static)
A
B
C
D
OEO pool
OEO pool
OEO pool
OEO features
OEO features
OEO pool
LSP set-up

## Slide 7: Modification 1 – Introduction of Resource Pool Pros and Cons
<number> | OSPF-TE extensions for WSON | IETF 81st
Pros:
  Formalized information structure
    more predictable information size
    insured coherence between wavelength usage and device usage
    Defined behavior insuring consistency during re-boots of CP
  Formalized updating process
  Finer updates granularity (single pool update)
Cons:
  Introduction of a new level of ID
  In some cases, the overall information size can be better with current WG draft tuning the appropriate information layout

## Slide 8: Modification 2 – USE of Node Connectivity Matrix TLV High-level view of change
<number> | OSPF-TE extensions for WSON | IETF 81st
A
C
D
A
C
D
OEO pool LSA
OEO pool LSA
B Node
Connectivity Matrix
WDM links LSAs
WDM links LSAs

## Slide 9: Modification 2 - USE of Node Connectivity Matrix TLV Details view of change
<number> | OSPF-TE extensions for WSON | IETF 81st
Use the connectivity matrix defined in current WG draft generic part:
  Needs IDs for Resource Pool ingress and Egress
  Need no change on the connectivity matrix
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Connectivity | MatrixID | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Link Set A #1 |
: : :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Link Set B #1 |
: : :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Additional Link set pairs as needed to specify connectivity :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Composed of
Link Local ID and
Resource Egress ID
Composed of
Link Local ID and
Resource Ingress ID
0 1 2 3 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| RESOURCE_INGRESS_ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| RESOURCE_EGRESS_ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sub-TLVs as needed (Opt) |
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 10: Modification 2 - USE of Node Connectivity Matrix TLV Example with draft-peloso
Node attribute TLV with connectivity matrix saying what can be connected:
  - (Entering interfaces A, C and outgoing RB1) to (outgoing interfaces X, Z and incoming RB1)
  - (Entering interfaces B,D and outgoing RB2) to (outgoing interfaces X,Y and incoming RB2)
<number> | OSPF-TE extensions for WSON | IETF 81st
RB1
OEO pool 3
OEO pool 2
A
B
C
D
X
Y
Z
Tun.
Drop
Tun.
Drop
RB 2

## Slide 11: Modification 2 - USE of Node Connectivity Matrix TLV Example with current WG draft
Node attribute TLV with connectivity matrix saying what can be connected:
- (Entering interfaces A and C) to (outgoing interfaces X and Z)
- (Entering interfaces B and D) to (outgoing interfaces X and Y)
Node property attribute TLV with connectivity matrix saying what can be connected:
- (Resource block 1) to (entering interfaces A and C)
- (Resource block 1) to (outgoing interfaces X and Z)
- (Resource block 2) to (entering interfaces B and D)
- (Resource block 2) to (outgoing interfaces X and Y)
draft-peloso needs the listing of 12 IDs.
current WG drafts needs the listing of 20 IDs.

## Slide 12: Modification 2 - USE of Node Connectivity Matrix TLV Pros and Cons
<number> | OSPF-TE extensions for WSON | IETF 81st
Pros:
  Gathering static information inside a same TLV, those sharing same nature (spatial connectivity constraints), inside a static dedicated entity.
  Avoiding creating 2 new sub-TLVs, each in different top-level TLV, while really similar – reuse of a generic object
  Gathering all connectivity info may compress information
Cons:
  Is sometimes interpreted as a mix of wson-specific and generic elements

## Slide 13: Modification 3 – Enhance Resource Block strength High-level view of change
Modification : Describe the resource properties instead of the resource block properties
Current WG draft describe the properties of Resource Blocks by associating RB IDs to Resource Block Information,
Resource Block information contains :
OEO Properties (Modulation, FEC, BitRate, ClientSignal, Regeneration, FaultMonitoring)
Resource Block specific property : NumResources
Proposal: associate the number of resource to the resource block state (hence advertised within Resource Pool TLVs).
<number> | OSPF-TE extensions for WSON | IETF 81st

## Slide 14: Modification 3 – Enhance Resource Block strength High-level view of change
<number> | OSPF-TE extensions for WSON | IETF 81st
Num Resources
Resource Description
Resource Block Information
Current draft describe the properties of Resource Blocks by associating RB IDs to Resource Block Information.
In Modulation
Out Modulation
In FEC
Out FEC

## Slide 15: Modification 3 – Enhance Resource Block strength Detailed view of change
<number> | OSPF-TE extensions for WSON | IETF 81st
  Current draft describe the composition of Resource Blocks by associating IDs to Resource Block Information.
  Having the number of device elsewhere allow better aggregation on that static part (The information is then describing the resources properties)
  In addition we propose one Sub-Sub-TLV modulation instead of one for Ingress modulation and one for egress modulation. This modulation Sub-Sub-TLV, contains a list of ingress or egress modulation, as the modulation already carry an Ingress flag.
  Same reasoning for FEC.
  Same reasoning for wavelength constraints in general

## Slide 16: Modification 3 – Enhance Resource Block strength Example
<number> | OSPF-TE extensions for WSON | IETF 81st
RB1
RB2
RB3
RB4
RB5
RB6
RB7
RB8
A
C
D
A
C
D
5x10Gbit/s
7x40Gbit/s
3x43Gbit/s
11x10Gbit/s
5x40Gbit/s
3x43Gbit/s
9x10Gbit/s
1x43Gbit/s
10Gbit/s
40Gbit/s
43Gbit/s
Current WG draft ----> draft-peloso

## Slide 17: Modification 3 – Enhance Resource Block strength Pro and cons
Pros:
  One resource description apply to more resource blocks : better aggregation, more compact encoding.
  Have less sub-sub-TLVs
  Number of resources is part of the Resource Block State?
Cons:
  Number of resources is part of the Resource Block State?
<number> | OSPF-TE extensions for WSON | IETF 81st

## Slide 18
<number> | OSPF-TE extensions for WSON | IETF 81st
<number> | OSPF-TE extensions for WSON | IETF 79th
Questions, discussions and adoptions of changes?
Notes: <number>

## Slide 19: Fully flexible Y-node with 1 pool of O-E-O
<number> | OSPF-TE extensions for WSON | IETF 81st
From node A
From node B
From node C
To node A
To node B
To node C
add
drop
…
…
Tun.
Drop
Tun.
Drop
OEO pool
With higher degree nodes (e.g. connectivity = 8):
Multiple pools are really likely to appear (depends on add-drop traffic)

## Slide 20: Fully flexible Y node with 4 pools of O-E-O fixed to links
<number> | OSPF-TE extensions for WSON | IETF 81st
From node A
From node B
From node C
To node A
To node B
To node C
Tun.
Drop
Tun.
Drop
Tun.
Drop
OEO pool 1
OEO pool 3
OEO pool 2
OEO pool 4

## Slide 21: Documents context
<number> | OSPF-TE extensions for WSON | IETF 81st
Scope: OEO equipments and their usage in RWA
Scope: Connectivity constraints in nodes and labels usage in links
draft-ietf-ccamp-rwa-wson-framework-07 (gone through last-call)
draft-ietf-ccamp-rwa-info-11
draft-ietf-ccamp-rwa-wson-encode-11
draft-ietf-ccamp-general-constraint-encode-04
draft-ietf-ccamp-wson-signal- compatibility-ospf-04
draft-ietf-ccamp-gmpls-general-constraints-ospf-te-00
draft-peloso-ccamp-wson-ospf-oeo-02
Back in Beijing - Alternative solutions

## Slide 22: Modification 3 – Enhance Resource Block strength
<number> | OSPF-TE extensions for WSON | IETF 81st
Currently RWA model defines “Resource Block Description” (OEO properties)
  same OEO features
  same number of device (ref to draft-ietf-ccamp-rwa-info)