## Slide 1: WSON Routing WG Drafts
Routing and Wavelength Assignment Information Model for WSON
General Network Element Constraint Encoding for GMPLS Controlled
Routing and Wavelength Assignment Information Encoding for WSON
OSPF Enhancement for Signal and Network Element Compatibility for WSON

## Slide 2: Authors/Contributors
Greg Bernstein (Grotto Networking)
Diego Caviglia (Ericsson)
Ander Gavler (Acreo AB)
Young Lee (Huawei)
Dan Li (Huawei)
Wataru Imajuku (NTT)
Jonas Martensson (Acreo AB)
Itaru Nishioka (NEC Corp.)
Jianrui (Rebecca) Han (Huawei)
Plus a whole lot of folks on the CCAMP list and at the last four years of meetings.

## Slide 3: WSON Draft Development Process (I)
First CCAMP presentation July 2007 (Chicago)
Status and copies of all supporting materials were made easily available from web site
Vendors, Carriers, Researchers, experienced GMPLS developers all contributed to drafts
Evaluated models against many test cases
Complied with CCAMP WG direction concerning structuring of drafts

## Slide 4: WSON Draft Development Process (II)
Many supplemental tutorials and presentations at IETF meetings, Optical Fiber Conference, IPoP, and OSA/IEEE Journal articles, e.g.,
  WSON Editing & Discussion meeting, 73rd IETF, MN, Nov., 2008 (models with resources introduced and inputs solicited).
  G. Bernstein and Young Lee, “Extending GMPLS/PCE for use in Wavelength Switched Optical Networks,” in Conference on OFC/NFOEC, 2008.
  G. Bernstein and Young Lee, “Overview of the Path Computation Element (PCE) and its application to Wavelength Routing,” presentation at Optical Routing Workshop OFC, 2008.
  G. M. Bernstein, Y. Lee, A. Gavler, and J. Martensson, “Modeling WDM Wavelength Switching Systems for Use in GMPLS and Automated Path Computation,” IEEE/OSA Journal of Optical Communications and Networking, vol. 1, no. 1, pp. 187-195, Jun. 2009.

## Slide 5: WSON Draft Development Process (III)
Many Test Cases (w/o resources) e.g.:
Etc…

## Slide 6: WSON Draft Development Process (IV)
Many Test Cases (with resources) e.g.:
Etc…

## Slide 7: WSON Draft Development Summary
Many person years of development
Open process with wide review of approach, beyond CCAMP and IETF
Call for inputs and evaluation of models with resources went out in November 2008
Any changes to documents at this point should be based on a well demonstrated problem, with clearly furnished minimalistic example
Proposed changes should be minimalistic to avoid breaking existing mechanisms.

## Slide 8: Changes Requested on List
“Introduction of the Resource Pool entity inside the model, which allows the definition of several resource entites per node independantly floodable.”
  Current encoding has this capability.
“Use of the connectivity matrix defined inside the node entity in order to describe connectivity constraints between node-external links and the resource pools.”
  No size or stability benefit from change, This was split out at 74th IETF meeting March 2009.
“Reduction of the scope of Resource Block Information, to keep only resource/device description (moved the number of devices away).”
  This is an optional static sub-sub-TLV, hence you don’t need to use it. Dynamic information is in the resource pool state sub-TLV

## Slide 9: Resources, Blocks, Sets and Pools
Simple hierarchy:
  The resource pool is partitioned into resource blocks containing individual resources.
Efficient and general encoding:
  Resources blocks are combined into sets for encoding of common properties.
R = resource
RB = resource block
Resource sets:
(RB1, RB2),
(RB2, RB3, RB4),
Etc…
RBp
R
R
RB1
R
R
R
…
RB2
R
R
R
R
Resource Pool

## Slide 10: Change Request 3 (I)
“Reduction of the scope of Resource Block Information, to keep only resource/device description (moved the number of devices away).”
“MOTIVATION:
  a/ to share resource description for all the (same devices) blocks (of a node), then decreasing the total size of information.
  b/ to create an independent flooding entity holding all the resource descriptions (which are static), the decreasing the size of updated information.”

## Slide 11: Change Request 3 (II)
What is this item?
  Section 4 of WSON encoding is concerned with properties of resources; Section 4.1 introduces the Resource Block Information sub-TLV
  Section 4.6 introduces the Processing Capabilities List sub-sub-TLV which includes the option of specifying the Number of Resources within the block
What is it for?
  In many cases multiple resources come bundled together, e.g., on a line card. This tells us the number of resources in this “block”.

## Slide 12: Change Request 3 (III)
Is it a dynamic or static quantity?
  This is a static quantity.
How does this differ from the Resource Pool State sub-TLV?
  This is a dynamic quantity that tells you the number of resources available in a particular RB pool set. It does not tell you the number in use/out of service.
Do I have to use it?
  No, it is an optional field
Can we remove it from the draft?
  No. A number of optimization algorithms want to know the total number of resources available at each node.

## Slide 13: Change Request 2 (I)
“Use of the connectivity matrix defined inside the node entity in order to describe connectivity constraints between node-external links and the resource pools.”
“MOTIVATION:
  a/ to gather static information inside node entity (for OSPF-TE inside a LSA never flooded upon LSP updates).
  b/ to limit the number of connectivity representations introduced by current extensions (draft-ietf-rwa-info proposes similar TLVs in different LSAs)”

## Slide 14: Change Request 2 (II)
What is this about?
  The WSON info model draft discusses connectivity between externally visible ingress and egress ports (the connectivity matrix) and connectivity between externally visible ingress and egress ports and internal resources (resource accessibility). These use similar mechanisms.
If these use similar mechanisms why aren’t they combined?
  We initially had these combined but were asked to separate out concepts and mechanisms with general applicability from those specific to WSON. This decision was discussed at a number of IETF meetings and finalized at the 74th IETF meeting in San Francisco, March 2009. This is why there are two encoding drafts (general constraints and WSON specific).

## Slide 15: Change Request 2 (III)
Does this result in any significant space savings or expansion?
  No. The same basic information needs to be conveyed whether it is split into two different top level TLVs or in just one.
What is the implications for static versus dynamic information?
  This is an orthogonal issue from this particular encoding choice. We recommend that static and dynamic information should be flooded separately. OSPF-TE provides a good mechanism for this. See the following slides for a review of the basic mechanisms.

## Slide 16: Updating WSON info with OSPF-TE (I)
OPSF Opaque LSA and Optical Node TLV
  All of GMPLS uses the OSPF-TE (RFC3630) Traffic Engineering LSA.
  “The LSA ID of an Opaque LSA is defined as having eight bits of type data and 24 bits of type-specific data. The Traffic Engineering LSA uses type 1. The remaining 24 bits are the Instance field, as follows:”
  “The Instance field is an arbitrary value used to maintain multiple Traffic Engineering LSAs. A maximum of 16,777,216 Traffic Engineering LSAs may be sourced by a single system.
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 1 | Instance |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 17: OSPF-TE LSA (RFC3630)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| LS age | Options | 10 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 1 | Instance |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Advertising Router |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| LS sequence number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| LS checksum | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
“The LSA payload consists of one or more nested Type/Length/Value (TLV) triplets for extensibility.”
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Value... |
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 18: Updating WSON info with OSPF-TE (II)
LSAs are the smallest flooding/update unit
  You pick what you want to put within a particular LSA instance within the constraints of the TLV hierarchy and rules, e.g., one top level TLV per LSA (RFC3630)
Currently Defined and Proposed Top Level TLVs
  RFC3630: Router Address, Link
  RFC5329: Router IPv6 Address, RFC4203: Link Local
  RFC5786: Node Attribute
  WSON OSPF extensions: Optical Node Property TLV

## Slide 19: Updating WSON info with OSPF-TE (III)
All of the WSON specific info goes into an Optical Node TLV?
  Yes.
How do I keep this TLV from getting too large? How do I separate dynamic and static information?
  Use multiple TE-LSA instances each with a Optical Node TLV containing one or more sub-TLVs.
  This is why we never mix static and dynamic information in the same sub-TLV
  This is also why we break information up into sub-TLVs

## Slide 20: Change Request 1 (I)
“Introduction of the Resource Pool entity inside the model, which allows the definition of several resource entites per node independantly floodable.”
“MOTIVATION: to decrease the size of flooding upon LSP changes (setup or tear down). (Resource Pool = group of resource blocks with same connectivity constraints).”

## Slide 21: Change Request 1 (II)
Current model has the containment hierarchy of:
  Resource, Resource Block, Resource Block Set, and Resource pool.
The Resource Block Set concept serves this function.
  A general group of resource blocks with similar properties of any kind
  No need for new terminology.

## Slide 22: Resource Block Set Usage
Resource pool accessibility sub-TLV
Resource block wavelength constraints sub-TLV
Resource block information sub-TLV
  Fixed this in March 2011 to use resource set
Block shared access wavelength availability sub-TLV
Resource pool state sub-TLV
These sub-TLVs can be placed in one or more Optical node property TLVs (in one or more Opaque LSAs), all independently floodable.
Static
Dynamic

## Slide 23: Example: Many types of regens (I)
Numbers: 4 ports, 200 wavelength converters, 10 types of converters, random assignment of converters to groups.
+-----------+ +------+
| |--------------------->| |
| |--------------------->| C |
/| | |--------------------->| o |
/D+--->| |--------------------->| m |
+ e+--->| | | b |========>
========>| M| | Optical | +-----+ | i | Port E1
Port I1 + u+--->| Switch | | WC | | n |
\x+--->| | |Group| | e |
\| | +------>| A |------->| r |
| | +-----+ +------+
| | +------+
/| | | +-----+ | |
/D+--->| +------>| WC |------->| C |
+ e+--->| | |Group| | o |
========>| M| | | | B | | m |========>
Port I2 + u+--->| | +-----+ | b | Port E2
\x+--->| |--------------------->| i |
\| | |--------------------->| n |
| |--------------------->| e |
+ | |--------------------->| r |
========>| ... | | +------+
Port I3 + | |
| | Similar structure ========>
| | with WC groups C and Port E3
+ | | D and combiners for
========>| ... | | ports E3 and E4
Port I4 + | | ========>
+-----------+ Port E4
Shared per fiber architecture

## Slide 24: Example: Many types of regens (II)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Connectivity=1| Reserved |
Note: I1-I4 can connect to any Wavelength converter
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Action=2 |0 1|0 0 0 0 0 0| Length = 12 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Link Local Identifier = #1 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Link Local Identifier = #4 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Action=2 |1| Reserved | Length = 8 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| RB ID = #1 | RB ID = #Total blocks |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Note: WC Group A can only connect to E1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Action=0 |1 0|0 0 0 0 0 0| Length = 8 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Link Local Identifier = #1 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Action=2 |0| Reserved | Length = 8 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| RB ID = #1 | RB ID = 50 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Note: WC Group B can only connect to E2
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Action=0 |1 0|0 0 0 0 0 0| Length = 8 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Link Local Identifier = #2 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Action=2 |0| | Length = 8 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| RB ID = 51 | RB ID = #100 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Accessibility sub-TLV:
Linear numbering
50 converters per group
Use ranges to describe group
Total words: 6+4x4 = 22  88 bytes
All information is static
Not shown WC Groups C and D

## Slide 25: Example: Many types of regens (III)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| RB Set Field |
: List of resource WC IDs that are of this type |
| Length in words = 1 + ceil{(Num WC total)/(2*NT)} = 11 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|0|0| Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Input Modulation Type List Sub-Sub-TLV |
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Input FEC Type List Sub-Sub-TLV |
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Input Client Signal Type Sub-TLV |
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Input Bit Rate Range List Sub-Sub-TLV |
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Processing Capabilities List Sub-Sub-TLV |
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Output Modulation Type List Sub-Sub-TLV |
:
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Output FEC Type List Sub-Sub-TLV |
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Resource Info sub-TLV:
Random numbering
20 converters per type
Use list to describe groups
Assume 32 words for info fields + 11 words for list = 43 words per type = 172 bytes per sub-TLV
Need 10 of these sub-TLVs
Sub-TLVs can be sent separately
All information is static

## Slide 26: Example: Many types of regens (IV)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Action = 1 | Reserved |
(bit map) Pool State sub-TLV followed by RB Set field
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Action=2 |0| Reserved | Length = 8 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| RB ID = #1 | RB ID = 50 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| RB Usage state bitmap (total 50 bits) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| (final 18 bits) | Padding bits |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Resource Status sub-TLV:
Four distinct groups, i.e., one per port with 50 resources, (but could grouped all together)
Linear numbering already used
Bit map representation for resource status
Total of 5 words (20 bytes) for each sub-TLV
Similarly for resources 51-100, 101-150, 151-200

## Slide 27: Example: Many types of regens (V)
All information in separate sub-TLVs can be sent in separate Traffic Engineering LSAs with different instance numbers
  Accessibility sub-TLV (88 bytes) –static--
  Resource Info sub-TLVs (10 @ 172 bytes each) –static --
  Resource Pool state sub-TLVs (4 @ 20 bytes each) – dynamic –
LSA, TLV, and sub-TLV overhead not included in estimates.

## Slide 28: Concern expressed on list: numbering of resource blocks
Potential Issue:
  I’ve got very complicated optical nodes and I can’t guarantee the linear assignment of RB identifiers, so can’t always use ranges for dynamic updates…
Potential Solution
  Add resource group definition sub-TLV
  Add predefined group identifier option to RB Set field.

## Slide 29: Numbering of resource blocks (II)
  Potential new Resource Group Definition Sub-TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Reserved | Group ID #1 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| RB Set Field for Group #1 |
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Reserved | Group ID #2 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| RB Set Field for Group #2 |
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
...
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Reserved | Group ID #N |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| RB Set Field for Group #N |
: :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 30: Numbering of resource blocks (III)
  Potential new RB Set Field Action
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Action =3 |E|C| Reserved | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| RB Group Identifier 1 | RB Group Identifier 2 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
: : :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| RB Group Identifier n-1 | RB Identifier n |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Action = 3 – Predefined Group Identifier
Indicates that the field contains one or more resource block group identifiers. This is potentially useful in cases where a very long resource block sets may be reused, such as in resource state update messages.
But is this really needed?
This is an extra complication and no realistic example has been given that justifies this addition.

## Slide 31: Other Concerns Expressed On List
Stability of resource block identifiers across life time of box.
  Three aspects here:
  your systems HA architecture (not standard),
  routing information and its configuration, (not standard)
  signaling state recovery (standardized)