## Slide 1: WSON Optical Interface Class
draft-martinelli-wson-interface-class-00
Giovanni Martinelli Cisco
Gabriele Galimberti Cisco
July 2011
IETF81 Quebec
<number>

## Slide 2: Overview
What: Propose a different way to solve the WSON signal compatibility.
Why: (to some extent) keep protocol extensions independent from ITU standard evolution.
Draft Status: a rough cut proposed here to start discussion.
July 2011
IETF81 Quebec
<number>

## Slide 3: Current WSON status
Signal compatibility parameters (RFC6163):
  FEC (forward error correction)
  Modulation Format
  Bit Rate
Definitions/Encodings:
  draft-ietf-ccamp-rwa-info-11, draft-ietf-ccamp-rwa-wson-encode-11
Protocol Extensions
  OSPF: draft-ietf-ccamp-wson-signal-compatibility-ospf-04
  RSVP: draft-ietf-ccamp-wson-signaling-01
  PCEP: draft-lee-pce-wson-rwa-ext-02
July 2011
IETF81 Quebec
<number>

## Slide 4: Example: Mod Format & FEC
July 2011
IETF81 Quebec
<number>
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|1|1| Modulation ID | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Possible additional modulation parameters depending upon |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
: the modulation ID :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|1|1| FEC ID | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Possible additional FEC parameters depending upon |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
: the FEC ID :
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Standard/
Proprietary
Length: depending also
on proprietary info.
Possible?
ID according to G.959.1 (only NRZ)
ID according to G.709 and G.975.1

## Slide 5: Problem
There are already new modulation formats available for 40/100G (e.g. DPSK/QPSK):
  standard will evolve soon (but we don’t know how).
What if we need some more parameters?
  E.g. The Optical Impairment awareness case.
July 2011
IETF81 Quebec
<number>

## Slide 6: The Optical Interface Class
It is a number
Protocol operations become trivial: if two interfaces have the same number, they are compatible.
The optical parameters values associated to this numbers are defined elsewhere.
  So when optical std evolve no changes are required.
July 2011
IETF81 Quebec
<number>

## Slide 7: Optical Interface Class: encoding
July 2011
IETF81 Quebec
<number>
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Optical Interface Class |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Class value = 1
{
FEC = …
Mod Format = …
Bit Rate = …
…
}
Class value = 2
{
FEC = …
Mod Format = …
Bit Rate = …
…
}
Reference to:
Class Values / Content
shall be defined
elsewhere.

## Slide 8: Conclusions
Comments?
From 00 to 01:
  Details encoding
  Refine how to associate Optical Interface Class with the set of optical parameters.
July 2011
IETF81 Quebec
<number>