## Slide 1: Flexible Grid Label Format in Wavelength Switched Optical Network
draft-li-ccamp-flexible-grid-label-00
Yao Li (li.yao3@zte.com.cn)
Fei Zhang (zhang.fei3@zte.com.cn)
Ramon Casellas (ramon.casellas@cttc.es )
Notes: <number>

## Slide 2: Motivation
Limitations
In fixed grid (channel spacing) network, constant spectral resource is allocated to every channel with different bitrates, resulting relatively low resource unitization efficiency.
High Speed Signals beyond 100 Gb/s are not expected to adapt such narrow channel spacing like 50 GHz.
Solutions
High capacity and high efficiency utilization of optical network resource is required. Flexible grid technique is a candidate to accomplish this requirement.
High resource utilization efficiency for mixed bitrates systems.
Adaptive to transmission distance and optical impairments.
Support ultra-high speed modulation format like OFDM.
Notes: Arbitrary spectral resource can be allocated to a channel acceding to the signal bitrate leading to
<number>

## Slide 3: Flexible grid Vs fixed grid
193.1 THz
193.05
193
193.15
193.2
10 Gb/s
40 Gb/s
100 Gb/s
10 Gb/s
10 Gb/s
Fixed grid
DWDM
50 GHz
193.1 THz
193.05
193
193.15
193.2
40 Gb/s
40 Gb/s
100 Gb/s
100 Gb/s
400 Gb/s
Flexible grid
DWDM
50 GHz
Signal spectrum
Frequency slot

## Slide 4: G.694.1 flexible grid definition
For the flexible DWDM grid, the allowed “ frequency slots” have
a nominal central frequency (in THz) defined by:
193.1 + n × 0.00625 where n is a positive or negative integer including 0.
and a slot width (GHz) defined by:
12.5 GHz × m where m is a positive integer.
Note: the values of 6.25 GHz is called “central frequency granularity” and 12.5 GHz “slot width granularity”
-2
-3
-5
-7
-9
-1
-11
-13
-15
-16
17
15
13
10
7
5
4
3
2
1
0
22
19
central frequency granularity 6.25GHz
Slot width
1×12.5GHz
Slot width
3×12.5GHz
Slot width
3×12.5GHz
Slot width
6×12.5GHz
n=
Slot width
4×12.5GHz
Slot with granularity 12.5 GHz
Notes: The slot width granularity is twice the channel spacing granularity, so that by carefully choosing n and m, the spectral resources can be allocated without leaving any gaps between slots.
<number>

## Slide 5: Flexible label format
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Grid | C.S. | Identifier | n |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Additional slot width parameters |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Additional slot width parameters:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| m | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
In WSON, the control plane allocates the wavelength label(RFC 6205) represented by center frequency for the LSP. While in flexible grid network, wavelength label represented by spectral resource or “frequency slot” should be assigned.
Grid | Value
DWDM | 1
CWDM | 2
Flexible DWDM | 3
C.S. (GHz) | Value
100 | 1
50 | 2
… | …
6.25 | 5
“m” represents how many slot width granularities the label has occupied
Notes: <number>

## Slide 6: Backward compatibility
Routing
Spectral range (frequency slots) constraints and available Spectral resources, etc. by label set: Inclusive list; excusive list; inclusive range; exclusive range; bitmap set (two bit for a flexible label).
New switching capability (ISCD), spectrum bandwidth limits.etc? , out of scope.
Signaling
Assigning available spectral resource by flexible label. However, wavelength/spectrum continuity still need to be satisfied.
PCE
PCEP message indicating the spectral constraints and available resources by label set .
Other constraints (new swcap, modulation formats, etc?), out of scope.
Notes: Spectrum Selective Switching
<number>

## Slide 7
Comments
Thanks!