## Slide 1: Requirement and protocol for WSON and non-WSON interoperability CCAMP WG, IETF 81th, Quebec City, Canada draft-shimazaki-ccamp-wson-interoperability-00
Daisaku Shimazaki shimazaki.daisaku@lab.ntt.co.jp
Rie Hayashi hayashi.rie@lab.ntt.co.jp
Kohei Shiomoto shiomoto.kohei@lab.ntt.co.jp
Notes: <number>

## Slide 2: outline
Interoperability problem
Requirements
Protocol
Operation example
Notes: <number>

## Slide 3: Interoperability problem –GMPLS case -
Control plane has been extended for various kinds of techniques.
New objects/TLVs are continuously defined.
 Interoperability among nodes becomes difficult.
D-plane
C-plane
GMPLS Path
Signaling (RSVP-TE)
Routing (OSPF-TE)
Notes: <number>

## Slide 4: WSON
One of GMPLS extensions is WSON.
   information (bit map, lambda label)
  PCE function (RWA…)
WSON nodes
   Advertise, relay, and compute with  information.
Non WSON nodes
   Need not understand  information.
How to interoperate these nodes automatically?
WSON node
Non WSON node
WSON
RSVP PATH
RSVP PATH
SRC
DST
 ???
 = 1550 nm !
Notes: <number>

## Slide 5: Requirements(1/2) non-WSON nodes
Having no impact on interoperating WSON nodes.
  Need to understand a network topology including WSON domain
  Need to calculate a route considering WSON topology
  Need to establish LSP between non-WSON nodes via WSON domain
WSON
RSVP PATH
RSVP PATH
SRC
O1
R1
O2
O3
O4
R2
DST
R1  O1  ….  R2
WSON node
Non WSON node
Notes: <number>

## Slide 6: Requirements(2/2) WSON nodes
Handling WSON-extended information.
  Need to understand a network topology including non-WSON
  Need to calculate RWA when it is needed
    Assign available 
    Assign a route and available 
  Need to establish LSPs
WSON
RSVP PATH
RSVP PATH
SRC
O1
R1
O2
O3
O4
R2
DST
RSVP PATH (=1550)
R1  O1  O2  R2
 = 1550 nm
R1  O1  ….  R2
WSON node
Non WSON node
Notes: <number>

## Slide 7: Protocol(1/2)- OSPF-TE
Non-WSON node
  Advertise TE-link information without 
  Ignore information in sub-TLV of link information
WSON node
  Advertise and share available information
  Understand TE-link in non-WSON topology without 
WSON
OSPF-TE
SRC
O1
R1
O2
O3
O4
R2
DST
1, 2
1, 2
1, 2
1, 2
WSON node
Non WSON node
Notes: <number>

## Slide 8: Protocol(2/2)- RSVP-TE
Non-WSON nodes send RSVP-TE PATH message including just a route information.
WSON nodes
  add  information to be used in WSON to RSVP-TE PATH message at the ingress of WSON domain
  Delete information from RSVP PATH message at the egress of WSON domain.
WSON
RSVP PATH
RSVP PATH
SRC
O1
R1
O2
O3
O4
R2
DST
RSVP PATH (=1550)
WSON node
Non WSON node
Notes: <number>

## Slide 9: Operation example(1/4)
Step 1:
  A source router R1 sends RSVP-TE signaling by assigning a path route and switching type as Label Switching Capable (LSC).
    R1 is assumed to understand a topology in LSC region including all of the routers and ROADMs with OSPF-TE.
ROADM
Router
WSON
RSVP PATH
SRC
***
ERO= O1,O2,R2 (or loosely assigning only R2)
Label Request
LSP Encoding Type=Ethernet
Switching Type = LSC
***
O1
R1
O2
O3
O4
R2
DST
CSPF computes a route
Notes: <number>

## Slide 10: Operation example(2/4)
Step 2:
  When a ROADM O1 receives the signaling message from R1, its RWA computes a route and one of available s.
  O1 then sends the signaling messages which assigns explicit route object (ERO) and  label to the next node.
ROADM
Router
WSON
RSVP PATH
RSVP PATH (1550)
SRC
***
ERO= O1,O2,R2 (or loosely assigning only R2)
Label Request
LSP Encoding Type=Ethernet
Switching Type = LSC
***
***
ERO=O2,R2
Label Request
LSP Encoding Type=Ethernet
Switching Type = LSC
λ= 1550.0nm
***
O1
R1
O2
O3
O4
R2
DST
RWA algorithm computes both  and route
Notes: <number>

## Slide 11: Operation example(3/4)
Step 3:
  When a ROADM O2 receives the signaling message from O2, it takes its ERO from the signaling messages and sends it to a router R2. (= normal signaling process)
ROADM
Router
WSON
RSVP PATH
RSVP PATH (1550)
RSVP PATH
SRC
O1
R1
O2
O3
O4
R2
DST
***
ERO= O1,O2,R2 (or loosely assigning only R2)
Label Request
LSP Encoding Type=Ethernet
Switching Type = LSC
***
***
ERO=O2,R2
Label Request
LSP Encoding Type=Ethernet
Switching Type = LSC
λ= 1550.0nm
***
Notes: <number>

## Slide 12: Operation example(4/4)
Step 4:
  When R2 receives the signaling messages, it relays replied signaling messages and finally a path is set up along the route.
ROADM
Router
WSON
RSVP PATH
RSVP PATH (1550)
RSVP PATH
SRC
***
ERO= O1,O2,R2 (or loosely assigning only R2)
Label Request
LSP Encoding Type=Ethernet
Switching Type = LSC
***
***
ERO=O2,R2
Label Request
LSP Encoding Type=Ethernet
Switching Type = LSC
λ= 1550.0nm
***
O1
R1
O2
O3
O4
R2
DST
CSPF computes a route
CSPF computes both  and route
Notes: <number>

## Slide 13: Next Steps
Refine the document according to the feedback of meeting and mailing list.
Notes: <number>