## Slide 1: Framework and Information model for G.709 Optical Transport Network (OTN)
draft-ietf-ccamp-g709-framework-04
draft-ietf-ccamp-otn-g709-info-model-00
CCAMP WG, IETF 81th Quebec City

## Slide 2: Status of the drafts
Framework draft – Version 04 of the WG document stable
Info model draft - Version 04 of draft-bccg-ccamp-otn-g709-info-model has become a WG from Prague meeting. Version 00 of the WG document
Both document MIGHT need to be updated since some open points are still pending and need clarification from CCAMP :
  TS granularity/Payload type auto-negotiation.
  Mapping of “non OTN client” over ODU server trails.
    Check needed on IACD format for OTN in MLN/MRN.
  Editorial notes already present in encoding notes need to be addressed into the Framework and Info documents.
  Ongoing discussion on open requirements (dedicated presentation following).

## Slide 3: Trib Slot granularity/Payload type
At interface commissioning time there is no default payload type value. The type of payload is related to TS granularity and is provided as soon as a client request is received on the server trail.
    If both interface support at least 1,25 TS, the link will work @1,25 TS
    If at least on of the interfaces supports only 2,5 TS, the link will work @2,5 TS
Impacts:
  If no auto-negotiation is active, no LMP present, Payload type is manually configured (no check available)
  Link end nodes must be aware of the TS for correctly extracting the payload from the frame
A
B
1,25Gbps
ODU3
2,5Gbps
1,25Gbps
A
B
1,25Gbps
ODU3
2,5Gbps
2,5Gbps

## Slide 4: Trib Slot granularity/Payload type
At interface commissioning time there is no default payload type value. The type of payload is related to TS granularity and is provided as soon as a client request is received on the server trail.
Switching
    In those cases where a 2,5 TS is used and a service requiring 1,25 TS is transparently switched, it is possible to set up an LSP at 1,25 TS (e.g. ODU0) over an higher order ODU (e.g. ODU3) using the 2.5 TS.
A
B
C
D
1,25Gbps
2,5Gbps
1,25Gbps
ODU0
ODU3
ODU3
ODU3

## Slide 5: Trib Slot granularity/Payload type
At interface commissioning time there is no default payload type value. The type of payload is related to TS granularity and is provided as soon as a client request is received on the server trail.
Termination
    In those case where the termination of a 1,25 TS service (e.g. ODU0) is required, an interface with auto-negotiation result equal to 1,25 TS must be preset. In figure below there are 2 interfaces between C and D. An ODU0 can be terminated on D only if the upper interface is chosen
A
B
C
D
1,25Gbps
2,5Gbps
1,25Gbps
ODU0
ODU3
ODU3
1,25Gbps
ODU3