## Slide 1: A Framework for Management and Control of Optical Interfaces supporting G.698.2
draft-kunze-g-698-2-management-control-framework-00
Ruediger Kunze
Manuel Paul Deutsche Telekom
July 2011
81st IETF Quebec
<number>

## Slide 2: Motivation
Define a Framework for the Control and Management of Optical Interfaces according to the Black Link approach
  Develop Enhancements for Control & Management to leverage the Black Link approach in carrier networks in large-scale
  Use Case: Improved Interworking between third party systems e.g. Router <-> DWDM <-> Router
  Support Status-Quo as well as future network management and control concepts
Black Link according to ITU-T G.698.2 provides options to deploy Optical Interfaces in a WDM network
  currently defined up to 10G
  being extended by ITU-T for 40G, 100G and beyond
  primarily intended for metro applications (i.e. up to 600km reach)

## Slide 3: Recap: G.698.2 in a colored Nutshell
Black Link: The Black Link approach [ITU-T G.698.2] allows supporting an optical transmitter/receiver pair of one or different vendors to inject an Optical Channel (OCh) and transfer it over a DWDM network composed of amplifiers and add-drop multiplexers from a different vendor. Therefore the standard defines the ingress and egress parameters at the reference points Ss and Rs.
G.698.2 provides an optical interface specifications towards the realization of transversely compatible dense wavelength division multiplexing (DWDM) systems primarily intended for metro applications which include optical amplifiers."
=> towards "multivendor DWDM optical transmission networks"

## Slide 4: Document Scope and Perspective
Solutions for Control and Management of Optical Interfaces
  Operational Scenarios and Uses Cases
  Requirements for Black Link deployments
Interoperable Control and Management Solutions required
  Supporting multivendor transverse interoperability DWDM networking
  Considering just one optical network operator (i.e. one administrative domain)
  Data Plane under consideration is well-defined and standardized (ITU-T G.698.2)
  IETF work focuses on the control and management aspects for the optical interface / optical system (excluding active optical components)
WSON work is complementary
Alignment with work going forward in ITU-T
Notes: Key Requirements
Interoperable BL solutions
Specification of solutions ensuring an interoperable management of BL deployments for 10G, 40G and beyond.
Must work with legacy equipment and management components.
WSON is complementary
  Focusing on the management and control of the optical interface.
  Dynamic Wavelength switching and assignment is out of scope

## Slide 5: Solution initially in Focus
Tp – Transponder (eliminated)
EMS – Element Management System
NMS – Network Management System
Optimized interconnection of client nodes to the optical transport network, being all in the same administrative domain (intra-domain)

## Slide 6: Current Status & Modifications
Presented first time at the last meeting in Prague
Feedback from the WG chairs
  Renaming the document
  Base management and control extensions on existing ITU-T standards
Work introduced to and discussed with ITU-T
Addressed the feedback from the working group and from ITU-T

## Slide 7: ITU-T Discussion Results
Black Link contributions for the recent ITU-T Chicago interim
  General proposal to progress BL work in ITU-T Q9, Q12, Q14 of SG15; beyond optical specifications being in the works by Q6
  Equipment Functions, Architecture & Features of Black Links (Q9, Q12)
  Protocol neutral Black Link Management models (Q14)
  Black Link will be subject of next SG15 Plenary Coordination Meeting
Clarifications from ITU-T discussions for the IETF activities
  Documents at IETF will focus on the management and control of optical interfaces based on existing ITU-T standards (ITU-T G.698.2)
  Management of the WDM network part of Black Links is out of scope

## Slide 8: Next Steps
Proposal to home/base this work in CCAMP, along with related Black Link work at ITU-T
Feedback from Operators and Vendors invited
  Requirements
  Use cases and deployment scenarios
Progress work on Use Cases and Requirements
Corresponding MIB document in progress