## Slide 1: RSVP-TE Extensions for SRLG Configuration of FA
CCAMP WG, IETF 81th, Quebec City, Canada
draft-zhang-ccamp-srlg-fa-configuration-03.txt
O. Gonzalez de Dios (ogondio@tid.es)
Fatai Zhang (zhangfatai@huawei.com)
Dan Li (danli@huawei.com)
C. Margaria. C (cyril.margaria@nsn.com)

## Slide 2: Changes from 02.txt
Added a section to describe the SRLG update procedure
  To address the comments from the last meeting
Added the content for Manageability Considerations

## Slide 3: SRLG Update
A
B
C
E
Client network/domain
Server network/domain
SRLG: 2
SRLG: 1
SRLG: 4
SRLG of the Link between D and E is changed.
D
SRLG: 3
LSP head node
LSP tail node
D detects the change of SRLG (from 3 to 5).
D finds out the LSP that traverses the link between D and E, then sends a Notify message to the head node of the LSP to re-collect the SRLG.
A receives the Notify message, then sends the Path message as a trigger message (RFC2961) to C to re-collect the SRLG.
The nodes collect the SRLG information hop by hop by the trigger Path/Resv messages, then A/B get the updated SRLG information.
SRLG: 3-->5

## Slide 4: Manageability Considerations
Policy Configuration
  Policy could be configured to disable/enable SRLG collection outside of the domain (either inter-domain or inter-layer scenarios).
Coherent SRLG IDs
  SRLG IDs must be unique and allocated based on a coherent rule.
  Further scenarios, where coherence in the SRLG IDs cannot be guaranteed are out of the scope of the present document and are left for further study.

## Slide 5: Next Steps
Adopt it as a WG document
Refine it according to the feedback from the meeting or mailing list