## Slide 1: OSPF-TE extensions for GMPLS Control of Evolving G.709 OTN
draft-ceccarelli-ccamp-gmpls-ospf-g709-06
CCAMP WG, IETF 81th Quebec City

## Slide 2: Authors/Contributors
Steve Balls (Steve.Balls@metaswitch.com )
Sergio Belotti (sergio.belotti@alcatel-lucent.com)
Diego Caviglia (diego.caviglia@ericsson.com)
Daniele Ceccarelli (daniele.ceccarelli@ericsson.com)
John Drake (jdrake@juniper.net )
Xihua Fu (fu.xihua@zte.com.cn )
Pietro Grandi (pietro_vittorio.grandi@alcatel-lucent.com)
Dan Li (danli@huawei.com)
Cyril Margaria (cyril.margaria@nsn.com )
Lyndon Ong (Lyong@Ciena.com)
Khuzema Pithewan (kpithewan@infinera.com)
Rajan Rao (rrao@infinera.com )
Jonathan Sadler (Jonathan.Sadler@tellabs.com)
Yunbin Xu (xuyunbin@mail.ritt.com.cn)
Fatai Zhang (zhangfatai@huawei.com)
Xiaobing Zi (zixiaobing@huawei.com)

## Slide 3: Agenda
Changes in version -06
  Merge of
    Draft-ceccarelli-ccamp-gmpls-ospf-g709-05
    Draft-ashok-ccamp-gmpls-ospf-g709-03
  New OTN ISCD,
  New SCSI sub-TLV
  New Bandwidth sub-sub-TLV
    1 – Fixed container
    2 – Flexible container
  Procedures
Next steps

## Slide 4: New OTN ISCD and SCSI TLV

## Slide 5: New Bandwidth sub-sub-TLV (1-BW-fix)
Num of stages: Number of muxing stages
  Signal type = Client layer
  Stage #1 = ODU where the client layer is muxed
  Stage #N = ODUk server layer
    E.g. ODU1->ODU2->ODU3->ODU4
      Signal Type = ODU1
      Stage #1 = ODU2
      Stage #2 = ODU3
      Stage #3 = ODU4

## Slide 6: New Bandwidth sub-sub-TLV (2-BW-var)
F flag - Unreserved vs MAX LSP bandwidth

## Slide 7: Procedures
A single ISCD per TE-Link MAY be advertised
Interfaces with different OTUk layers and different muxing hierarchies MAY be bundled together but a different SCSI TLV MUST be used for each different type of muxing hierarchy.
  Merging all the 3 different component links in the example above would cause and advertisement:
      ODU0->ODU3->ODU4 and ODU3->ODU4
  But in this case it is not possible to know how many ODU3->ODU4 are available for ODU3 FA set up (i.e. belonging to the ODU0->ODU3->ODU4 hierarchy) and how many simple ODU3 cannot be used for ODU0 transport (i.e. belonging to ODU3->ODU4 hierarchy).

## Slide 8: Next steps
Collect feedbacks from the meeting and ML
Keep alignment with OTN Framework and G.709 Info Model.
Adopt as WG document

## Slide 9: QUESTIONS ?
THANK YOU