## Slide 1: G.709 Optical Transport Networks Signaling Model Discussion
Chairs:
Lou Berger <lberger@labn.net>
Deborah Brungard <db3546@att.com>

## Slide 2: Purpose of today’s discussion
The WG has a disagreement about G.709 OTN signaling requirements
  Lots of discussion – on list and off list
  Much of the discussion has focused on a proposed mechanism and not requirements
This discussion is limited to requirements
  Once we have consensus on requirements can then move on to mechanisms

## Slide 3: Some relevant reminders: OTN
OTN supports multiple data rates / switching levels
  ODU0  ODU1  ODU2  ODU3  ODU4
  Lower rate ODUs may be multiplexed onto higher rate ODUs
    Without strict ordering
  Equipment may support switching at one or more ODU levels
  Equipment may have constraints on supported ODU levels per physical interface

## Slide 4: Some relevant reminders: GMPLS
LSP Tunnels or TE-LSPs
  Represent a data path between end-points in a single switching layer
  LSP Tunnels may or may not be established via control plane (e.g., RSVP-TE)
LSP Hierarchy, H-LSPs and FAs
  Hierarchy refers to the stacking of LSP tunnels
  H-LSPs refers to an LSP tunnel that may carry another LSP tunnel, and are typically represented as a TE link
    Represent a data path between end-points in a single switching layer
  An FA is a data (& TE) link provided by an H-LSP (or FA-LSP)
  Each level of the hierarchy may or may not be established via control plane (e.g., RSVP-TE)
Virtual TE Link
  TE link without a fully provisioned H-LSP/FA-LSP

## Slide 5: Consensus
There is a fair amount of agreement captured in
  draft-ietf-ccamp-gmpls-g709-framework
  draft-ietf-ccamp-otn-g709-info-model
  draft-khuzema-ccamp-gmpls-signaling-g709
Major points of agreement
  Need to support all ITU-T defined ODU levels and multiplexing in GMPLS signaling
  All existing signaling mechanisms can be used, notably: H-LSPs, FAs, Virtual TE Links

## Slide 6: Open requirements question: #1
ODU1 ODU1
| |
ODU2 ODU2
| |
ODU3 ODU3
| |
OTU3 OTU3
------ -----/ ------ \------ ------
|Node| |Node| |Node| |Node| |Node|
| |--------| |--------| |--------| |--------| |
| A | | B | | C | | D | | E |
------ ------ ------ ------ ------
|<-OTU2->| |<-OTU3->| |<-OTU3->| |<-OTU2->|
|<-----ODU3 H-LSP----->|
|<-------------------------ODU1 LSP------------------------->|
How many ODU (switching) levels can be represented in one signaled LSP?
  Today:
    LSP tunnel – 1
    H-LSP – 1 + TE Interface information for next level LSPs
  Proposed:
    1 service level + up to full underlying ODU multiplexing hierarchy on a given TE interface (physical or H-LSP)
  Discussion:

## Slide 7: Open requirements question: #2
How many layers can be identified in a signaled LSP’s ERO?
  Today:
    1 + TE interface information (including FAs & H-LSPs)
  Proposed:
    Up to full underlying ODU multiplexing hierarchy, & use to trigger FA-LSP creation
    Up to full underlying ODU multiplexing hierarchy, & use mechanism to support #1
  Discussion

## Slide 8: Open requirements question: #3
Should it be possible to signal in one LSP more than one layer on an egress?
  Today:
    Follows ERO
  Proposed:
    Up to full ODU multiplexing hierarchy
  Discussion

## Slide 9: G.709 Optical Transport Networks Signaling Model Discussion
Chairs:
Lou Berger <lberger@labn.net>
Deborah Brungard db3546@att.com