## Slide 1: GMPLS Signaling Extensions for the Evolving G.709 OTN Control
CCAMP WG, IETF 81th, Quebec City, Canada
draft-zhang-ccamp-gmpls-evolving-g709-08.txt
Authors & Contributors
Notes: <number>

## Slide 2: Authors & Contributors
Fatai Zhang zhangfatai@huawei.com
Guoying Zhang zhangguoying@mail.ritt.com.cn
Sergio Belotti sergio.belotti@alcatel-lucent.it
Daniele Ceccarelli daniele.ceccarelli@ericsson.com
Khuzema Pithewan kpithewan@infinera.com
Yi Lin yi.lin@huawei.com
Yunbin Xu xuyunbin@mail.ritt.com.cn
Pietro Grandi pietro_vittorio.grandi@alcatel-lucent.it
Diego Caviglia diego.caviglia@ericsson.com
Mohit Misra mmisra@infinera.com
Rajan Rao rrao@infinera.com
Ashok Kunjidhapatham akunjidhapatham@infinera.com
Biao Lu blu@infinera.com
Lyndon Ong lyong@ciena.com
Igor Bryskin IBryskin@advaoptical.com
Thanks Jonathan Sadler, John E Drake and other active experts for their useful comments to the document.

## Slide 3: Changes from Version 07
Merged <draft-khuzema-ccamp-gmpls-signaling-g709> and introducing the multi-stage label solution
Section 5.1
Definition of Generalized Label
Description of H-LSP using Generalized Label
Introducing optional multi-stage label object (New)
Description of multi-stage label solution using Generalized Label + multi-stage label (New)
Section 5.2
From <draft-khuzema>
Definition of multi-stage Generalized Label
Description of multi-stage label solution using multi-stage Generalized Label
Section 3.1
Requirements of ODU multiplexing (the reqs would be moved to <draft-ietf-ccamp-gmpls-g709-framework> after agreement)
New Development:
Authors agreed to have Generalized Label Format as specified in Section 5.2

## Slide 4: Requirements of ODU Multiplexing
[R2.1]: Pre-provisioned of intermediate ODU2
[R2.2]: Dynamic creation of intermediate ODU2
[R1]: Single-stage multiplexing (e.g., ODUj->ODUk, or ODUj->OTUj)
[R2]: Multi-hops multi-stage multiplexing
[R3]: One-hop multi-stage multiplexing
[R4]: Control & management of intermediate ODU layer
[R5]: Creating ODUj service involving various mux hierarchies on each hop
[R6]: Egress control of OTN interface
[R3.1]: Pre-provisioned of intermediate ODU2
[R3.2]: Dynamic creation of intermediate ODU2
OTU3
OTU3
ODU0
ODU2
ODU0->ODU2->ODU3
Section 3.1

## Slide 5: Multi-stage Labels
Multi-stage multiplexing
Multi-hop Multi-stage multiplexing
One-hop Multi-stage multiplexing
H-LSP
ODU multiplexing
One-stage multiplexing
No multi-stage muxing.
Don't need H-LSP or multi-stage label
Pre-provisioned of intermediate ODU
Dynamic creation of intermediate ODU
Pre-provisioned of intermediate ODU
Dynamic creation of intermediate ODU
H-LSP
H-LSP
multi-stage label
H-LSP
ODU multiplexing scenarios
Potential Solutions
Only need "service ODUj -> intermediate ODUk "label;
Multi-stage label is not necessary
Generalized Label = all stage muxing
Label format (Section 5.2)
Section 5.1 & 5.2

## Slide 6: Need Clarification w.r.t. RFC3471/3945
  RFC 3471/3945 states
    “A Generalized Label only carries a single level of label, i.e., it is non-hierarchical. When multiple levels of label (LSPs within LSPs) are required, each LSP must be established separately, see [MPLS- HIERARCHY].”
  OTN Label can essentially contain multiple stages, as described in section 5.2. Should we call it hierarchical Label or something different (OTN Composite Label?)?
  If it is hierarchical Label, then we might need a new draft to get this clarified w.r.t. RFC3471/3945

## Slide 7: Next Steps
WG document adoption?

## Slide 8
Backup slides for discussion

## Slide 9: Discussion Item#1 : Applicability of Multi-stage Label
Multi-stage label replaces single hop H-LSP(s).
  Multiplexing hierarchy needs to be same on the both ends of the link for multi-stage label to work.
If Multiplexing hierarchy on the 2 ends of the link is not same, then it calls for multi-hop H-LSP.
  Multi-stage label is not meant to replace multi-hop H-LSP
Notes: <number>

## Slide 10: Discussion Item#2: Restoration of single hop H-LSP
Single Hop H-LSP is a direct connection between 2 interfaces.
There is no switch fabric configuration involved in single hop H-LSP.
Since there is no mesh here, restoration is not applicable.
Only Link protection 1+1 or 1:n is applicable

## Slide 11: Discussion Item #3: Multi-stage Label and OAM
Ref: RFC 4783, draft-ietf-ccamp-oam-configuration-fwk-06
Both of these documents talk about end-to-end OAM of service layer.
It doesn’t address server layer(s) involved in supporting service layer.
If Multi-stage Label is used, OAM is applicable only to client signal that is mentioned in traffic specs.
  All the other layers, that are created to support service layer, doesn’t come in the purview of end-to-end OAM.

## Slide 12: Discussion Item#4: Egress Control through signaling
In the absence of multi-stage label as “egress label”, manual steps are needed to
  create the multiplexing hierarchy on lsp egress interface
  assign the interface indexes to each layer of the hierarchy
  This index and corresponding time slot information needs to be configured as part of LSP configuration.
Multi-stage label automates these manual steps through signaling (Ref: RFC4003)