## Slide 1: RSVP-TE Signaling Extension for Explicit Control of LSP Boundary in MRN/MLN draft-fuxh-ccamp-boundary-explicit-control-ext-03.txt
Xihua Fu
Qilei Wang
Yuanlin Bao
ZTE Corporation
Ruiquan Jing
Xiaoli Huo
China Telecom
Notes: fu.xihua@zte.com.cn
wang.qilei@zte.com.cn
bao.yuanlin@zte.com.cn
<number>

## Slide 2: Changes since last version
Adding a boundaries determination mechanism
Refining requirement
Editorial changes

## Slide 3: Boundaries Determination Mechanism
Problem Statement
  The boundary determination mechanism in [RFC4206] depends on the comparing of interface switching capabilities.
  For TDM switching capability, the comparing of interface switching capabilities relies on the max LSP bandwidth of interface.

## Slide 4: Boundaries Determination Mechanism
Problem Statement
  One interface in OTN network could support several ODUk signal types. The max LSP bandwidth makes no any sense to path computation entity. So the mechanism in [RFC4206] isn't applied to OTN multi-layer network.
  For example, PCE don’t know which are the boundary nodes of FA-LSP (e.g., ODU1 or ODU2) for e2e ODU0 LSP based on [RFC4206].
  This document introduces a generic mechanism for MRN/MLN to determine the boundaries of FA-LSPs by using termination and switching capability from IGP database.

## Slide 5: Boundaries Determination Mechanism
Example: Node B and D support ODUj being mapped into ODUk (k>j). Interface IF-B and IF-D support ODUj switching capability (ODUj(S)) and ODUk termination capability (ODUk(T)). Interface within node C only supports ODUk switching capability. So Node B and D could be boundaries of ODUk FA-LSP for ODUj LSP.

## Slide 6: Boundaries Determination Mechanism
Example: Hybrid node B and D support PSC being mapping into ODUk (e.g., by GFP-F). Interface IF-B and IF-D support PSC switching capability (PSC(S)) and ODUk termination capability (ODUk(T)). Interface within node C only supports ODUk switching capability. So Node B and D could be boundaries of ODUk FA-LSP for PSC LSP.

## Slide 7: Next steps
Refine the document according to the feedback of meeting and mailing list.