## Slide 1: LMP Behavior Negotiation and Configuration Modifications
CCAMP WG, IETF 81th, Quebec - CA
draft-ietf-ccamp-lmp-behavior-negotiation-04
Dan Li (danli@huawei.com)
D. Ceccarelli (daniele.ceccarelli@ericsson.com)
Lou Berger (lberger@labn.net )
Notes: <number>

## Slide 2: After Prague (80th) Meeting
Changes from 02 version:
  Added a new section 2: LMP Message Modifications
    To address the multiple config object issue
    Introduced the config object to ConfigAck and ConfigNack to allow explicit identification of non-supporting nodes
  Renamed BEHAVIOR_CONFIG to BehaviorConfig
    Consistent with 4240 naming style;
  Introduced separate format and procedures sub-sections in section 2 and 3;
  Slightly changed the format of BehaviorConfig
    Removed duplicate “Length” field
    "B" bit was dropped
  Revised backward compatibility section
  Added Lou Berger as a co-author
Notes: <number>

## Slide 3: Multiple CONFIG Objects Support
LMP Config, ConfigNack and ConfigAck messages are modified by this document to allow for the inclusion of multiple CONFIG objects:
<Config Message> ::= <Common Header> <LOCAL_CCID> <MESSAGE_ID> <LOCAL_NODE_ID> <CONFIG> [ <CONFIG> ... ]
<ConfigAck Message> ::= <Common Header> <LOCAL_CCID> <LOCAL_NODE_ID> <REMOTE_CCID> <MESSAGE_ID_ACK> <REMOTE_NODE_ID>[ <CONFIG> ... ]
<ConfigNack Message> ::= <Common Header> <LOCAL_CCID> <LOCAL_NODE_ID> <REMOTE_CCID> <MESSAGE_ID_ACK> <REMOTE_NODE_ID> <CONFIG> [ <CONFIG> ... ]
Notes: <number>

## Slide 4: Format of BehaviorConfig
Format of BehaviorConfig is changed:
  0 1 2 3
  0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  |S|D|C| Must Be Zero(MBZ) |
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
S: 1 bit --- [RFC4207] D: 1 bit --- [RFC4209] C: 1 bit --- [RFC5818]
Must Be Zero (MBZ): Variable length
Note:
The remaining bits in the flags field MUST be set to zero (0).
The number of bits present is based on the Length field of the LMP object header and MUST include enough bits so the Length field MUST be at least 8, and MUST be a multiple of 4.
Notes: <number>

## Slide 5: Backward Compatibility
  How will a legacy node handle a Config Message containing a BehaviorConfig:
ConfigNack -- due to unknown BehaviorConfig object type
ConfigNack -- due to multiple CONFIG objects
ConfigAck -- without any CONFIG objects
No response -- treat as malformed and drop without any response
  What a draft compliant node should do:
Cases (a), (b) and (c) allow explicit identification of a legacy neighbor  node should revert to current behavior
Case (d) results in reaching RFC4204 "retry limit"  node should revert to current behavior
Notes: <number>

## Slide 6: Next Steps
  Solicit feedback from WG
  Update document based on comments
  Comments?
Notes: <number>