## Slide 1: Akbar Rahman Esko Dijk IETF 81, July 2011 http://tools.ietf.org/html/draft-rahman-core-groupcomm-06
Group Communication for CoAP

## Slide 2: CoAP Group Communications Concept
1) Multiple receiver nodes form a group
3) Content is distributed to all members of group (e.g. multicast, series of multicast, or serial unicast)
2) Source (sender) sends a single message with content to the group address
4) Optional Response

## Slide 3: Requirements for Group Comm (1/4)
REQ1: Selectable Reliability:
  At least unreliable group communication supported, but preferably reliable group communications as well if possible
REQ2: Efficiency:
  Delivers messages more efficiently than a “serial unicast only” solution. Also, it should provide a right balance between group data traffic and control overhead
REQ3: Low Latency:
  Deliver a message (preferably) as fast as possible
REQ4: Synchrony:
  Allows near-simultaneous modification of a resource on all devices in a group, providing to users a perceived effect of synchrony or simultaneity
  It can be expressed as a time span “D” such that message “m” is delivered to all destinations in a time interval [t, t+D] for arbitrary “t”

## Slide 4: Requirements for Group Comm (2/4)
REQ5: Ordering
  [TBD to check what use cases require in terms of message ordering especially in multi-source situations]
REQ6: Security
  See Backup slides for 7 security requirements (reviewed in IETF Prague)
REQ7: Flexibility:
  Support for one or many source(s), for dense and sparse networks, for high or low listener density, one or many group(s), and multi-group membership
REQ8: Robust Group Management:
  Includes functionality to join groups, leave groups, view group membership, and persistent group membership in failing node or sleeping node situations

## Slide 5: Requirements for Group Comm (3/4)
REQ9: Network Layer Independence
  A solution should be specified independent from specific unicast and/or IP multicast routing protocols
  It should support different routing protocols and implementations thereof
REQ10: Minimal Specification Overhead
  A group communication solution should preferably re-use existing/established (IETF) protocols that are suitable for Low Power Lossy Network (LLN) and standard backbone deployments, instead of defining new protocols from scratch
REQ11: Minimal Implementation Overhead
  E.G. A solution allows to re-use existing (software) components that are already present on constrained nodes such as (typical) 6LoWPAN/CoAP nodes

## Slide 6: Requirements for Group Comm (4/4)
REQ12: Mixed backbone/LLN Topology Support
  A solution should work within a single LLN, and in combined LLN/backbone network topologies, including multi-LLN topologies
  Both the senders and receivers of CoAP group messages may be attached to different network links or be part of different LLNs, possibly with routers or switches in between group members
  In addition, different routing protocols may operate on the LLN and backbone networks. Preferably a solution also works with existing, common backbone IP infrastructure (e.g. switches or routers)
REQ13: CoAP Proxying Support
  A CoAP proxy can handle distribution of a message to a group on behalf of a (constrained) CoAP client

## Slide 7
Potential Approaches for Group Communication
There are three alternative approaches possible for CoAP group communications each with associated pros/cons:
  IP Multicast
    Routers must support multicast protocols
  Overlay Multicast
    CoAP Proxy nodes must support hybrid multicast functionality
  CoAP Application level Group Management
    CoAP application layer must support multicast functionality
(See backup slides for more details - reviewed in previous IETFs)

## Slide 8
Recommended Solution (1/2)
We recommend that IP Multicast be adopted as the base solution for CoAP Group Communication
  This approach requires no standards changes to the IP Multicast suite of protocols
  It does, however, require carfully implementing pieces of IP Multicast functionality in an LLN, in a backbone network, or in both
Implementation strategies for the following target network topologies are outlined in the I-D:
  Single LLN topology
  Single LLN with backbone topology
  Multiple LLNs with backbone topology

## Slide 9
Recommended Solution (2/2)
For all network topologies that were evaluated, CoAP group communication can in principle be supported with IP Multicast, making use of existing protocols
Also potential (but optional) optimizations were identified for an “MLD-like” or “MLD-lightweight” protocol specifically for LLNs, which would interwork with regular MLD on the backbone network
  E.G: A subset of MLD could be defined for an “MLD for 6LowPAN” to minimize complexity for constrained nodes

## Slide 10: BACKUP

## Slide 11
Background
This draft is a follow up to our previous draft on “Sleeping and Multicast Considerations for CoAP” which was in a problem statement format:
  http://tools.ietf.org/html/draft-rahman-core-sleeping-00
During the previous CORE Webex calls, we were asked to produce satellite drafts to more precisely identify the problems and provide some initial solution proposals for:
  Group Communications (as the more general problem of multicast) – This draft
  Sleeping Nodes – TBD draft (but in progress)

## Slide 12
IP Multicast
Concept:
  CoAP sub-networks to be connected directly to IP multicast enabled routers (e.g. running PIM-SM [RFC4601]).
  Sending CoAP node can directly transmit group messages by setting IP address to selected multicast IP group address
  Receiver CoAP nodes use MLD [RFC3810] to subscribe (listen) to any messages sent to selected IP multicast group
Pros
  Most efficient solution since done at IP layer
  ROLL [draft-ietf-roll-rpl-14] assumes IP multicast supported
  CoAP-03 draft [section 4.1] assumes IP multicast supported
Cons
  IP multicast is not generally deployed outside of corporate LANs and a few ISPs. So we may specify IP multicast support but practically it may often not be deployed

## Slide 13
Overlay (Proxy based) Multicast (1/2)
Concept:
  We define overlay multicast as one that utilizes an infrastructure based on proxies (rather than an IP router based multicast backbone) to deliver IP multicast packets to an end device
  Since ROLL and CoAP drafts already support MLD (see pg. 4), we propose MLD Proxy [RFC3810] to be used as the overlay multicast approach
  Specifically, the CoAP proxy node will also support Proxy MLD
  Receiver CoAP nodes use MLD Proxy signaling to subscribe (listen) to any messages sent to selected IP multicast group
  The CoAP (MLD) proxy node would be responsible for delivering any IP multicast message to the subscribed CoAP devices
  Note that the CoAP (MLD) proxy need not necessarily be connected to an external multicast backbone

## Slide 14
Overlay (Proxy based) Multicast (2/2)
Pros
  Ties well into existing CoAP proxy concept
Cons
  It is not obvious that existing MLD Proxy [RFC 3810] allows the specific scenario we are proposing. Further investigation required.

## Slide 15
CoAP Application level Group Mgmt
Concept:
  Perform all group communications at the CoAP application level
  Expand CoAP headers to allow simple group mgmt functions (Join, Leave, etc.)
  The CoAP proxy node would be responsible for group mgmt
  Any CoAP node that wanted to send a message to a CoAP group would first send the CoAP message to the proxy. The proxy would then explode it out to the group
Pros
  Functionality fully within the CoAP protocol (and CORE WG control)
  Analogous approach as Email group management (and other Apps)
Cons
  Has high overhead compared to lower layer solutions

## Slide 16
Group Resource Manipulation (1/3)
Needed to replicate functionality of existing standards, e.g. BACnet’s Alarm and Event Notification service
Two forms of group resource manipulation should be supported:
  Push (PUT or MPUT) as for example “turn off all lights simultaneously”
  Pull (GET or MGET) as for example “return all the resources matching a well known URI”
Conceptually, the result of a MGET or MPUT should be the same as if the client had unicast them serially

## Slide 17
Group Resource Manipulation (2/3)
Limit manipulation to idempotent methods (PUT/GET/DEL)
  Repeat requests can then be used to increase reliability of receipt
Requires a consistent naming and addressing scheme for groups
  Multicast is the easy case; can use DNS to resolve FQDN in authority to multicast or unicast address
Can a group be represented by a list of addresses as well?
  If so, perhaps this argues for a group scheme, e.g. “coapm” to signal a proxy to do fan-out task

## Slide 18
Group Resource Manipulation (3/3)
Target resource must be located at same port and path for all group members
  Suggests a need to advertise path, port or have a priori agreement

## Slide 19: Security Considerations
As per major comment from IETF79 (Beijing), reviewed output of:
  IETF MSEC (Multicast Security)
    In particular, [RFC3740], [RFC5374] and [RFC4046] are very instructive
  IRTF SAMRG (Scalable Adaptive Multicast Research Group)
And derived the following requirements for securing group communications in CoAP

## Slide 20: Group Security Requirements for CoAP (1/3)
REQ1: Group communications data encryption:
  Important CoAP group communications shall be encrypted (using a group key) to preserve confidentiality. It shall also be possible to send CoAP group communications in the clear (i.e. unencrypted) for low value data.
REQ2: Group communications source data authentication:
  Important CoAP group communications shall be authenticated by verifying the source of the data (i.e. that it was generated by a given and trusted group member). It shall also be possible to send unauthenticated CoAP group communications for low value data.
REQ3: Group communications limited data authentication:
  Less important CoAP group communications shall be authenticated by simply verifying that it originated from one of the group members (i.e. without explicitly identifying the source node). This is a weaker requirement (but simpler to implement) than REQ2. It shall also be possible to send unauthenticated CoAP group communications for low value data.

## Slide 21: Group Security Requirements for CoAP (2/3)
REQ4: Group key management:
  There shall be a secure mechanism to manage the cryptographic keys (e.g. generation and distribution) belonging to the group; the state (e.g. current membership) associated with the keys; and other security parameters.
REQ5: Use of Multicast IPSec:
  The CoAP protocol [I-D.ietf-core-coap] allows IPSec to be used as one option to secure CoAP. If IPSec is used at the CoAP level, then multicast IPSec [RFC5374] should be used for securing CoAP group communications.
REQ6: Independence from underlying routing security:
  CoAP group communication security shall not be tied to the security of underlying routing and distribution protocols such as PIM [RFC4601] and ROLL [I-D.ietf-roll-rpl]. Insecure or inappropriate routing (including multicast routing) may cause loss of data to CoAP but will not affect the authenticity or secrecy of CoAP group communications.

## Slide 22: Group Security Requirements for CoAP (3/3)
REQ7: Interaction with HTTPS:
  The security scheme for CoAP group communications shall account for the fact that it may need to interact with HTTPS (Hypertext Transfer Protocol Secure) when a transaction involves a node in the general Internet (non-constrained network).

## Slide 23: CoAP Multicast and HTTP Unicast Interworking (1/2)

## Slide 24: CoAP Multicast and HTTP Unicast Interworking (2/2)
Proxy node needs to have the following functionalities to interwork CoAP/UDP (multicast) and HTTP/TCP (unicast):
  Incoming HTTP Request will carry a URI (with HTTP scheme)
  At the proxy node, the URI will then be again resolved (with CoAP scheme) to an IP multicast. This may be accomplished, for example, by using DNS-SD
  The proxy node will then multicast the CoAP Request to the appropriate nodes
CoAP proxy can be considered to be a "non-transparent" proxy according to [RFC2616]:
  Specifically, [RFC2616] states that a "non-transparent proxy is a proxy that modifies the request or response in order to provide some added service to the user agent, such as group annotation services, media type transformation, protocol reduction or anonymity filtering."