## Slide 1: CoAP Size Option Extension
draft-li-core-coap-size-option-01

## Slide 2: Current Issue 1: Post/Put
Using Post/Put for a large object
Client
Server
Post/Put: Blocks
Data is too big to be accepted
4.13 Request Entity Too Large
Issue: In this case the whole transmission has failed, and the previous received data will be useless. This is a waste of transmission resources.
Transmission failed
.
.
.

## Slide 3: Current Issue 2: Get
Current feature:
  Use link-format to retrieve the maximum estimated size
Issues
  It is not accurate, and the resource size may be changed
  It is not possible for the requester to know exactly how many blocks will be transmitted, therefore, concurrent Get can't be supported.

## Slide 4: Size Option
Usage
  In Put/Post request and Get response:
--Indicate the resource size
  In Get request with Size=0:
--Get the resource size, not the payload
+-------+------+---------+--------------+-----------+---------------+
| Type | C/E | Name | Data type | Length | Default |
+-------+------+---------+---------------+----------+---------------+
| 12 | E | Size | uint | 1-4 B | |
+-------+------+---------+---------------+----------+---------------+
Definition

## Slide 5: Size Option in a Get response
CLIENT SERVER
| |
| CON [MID=1234], GET, /status ------> |
| |
| <------ ACK [MID=1234], 2.00 OK, 0/1/128, Size: 5000 |
| |
| CON [MID=1235], GET, /status, 1/0/128 ------> |
| |
| <------ ACK [MID=1235], 2.00 OK, 1/1/128 |
| |
| ... ... |
| |
| CON [MID=1280], GET, /status, 40/0/128 ------> |
| |
| <------ ACK [MID=1280], 2.00 OK, 40/0/128 |
| |

## Slide 6: Size Option in a Put request
CLIENT SERVER
| |
| |
| CON [MID=1234], Put, /options, 1/0/128, Size: 5000 ----> |
| |
| <------ ACK [MID=1234], 4.13 Request Entity Too Large |
| |
| |
| |
| |

## Slide 7: Conclusion
Open Issues from the discussion in the mailing list
  Should the Size option be Elective or Critical?
  Need analysis about the influence of the Block1/Block2 design
  Need to check implementations about this option
Next steps
  Is it OK for the group to accept this as a WG item?