## Slide 1: CoAP Request-Timeout Option
draft-li-core-coap-request-timeout-option-00

## Slide 2: Request-Timeout option
Purpose
  Indicate the maximum time that a client is prepared to wait for a response
  Client knows how long it should wait for the response, and keeps state for the request for the indicated time
  After the indicated time, client may give up the request
Benefit
  It can avoid that the server wastes resources by sending a response which already exceeds the set timeout of the client.
  The transmission resource can be saved to avoid the retransmission of requests.

## Slide 3: Request-Timeout Option
0
  0 1 2 3 4 5 6 7
  +-+-+-+-+-+-+-+-+
  | T |
  +-+-+-+-+-+-+-+-+
  Request-Timeout = 2^T milliseconds
+-------+------+--------------------------+--------------+-----------+---------------+
| Type | C/E | Name | Data type | Length | Default |
+-------+------+--------------------------+---------------+----------+---------------+
| 20 | E | Request-Timeout | uint | 0-1 B | |
+-------+------+---------------------------+---------------+----------+---------------+
Definition
Notes: "two to the power of T“. T is from 0 to 255, Request-Timeout is from 2^0 ~ 2^255
<number>

## Slide 4: Example
Client Server
| |
| |
+-----------> | Header: GET (T=CON, Code=1, MID=0x7d38)
| GET | Token: 0x53
| | Request-Timeout: 00001011 (2048 milliseconds)
| | Uri-Path: "temperature"
| |
|<-------- ---+ Header: 2.05 Content (T=ACK, Code=69, MID=0x7d38)
| 2.05 | Token: 0x53
| | Payload: "22.3 C"
| |

## Slide 5: Conclusion
Open Issues from the discussion in the mailing list
  Should we use milliseconds or mibiseconds (1/1024s)?
  Differences between Request-Timeout and Connection-Timeout?
  Need to check implementations about this option
Next steps
  Is it OK for the group to accept this as a WG item?