## Slide 1: Diameter Bulk Signaling draft-liebsch-dime-diameter-bulksig-00.txt
M. Liebsch, G. Punz
IETF81, Quebec Diameter Maintenance and Extensions (DIME) WG
28th July 2011

## Slide 2: Outline
Motivation to have this document
Proposed structure for a joint draft
Some details on proposed content
Next steps

## Slide 3: Motivation & Background (1/2)
SDOs utilize Diameter on various reference points in their architecture
  3GPP
  ETSI‘s TISPAN
Need for bulk signaling identified and discussed
  Mass handling, e.g. re-registration, state restoration
Discussion about draft-liebsch-dime-diameter-gps during IETF79 and IETF80
  Proposes dedicated Diameter Session for bulk signaling
  Discusses grouping of Attribute-Values for bulk transmission

## Slide 4: Motivation & Background (2/2)
Valuable feedback received
  More use cases and enlarged scope
  GP Session has value, but represents a new application
    Platform for specification: DIME or alternative group
  Good idea, but overloading is 3GPP habit
    New messages as alternative
  GP Session has clear rules, but other SDOs (TISPAN) just ignore the Session ID
  Enlarge the scope of the idea to address also signaling without Session ID
    Focus on grouping for bulk signaling
Conclusion at IETF80: Interest & space for this work in the DIME group
Start with Use Cases & Practices

## Slide 5: First version of the draft..
Is a proactive submission to initiate new work
Reflects the discussion with the WG
Proposes initial structure and content
Solicit input and contributions towards a joint WG document
Target: Specification of bulk signaling as solution for SDOs

## Slide 6: Proposed Document Structure
Introduction
Conventions and Terminology
Analysis of Use Cases
Practices for Bulk Signaling & Classification
Detailing selected Practice
Approaches to group Attribute-Value-Pairs for bulk transfer of multi-user context
Security Considerations
IANA considerations

## Slide 7: Analysis of Use Cases
General: Reduce signaling volume
  Signal bulk information to reduce number of single protocol handshakes
State restoration
  After node failure/restart [3GPP TS 29.816]
  Client re-registration after node failure addressed in [TD S2-113795]
Group handling
  Policy enforcement [ETSI TS 183 060]
  Policy requests

## Slide 8: Analysis of Use Cases Example from 3GPP, Concern about signaling volume
MME
Home Subscriber Server
Mobility Management Entity
HSS
Location Update (new Tracking Area)
Update Location Request
Diameter on S6a
MME
Inter-MME Tracking Area Update

## Slide 9: Practices
Overloading the Session ID
  Use single user‘s Session ID, signal multi-user context
Disregarding the Session ID
  Application user key/Identifier not linked to Session ID
  No Session-ID maintained for subscribers
    Auth-Session-State AVP has value NO_STATE_MAINTAINED
  New application, Diameter Session-ID ‘terminated implicitly‘
    Used messages mandate Session-ID AVP, but it has no meaning
  Approach suitable for bulk signaling

## Slide 10: Practices
Use of messages, which do not use Session IDs
  Limited existing messages
  New messages
Dedicated Session ID
  Dedicated for bulk operations in addition to per-user Session IDs

## Slide 11: Practices / Categories
Application
Diameter base
Session-ID
User Info/key
Category:
( I )
( II )
( III )
( IV )
Session-ID linked to Application user key
Session ID independent of Application user key
No Session ID used, single Application user key signaled
Overloading of Session ID, which is linked to one of multiple signaled Application user keys
Overloading of Session ID, which is independent of multiple signaled Application user keys
No Session ID used, multiple Application user keys signaled
( V )
( VI )
Single-user context
Multi-user context (bulk)

## Slide 12: Grouping APVs for bulk signaling (in the order of efficiency)
Group-ID identifies multiple users, list of attributes/values applies to all users of the group
List of Session-IDs identifies a group of users, list of attributes/values applies to all users of the group
List of Session-IDs identifies multiple users, each Session-ID has an individual list of AVPs associated
Diameter Hdr
[Session-ID]
AVP 1
Group-ID
AVP 2
AVP N
Diameter Hdr
[Session-ID]
AVP 1
Session-ID 1
AVP 2
AVP N
Session-ID K
Diameter Hdr
[Session-ID]
AVP 1.1
Session-ID 1
AVP K.1
Session-ID K
AVP 1.2
AVP 1.N
AVP K.2
AVP K.N

## Slide 13: References
ETSI TS 183 060, Resources and Admission Control Subsystem (RACS); Re interface based on the Diameter protocol
3GPP TS 29.272, Mobility Management Entity (MME) and SGSN related interfaces based on the Diameter protocol
3GPP TS 29.816, Study on PCRF Failure and Restoration
TD S2-113795, Contribution to 3GPP TSG SA2 WG2 meeting #86, 11-15 July 2011, Core Network Overload Solution Study
  Scope: Identify and document scenarios, that may result in signaling overload
    State restoration after reboot, results in burst of re-registrations from mobile nodes

## Slide 14: Next
Update according to agreed structure
Target mature version before next IETF
Adoption of this work item and document