## Slide 1: Revision of the Binary Floor Control Protocol (BFCP) for use over an unreliable transport (draft-sandbakken-dispatch-bfcp-udp-02)
Charles Eckel, Tom Kristensen, Mark Thompson, Geir Arne Sandbakken, Eoin McLeod
IETF-81, Quebec City, July 25-29, 2011

## Slide 2: Changes from Previous Version
Switched from standard track to informational
Added section on motivation, including alternatives considered
Changed semantics of the Transaction Initiator (I) flag-bit
Expanded transport section with considerations for:
  congestion control
  ICMP errors
  large messages/fragmentation
Updated security related sections
  DTLS when using UDP
Added section on NAT Traversal

## Slide 3: Use Case – SIP Videoconferencing
BFCP used for floor control of content sharing video stream
BFCP server and participant roles negotiated via SDP offer/answer exchange
Responsibility for opening the BFCP channel negotiated via SDP offer/answer exchange
A “normal user endpoint” might need to act as a BFCP server and/or initiate the connection for the BFCP channel
  Point-to-point/Peer-to-peer/Business-to-business
  Point-to-multipoint (potential internal MCU)
One/Both BFCP entities behind NATs/firewalls

## Slide 4: Motivation
Existing deployments of SIP based videoconferencing typically:
  Consist of RTP media streams for audio and video
  Use ICE and/or other methods for NAT/firewall traversal
  Found in enterprise networks
When enhancing with support for content sharing, the BFCP connection often poses a problem
  There may be a strong preference for UDP based signaling in general
  Establishment/traversal of the TCP connection involving ephemeral ports, as is typically the case with BFCP over TCP, can be problematic
This draft defines UDP as an alternate transport for BFCP, leveraging the mechanisms in place for RTP over UDP media streams for the BFCP communication

## Slide 5: Approach
Minor changes to transaction model
  All requests now have a response to complete transaction
    Added an explicit “Ack” primitive for each case in which none existed
  Retransmission timer to ensure reliability
  Transaction Initiator flag to distinguish request vs. response
  One pending request per entity (ordering, congestion control)
Goodbye/GoodbyeAck dissociate (TCP/BFCP close)
New ERROR-CODEs for following cases:
  Unable to parse message
  Use DTLS
DTLS MUST be supported
ICE/STUN if applicable and needed

## Slide 6: Request/Response
RFC 4852 primitives in BLUE, new primitives in GREEN ITALICS
FloorRequest / FloorRequestStatus
FloorRelease / FloorRequestStatus
FloorRequestStatus / FloorRequestStatusAck
FloorRequestQuery / FloorRequestStatus
UserQuery / UserStatus
FloorQuery / FloorStatus
FloorStatus / FloorStatusAck
ChairAction / ChairActionAck
Hello / HelloAck
Error / ErrorAck
Goodbye / GoodbyeAck
UserStatus / UserStatusAck [QUESTION: DO WE NEED TO ADD THIS]

## Slide 7: Transaction Initiator (the problem)
Some primitives can be either a request or a response
    FloorRequest / FloorRequestStatus
      but then
    FloorRequestStatus / FloorRequestStatusAck
    FloorQuery / FloorStatus
      but then
    FloorStatus / FloorStatusAck
Distinguishing between the two requires some state information beyond that desirable at the stack level

## Slide 8: Transaction Initiator (the solution)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-++
| Ver |I| Res | Primitive | Payload Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Conference ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transaction ID | User ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Has relevance only for use of BFCP over unreliable transport.
When clear, it indicates that this message is a request initiating a new transaction, and the Transaction ID that follows has been generated for this transaction.
When set, it indicates that this message is a response to a previous request, and the Transaction ID that follows is the one associated with that request.
When BFCP is used over reliable transports, the flag has no significance and SHOULD be cleared.

## Slide 9: Security
Mandate support for DTLS for transport over UDP:
  BFCP floor control servers and clients (which include both floor participants and floor chairs) MUST support TLS for transport over TCP and MUST support DTLS for transport over UDP [RFC5246].
  Which party, the client or the floor control server, acts as the TLS/DTLS server depends on how the underlying TCP/DTLS connection is established. For example, when the TCP/DTLS connection is established using an SDP offer/answer exchange [RFC4583], the answerer (which may be the client or the floor control server) always acts as the TLS/DTLS server.
TLS  TLS/DTLS for mutual authentication and security considerations
Adopt strategy similar to DTLS-SRTP specifications (RFC5763 and RFC5764) for negotiation

## Slide 10: NAT Traversal
Leverage existing NAT traversal infrastructure and strategies deployed to facilitate transport of the media associated with video conferencing sessions
Typically includes some subset of ICE [RFC5245]
RECOMMEND STUN [RFC5389] for keep-alives
  As described for SIP [RFC5626]
  Facilitate establishment and maintenance of NAT bindings
RECOMMEND symmetric ports for sending and receiving BFCP packets
  As recommended for RTP/RTCP [RFC4961]

## Slide 11: Future Work
Adapting DTLS usage to BFCP
  DTLS-SRTP specifications RFC 5763 and RFC 5764 referenced as example, need to add details
Example signaling exchanges over unreliable transport
  updated transactions
  message retransmission
  DTLS during call setup
IANA Considerations
  Now that draft is informational, it can no longer add attributes to the registries defined for BFCP per the requirements stated in RFC 4582
  Sections related to IANA considerations will need to be reworked

## Slide 12: Thank You
Charles Eckel, Tom Kristensen, Mark Thompson, Geir Arne Sandbakken, Eoin McLeod
IETF-81, Quebec City, July 25-29, 2011