## Slide 1: Extensions to the Emergency Services Architecture for dealing with Unauthenticated and Unauthorized Devices
draft-ietf-ecrit-unauthenticated-access-03.txt

## Slide 2: Status
draft-ietf-ecrit-unauthenticated-access-02.txt received a number of review comments from Bernard Aboba, Martin Thomson, and Marc Linsner
Main issues on the next few slides.
draft-ietf-ecrit-unauthenticated-access-03.txt addresses editorial comments and minor comments.

## Slide 3: Issue #1: No Access Authentication (NAA)
Start
Lower-layer attach
Waiting for ES call initiation
NAA
NASP
PhoneBCP
PhoneBCP
ZBP
Credentials for network access authentication available?
yes
yes
Emergency NW attach possible?
yes
no
ASP configured?
no
yes
Authorized to make ES call?
no
no
Tell user that ES call is not
allowed in jusristiction

## Slide 4: Call Flow
Routing Database
PSAP
(1)
Location
Location + Service Identifier
(2)
PSAP URI + emergency number
(3)
(4)
(5)
Location Information Server
INVITE
Request URI: urn:service:sos
To: urn:service:sos
Route Header: PSAP URI
<PIDF-LO>
INVITE
Request URI: urn:service:sos
To: urn:service:sos
Route Header: PSAP URI
<PIDF-LO>
dial 9-1-1
VSP
SIP Proxy

## Slide 5: Issue #2: The State of Hotspot Access
Bernard illustrated that the current hotspot access is quite bad and there is no easy way to get to the functionality we would need.
The currently described functionality captures the envisioned end state and does not explain how to get to that state given the nastiness of today's network deployments.
On one hand we want to provide a technical write-up about the functionality that is needed to make calls in the NAA case but on the other hand we need to point to the problems to get there.

## Slide 6: Issue #3: Lack of network access authorization
The NAA case only focuses on the lack of credentials but does not consider the case where credentials are available but network access authorization fails nevertheless.
Lack of authorization at the application layer is covered.

## Slide 7: Network Access Authentication Architecture
EAP peer (supplicant)
EAP lower
Layer
(e.g.,
802.11i)
AAA Client
EAP lower
Layer
(e.g.,
802.11i)
AAA
Server
EAP server
End Host /
EAP Peer
Network Access Server /
Authenticator /
AAA Client
AAA Server /
EAP server
EAP method
EAP MSK
EAP MSK

## Slide 8: Issue #4: Document Writing Style
An editorial question was raised by Martin as well
  Currently, the draft states the steps that are necessary for performing the emergency call. There are only a few steps.
  Martin suggested to instead reference the selected parts from the phone BCP and say what is not applicable.
  Another option is to provide a summary of what is different.