## Slide 1: EAP Extensions for EAP Re-authentication Protocol draft-ietf-hokey-rfc5296bis-04
26/7/31
Hokey IETF 81 Quebec
<number>
Qin Wu
Zhen Cao
Yang Shi
Baohong He

## Slide 2: Outline
26/7/31
Hokey IETF 81 Quebec
<number>
Changes
Issues
Moving Forwarding
Notes: Being Adopted after IETF 79, Beijing
00 version WG draft submitted before IETF 80, Prague
Remaining issues waiting for being addressed
  How FEC is taken into account in this draft
  how Distribution source in the SSM case react to different reports

## Slide 3: Changes since previous version
26/7/31
Hokey IETF 81 Quebec
<number>
Explain why SHOULD is implemented instead of using MAY in section 5.3.1.1.
Keep local and home distinction in accordance with last meeting consensus
Separate the last two paragraph as independent bullets in section 8.
  Prevent DoS attack
  Keying materials Transport
Simplify Implicit bootstrapping and Explicit bootstrapping
  Keep ‘B’ flag in the ERP Initiate message
  Allow ER authenticator respond to the peer directly without forwarding the ERP message to the home domain

## Slide 4: Issue from Diameter ERP
Session Management during Peer handover
  Is the session considered a new session each time handover?
    Yes: different Session-Id, new Authorization, …
    No: problem with server-initiated messages
      When the peer move to the new authenticator, how does the server know this and send the message to the new authenticator?
      Possible way to solve this is to register the new location of the new authenticator each time peer moves.
    In both cases, problem with accounting if there is no constant unique identifier to identify session during handoff
    Possible workaround: Using Acct-Multiple-Session-Id to treat the sessions during handoff as the same session
26/7/31
Hokey IETF 81 Quebec
<number>
Client
Previous
NAS
New
NAS
Home Diameter
EAP Server
Session-Id1
Session-Id1
Acct-Multi-Session-Id

## Slide 5: Issue from Diameter ERP
Multiple EAP servers located in the same home realm
  Finding the right EAP server for bootstrapping
    Which one has the EMSK for the session?
Previous
NAS
Current
NAS
Local
ER Server
Client
Home EAP Server 1
Home EAP
Server 2
Home EAP
Server 3
  Possible Workaround
    Allow multiple EAP severs located in the home realm (1)
      Not specific to Diameter ERP application since various home EAP servers can not be distinguished using the same real name.
      Even Using Decorated NAI can not reach the right Home EAP server
      Allow local ER server to save the the home EAP server name if all NAS share the same Local ER server
    Only allow one home EAP server located in the home realm (2)
@Example.com
@Example.com
@Example.com
Realm Part of KeyName-NAI
Username part of KeyName-NAI
e.g.,Efdgegdgad @

## Slide 6: Issue from Diameter ERP
Multiple EAP servers located in the same home realm
    New issue arises when we allow multiple local ER server located in the same visited realm
      When the client handover from previous local ER server to the new local ER server, Previous local ER server save home EAP server name but current Local ER server haven’t saved home EAP server name.
  Possible workaround
    Possible way to fix this is to allow previous Local ER server inform other ER server in the same visited domain about home EAP server name.
26/7/31
Hokey IETF 81 Quebec
<number>
Previous
NAS
Current
NAS
Previous
Local ER Server
Current
Local ER Server
Home EAP Server 1
Home EAP Server 2
Home EAP Server 3
Client
@Example.com
@Example.com
@Example.com

## Slide 7: Moving Forward
26/7/31
Hokey IETF 81 Quebec
<number>
Known issue waiting for being addressed
  remove Explicit bootstrapping case
  Limit use of ERP in the visited domain or local domain
Encourage more review of draft and early feedback