## Slide 1: Exploring the multi-router SOHO network
draft-baker-fun-multi-router
Fred Baker

## Slide 2: Residential Network and Home Area Network Interaction
Imagine a high end home network:
  Audio/Video
  Wireless
  Telecommuting
  Home Area Network
What is the HAN?
  Network connecting sensors in the home
  Communications with utilities
  Services to residents
Her
Office
His
Office
A/V LAN
Home
Wireless
“Home
Area
Network”
ISP

## Slide 3: Related to sensor networks for health…
Infrared
Motion sensors
EKG
Pedometers
…
Her
Office
His
Office
A/V LAN
Home
Wireless
Health
Network
ISP

## Slide 4: Add residential multihoming
Requirement in Japan
  Typical residence typically has at least two ISPs
  One serves IPTV only
  One is for general internet access
Her
Office
His
Office
A/V LAN
Home
Wireless

## Slide 5: We could do this all with one router (and my company would like to sell it to you)
My home is actually somewhat like this
Cisco 871/891 is not exactly free
Her
Office
His
Office
A/V LAN
Home
Wireless

## Slide 6: Discussion in the draft
Issues
  Routing in a small network
  Assigning Subnet Numbers
Possible Requirements
  Source/Destination Routing
  Subnet assignment
  Recommended upstream route

## Slide 7: Issue: Routing in a small network
If you go with the lower cost add-as-you-go model, you wind up with multiple routers
  That implies some variation on routing within the home
  Hiding your head under a rock is not a good solution to routing
What recommendations do we make?
  RIPng? OSPFv3? IS-IS? BGP4+? Something else?

## Slide 8: Issue: Assigning Subnet Numbers
If you have multiple LANs, you wind up with multiple subnets
  That implies some way to (zeroconf) assign subnet numbers
What recommendations do we make?
  New protocol?
  DHCPv6? Keyed off OSPF/IS-IS?
  Netconf Network Management?

## Slide 9: Assigning Subnet Numbers
One way to do this might be to
  Have ISP-facing router implement a DHCPv6 server to allocate subnets
  Use OSPF/IS-IS to identify a significant (“designated”) router on each LAN
  Designated router allocates subnet prefix from the DHCPv6 server
That’s an example
  How should it be done?

## Slide 10: Exit Routing
The current IPv6 multihoming model calls for
  Hosts, which have no knowledge of routing, select optimal source address
  Routers, which have no semantic for the purpose, to route traffic to the right exit gateway
It would be nice if we had a way to do exit routing (comment made in shim6, applies here)

## Slide 11: Recommended upstream route
In routing, a router or network generally tells neighboring routers or networks what routes it might be able to handle
  Japanese IPTV ISP only accepts traffic using its assigned source address and heading to it
  Other ISPs will require use of their source address (BCP 38) and give access to other destinations
ISPs don’t generally exchange routing with residential customers
  Would it be nice to configure a recommended upstream route using DHCPv6?