## Slide 1: Routing a class of traffic
draft-baker-fun-routing-class
Fred Baker

## Slide 2: Change of paradigm
Typical Internet routing (RIP, OSPF, IS-IS, BGP) routes to a destination
  Variation: OSPF supports routing to a destination using a DSCP
  Proprietary extensions: traffic matching an ACL is routed to a neighboring router
Generalization:
  Traffic conforming to a certain description is routed somewhere (“route a class of traffic”)
  Traffic class definition:
    {destination, source|*, DSCP|*, …}

## Slide 3: Examples
    Destination route
      {D=prefix, S=::, *, …}
    Route from IPTV-allocated prefix to IPTV ISP
      {D=IPTV ISP, S=TV-prefix, *, …}
    Route from ISP-allocated prefix to ISP
      {D=2001::/3, S=ISP-prefix, *, …}

## Slide 4: Conceptual model
Replace “longest match” rule with “most specific”
  Consider a route to be an aggregation of some number of host-to-host routes
  Select the matching traffic class that does so most specifically
Aggregation of routes:
  A traffic class that matches several more specific traffic classes is an aggregation of those traffic classes

## Slide 5: Implementation with DV or SPF algorithms
Discussed in draft in hand-wavy fashion
  I won’t bore you here unless you really want me to…