## Slide 1: Scalable Loop Free BGP FRR Using Repair Label draft-bashandy-idr-bgp-repair-label-02
EDCS-875479
1
IETF 81, Jul/2011, Quebec City, Canada
draft-bashandy-idr-bgp-repair-label-02
Presenter :
Jakob Heitz,
Ericsson
IETF81, Jul/2011
Quebec City, Canda
Authors :
  Ahmed Bashandy, Cisco Systems
  Burjiz Pithawala, Cisco Systems
  Jakob Heitz, Ericsson

## Slide 2: What do we want to do
EDCS-875479
2
IETF 81, Jul/2011, Quebec City, Canada
draft-bashandy-idr-bgp-repair-label-02
BGP free core
  Packets are tunneled between edge routers
On loss of primary path, we want to
  Restore traffic through a pre-calculated repair path
    without waiting for control plane convergence, and
    avoid loops when restoring traffic

## Slide 3: Possible Solution
EDCS-875479
3
IETF 81, Jul/2011, Quebec City, Canada
draft-bashandy-idr-bgp-repair-label-02
PE1
PE2
VPNPE2
LDPPE2
Packet
Network X
Packet
Packet
VPNPE3
Packet
VPNPE2
PE3
CE1
Swap VPNPE2 with VPNPE3
Push LDPPE3
VPNPE3
LDPPE3
Packet
CE2
Packet
Packet

## Slide 4: Problem: If CE fails
EDCS-875479
4
IETF 81, Jul/2011, Quebec City, Canada
draft-bashandy-idr-bgp-repair-label-02
PE1
PE2
VPNPE2
LDPPE2
Packet
Network X
Packet
Packet
VPNPE2
PE3
CE1
CE2
VPNPE2
LDPPE2
Packet
Packet
VPNPE2
VPNPE3
LDPPE3
Packet
Packet
VPNPE3
Packet
If the CE fails, we have a loop !!!

## Slide 5: Proposed Solution
EDCS-875479
5
IETF 81, Jul/2011, Quebec City, Canada
draft-bashandy-idr-bgp-repair-label-02
A PE having an external path advertises a “repair” label
  Optional non-transitive attribute
When repairing a failed NH, the repairing router uses the repair label instead of the primary label advertised by the repair PE
The repair PE never repairs repaired traffic:
  Deliver the packet to the external next hop
  OR
  Drop it

## Slide 6: Proposed Solution
EDCS-875479
6
IETF 81, Jul/2011, Quebec City, Canada
draft-bashandy-idr-bgp-repair-label-02
PE1
PE2
VPNPE2
LDPPE2
Packet
Network X
Packet
Packet
VPNPE2
PE3
CE1
CE2
Packet
REPPE3
REPPE3
LDPPE3
Packet
Packet
No Loop

## Slide 7: Changes from Previous Version
EDCS-875479
7
IETF 81, Jul/2011, Quebec City, Canada
draft-bashandy-idr-bgp-repair-label-02
Specify forwarding behavior for edge node
A packet arrives from the core
  If there is an external path
    Deliver to external path
  If there is no external path
    If there is a repair PE, forward to repair PE
    Else
      Drop
A packet arrives NOT from the core
    Forward with the regular label

## Slide 8: Q & A
EDCS-875479
8
IETF 81, Jul/2011, Quebec City, Canada
draft-bashandy-idr-bgp-repair-label-02