## Slide 1
July 18
IEEE Plenary San Francisco
IEEE 802.1
1
802.1aq/SPB - 3rd Interop Overview
Onsite
Edgard Vargas – Alcatel Lucent Peter Ashwood-Smith - Huawei John Vant Erve - Avaya Stephane Vinet - Spirent Bis Nandy – Solana
Rup Makkar - Solana
Date
June 27-30 Ottawa/Canada

## Slide 2: 802.1aq Standardization
July 18
IEEE Plenary San Francisco
IEEE 802.1
2
Project
802.1aq
draft-ietf-isis-ieee-aq-05.txt
IEEE 802.1
IETF IS-IS WG
Main Project, IEEE Experts
Ethernet, Data Plane
BPDU and IS-IS extensions
IS-IS TLVs, Expert Review
and Code point allocation
Common
Authors
Demonstration of Implementation
Interoperability
Co-operation
synch

## Slide 3: 802.1aq (SPBm) Interop's
July 18
IEEE Plenary San Francisco
IEEE 802.1
3
1st Interop was 2010 Avaya/Huawei
  Simple control plane/data/.1ag – 5 nodes.
  Report available via the wikipedia 802.1aq page.
2nd Interop was in January 2011 Avaya/Huawei
  Full data plane/control/.1ag – 9 nodes including VM moves (report pending..)
3rd Interop was in June 2011 Avaya/Huawei/ALU
  Full control plane/ some .1ag – 187 nodes and 412 links
4th Interop will be in a few months

## Slide 4: Third Interop Summary (SPBM)
July 18
IEEE Plenary San Francisco
IEEE 802.1
4
Based the IETF draft-05 with current IANA code point allocations and the IEEE D4.0 – June 2011.
Focus on SPBM mode
Brought together 5 vendors products representing 6 independent implementations.
10 real switches
1 high end tester
1 passive network viewer (via NNI)
1 LINUX/Quagga emulator.
Built a IS-IS SPB network with 187 nodes and 412 links.

## Slide 5: Actual TLV’s Tested
These are the proper IANA code points

## Slide 6: Simulate a Large Network
July 18
IEEE Plenary San Francisco
IEEE 802.1
5
<ottawa-s9300-6>d spb status
SPB Status:
mode SPBM, nodes 187, links 412, adj 6, ufib 372, mfib 45

## Slide 7: Viewer –via passive NNI - Solana
July 18
IEEE Plenary San Francisco
IEEE 802.1
6
Implemented the hello protocol.
Passive Llsten to the IS-IS LSP’s Draw the topology they see.
Automatic network drawing layout.

## Slide 8: Network emulator - Spirent
July 18
IEEE Plenary San Francisco
IEEE 802.1
7
Formed 3 SPBM Adjacencies. Inject various topologies including ISIDs info.
Injected packets with PBB encapsulation.
Also used as Customer test point for ISID.
Spirent SPB

## Slide 9: Network emulator - Quagga
July 18
IEEE Plenary San Francisco
IEEE 802.1
8
Linux/Laptop Modified Quagga ISIS+Java
Draw picture & inject/change
Quagga

## Slide 10: Physical Network
July 18
IEEE Plenary San Francisco
IEEE 802.1
9

## Slide 11: Physical topology
July 18
IEEE Plenary San Francisco
IEEE 802.1
10
S9303-1
S9303-2
S9303-3
S9303-4
ERS-6
omniswitch
S9303-5
S9303-6
S9303-7
S9303-8
SPIRENT
QUAGGA
SOLANA
PC
PC
uni
uni
uni
ISID 1000
ISID 1000
ISID 1000
ISID 1000
ISID 1000
ISID 1000

## Slide 12: Link State Database
July 18
IEEE Plenary San Francisco
IEEE 802.1
15
<ottawa-s9300-6>d isis lsdb
Database information for ISIS(1)
--------------------------------
Level-1 Link State Database
LSPID Seq Num Checksum Holdtime Length ATT/P/OL
-------------------------------------------------------------------------------
0001.0000.0001.00-00 0x00000066 0xd16 648 202 0/0/0
...
Instance_2.00-00 0x000000b6 0xa06e 850 209 0/0/0
Instance_3.00-00 0x000000b6 0x85c4 313 269 0/0/0
Instance_4.00-00 0x000000b4 0xcd4f 811 239 0/0/0
Instance_5.00-00 0x000000b6 0xe9e9 1002 275 0/0/0
ERS-6.00-00 0x000001e9 0x28d5 694 324 0/0/0
omniswitch.00-00 0x00000085 0xb9bf 839 176 0/0/0
s9303-1.00-00 0x00000143 0x8961 717 162 0/0/0
s9303-2.00-00 0x0000036f 0x1714 715 219 0/0/0
s9303-3.00-00 0x00000311 0xb5ba 727 200 0/0/0
s9303-4.00-00 0x0000035a 0xbbba 676 219 0/0/0
s9303-5.00-00 0x000003d0 0x7cde 432 183 0/0/0
s9303-6.00-00* 0x000003ce 0x81d8 503 202 0/0/0
s9303-7.00-00 0x000003d3 0xff18 889 183 0/0/0
s9303-8.00-00 0x0000016d 0x15cc 1015 145 0/0/0
Spirent
Quagga
Alu
Huaweii
Avaya
Solana is passive so no LSP

## Slide 13: Filtering Database
July 18
IEEE Plenary San Francisco
IEEE 802.1
16
ERS-6:3/show/isis/spbm# unicast-fib
*******************************************************************************
Command Execution Time: THU JUN 30 12:04:29 2011 UTC
*******************************************************************************
================================================================================
SPBM UNICAST FIB ENTRY INFO
================================================================================
DESTINATION BVLAN SYSID HOST-NAME OUTGOING COST
ADDRESS INTERFACE
--------------------------------------------------------------------------------
00:01:00:00:00:03 40 0001.0000.0003 NULL 2/18 70
..
00:55:66:77:10:05 41 0055.6677.1005 Instance_5 2/20 40
00:e0:b1:e7:0b:d3 40 00e0.b1e7.0bd3 omniswitch 2/4 100
00:e0:b1:e7:0b:d3 41 00e0.b1e7.0bd3 omniswitch 2/4 100
44:55:66:77:00:01 40 4455.6677.0001 s9303-1 2/20 20
44:55:66:77:00:01 41 4455.6677.0001 s9303-1 2/20 20
44:55:66:77:00:02 40 4455.6677.0002 s9303-2 2/20 20
44:55:66:77:00:02 41 4455.6677.0002 s9303-2 2/20 20
44:55:66:77:00:03 40 4455.6677.0003 s9303-3 2/20 20
44:55:66:77:00:03 41 4455.6677.0003 s9303-3 2/20 20

## Slide 14: Multicast FDB
July 18
IEEE Plenary San Francisco
IEEE 802.1
20
ERS-6:3/show/isis/spbm# multicast-fib
*******************************************************************************
Command Execution Time: THU JUN 30 12:08:33 2011 UTC
*******************************************************************************
================================================================================
SPBM MULTICAST FIB ENTRY INFO
================================================================================
MCAST DA ISID BVLAN SYSID HOST-NAME OUTGOING-INTERFACES
--------------------------------------------------------------------------------
23:00:0e:00:03:e8 1000 40 0001.0000.000e NULL 2/20,2/2
...
03:00:06:00:03:e8 1000 40 00be.b000.0600 ERS-6 2/18,2/20,2/4,2/2
03:00:06:00:03:e9 1001 41 00be.b000.0600 ERS-6 2/18,2/20,2/4,2/2
73:0b:d3:00:03:e8 1000 40 00e0.b1e7.0bd3 omniswitch 2/18,2/20,2/2
73:0b:d3:00:03:e9 1001 41 00e0.b1e7.0bd3 omniswitch 2/18,2/2
73:00:01:00:03:e8 1000 40 4455.6677.0001 s9303-1 2/18,2/4,2/2
73:00:01:00:03:e9 1001 41 4455.6677.0001 s9303-1 2/18,2/2

## Slide 15: Shortest Path Next hop
July 18
IEEE Plenary San Francisco
IEEE 802.1
17
6900-X40-A2_14_2_3-> show ip isis spf
==================================================================
ISIS Path Table
==================================================================
Node Interface Nexthop
------------------------------------------------------------------
0001.0000.0001.00 1/3 0010.9400.0001
0001.0000.0002.00 1/3 0010.9400.0001
0001.0000.0003.00 1/3 0010.9400.0001
....
4455.6677.011a.00 1/2 00be.b000.0600
4455.6677.011b.00 1/2 00be.b000.0600
4455.6677.1008.00 1/2 00be.b000.0600
4455.6677.1009.00 1/1 4455.6677.0004
4455.6677.100a.00 1/2 00be.b000.0600
4455.6677.100b.00 1/2 00be.b000.0600
4455.6677.100c.00 1/1 4455.6677.0004
------------------------------------------------------------------
SPF count: 185
=================================================================

## Slide 16: Route query for two ECT-ALGORITHMS.
July 18
IEEE Plenary San Francisco
IEEE 802.1
18
S9303-1
S9303-2
S9303-3
S9303-4
ERS-6
omniswitch
S9303-5
S9303-6
S9303-7
S9303-8
SPIRENT
QUAGGA
SOLANA
PC
PC
uni
uni
uni
ISID 1000
ISID 1000
ISID 1000
ISID 1000
<ottawa-s9300-6>d spb uroute s9303-1 omniswitch vlan 40
PATH:
s9303-1 -> s9303-6 -> ERS-6 -> omniswitch
<ottawa-s9300-6>d spb uroute s9303-1 omniswitch vlan 41
PATH:
s9303-1 -> s9303-7 -> s9303-4 -> omniswitch
<ottawa-s9300-6>
ISID 1000

## Slide 17: Route query for distant nodes
July 18
IEEE Plenary San Francisco
IEEE 802.1
19
<ottawa-s9300-6>d spb uroute s9303-1 Instance_22 vlan 40
PATH:
s9303-1 -> s9303-6 -> Instance_2 -> Instance_3 -> Instance_8 -> Instance_14 -> Instance_24 -> Instance_23 -> Instance_22
<ottawa-s9300-6>d spb uroute s9303-1 Instance_22 vlan 41
PATH:
s9303-1 -> s9303-7 -> Instance_4 -> Instance_5 -> Instance_8 -> Instance_14 -> Instance_24 -> Instance_23 -> Instance_22
S9303-1
S9303-2
S9303-3
S9303-4
ERS-6
omniswitch
S9303-5
S9303-6
S9303-7
S9303-8
SPIRENT
QUAGGA
SOLANA
PC
PC
uni
uni
uni
ISID 1000
ISID 1000
ISID 1000
ISID 1000
ISID 1000

## Slide 18
July 18
IEEE Plenary San Francisco
IEEE 802.1
12
<ottawa-s9300-6>d spb status
SPB Status:
mode SPBM, nodes 187, links 412, adj 6, ufib 372, mfib 45
Collision:
<ottawa-s9300-6>
<ottawa-s9300-6>d isis peer
Peer information for ISIS(1)
System Id Interface Circuit Id State HoldTime Type PRI
-------------------------------------------------------------------------------
s9303-1 GE1/0/10 0000000002 Up 23s L1 --
s9303-2 GE1/0/11 0000000004 Up 25s L1 --
s9303-3 GE1/0/12 0000000002 Up 29s L1 --
s9303-4 GE1/0/13 0000000003 Up 27s L1 --
Instance_2 GE1/0/14 005 Up 26s L1 --
ERS-6 GE1/0/24 0825505536 Up 23s L1 --
Total Peer(s): 6
Huawei “S9303”

## Slide 19
July 18
IEEE Plenary San Francisco
IEEE 802.1
13
ERS-6:3# show isis adj
*******************************************************************************
Command Execution Time: THU JUN 30 11:36:15 2011 UTC
*******************************************************************************
================================================================================
ISIS Adjacencies
================================================================================
INTERFACE L STATE UPTIME PRI HOLDTIME SYSID HOST-NAME
--------------------------------------------------------------------------------
Port2/18 1 UP 18:24:49 127 25 0010.9400.0008 (null)
Port2/19 1 UP 04:27:27 127 29 4455.6677.0005 s9303-5
Port2/20 1 UP 04:25:41 127 28 4455.6677.0006 s9303-6
Port2/4 1 UP 14:39:30 127 21 00e0.b1e7.0bd3 omniswitch
--------------------------------------------------------------------------------
4 out of 4 interfaces have formed an adjacency
--------------------------------------------------------------------------------
Avaya “ERS-6”

## Slide 20
July 18
IEEE Plenary San Francisco
IEEE 802.1
14
6900-X40-A2_14_2_3-> show ip isis adjacency
=======================================================================================
ISIS Adjacency
=======================================================================================
System ID Type State Hold Interface Hostname
---------------------------------------------------------------------------------------
4455.6677.0004 L1 UP 27 1/1 s9303-4
00be.b000.0600 L1 UP 25 1/2 ERS-6
0010.9400.0001 L1 UP 28 1/3 None
---------------------------------------------------------------------------------------
Adjacency : 3
=======================================================================================
ALU “omniswitch”

## Slide 21: Compliance points
July 18
IEEE Plenary San Francisco
IEEE 802.1
21
Bridge Priority
Test > 2 ECT (but should be easy)
Do more adjacency rejection tests
MIBs?
More .1ag tests

## Slide 22: Recommended but not required for compliance
July 18
IEEE Plenary San Francisco
IEEE 802.1
22
Be nice to have Default B-VIDs/ECT mappings. I.e Best Common Practice eg: 4000-4015 as default set?
Align SpSouceID’s, MEPID’s.
Hostname very useful, if not set by user suggest (ASCI of your OUI) + instance.

## Slide 23: Next Steps
July 18
IEEE Plenary San Francisco
IEEE 802.1
23
Tata has offered to host 4th Interop in NJ and offered use of a transatlantic link.
More in depth.1ag tests
IETF interop informational but want to use also to recommend good practices (BCP).
Perhaps test the MIBs?

## Slide 24: Thank-you
July 18
IEEE Plenary San Francisco
IEEE 802.1
24
Edgard, Peter, John, Stephane, Bis & Rup (not shown)... and many others of course in 3 different countries.