## Slide 1: Possible TRILL Use of GENAPP in draft-ietf-trill-rbridge-channel
Donald E. Eastlake, 3rd
Huawei Technologies (USA)
d3e3e3@gmail.com

## Slide 2: Possible TRILL Use of GENAPP
draft-ietf-trill-rbridge-channel, if approved in its current form
  allocates a GENAPP ID for TRILL to conserve other IDs
  specifies an APPsub-TLV for use in the instance zero LSP to announce support of RBridge channel protocols
The RBridge channel facility is used to support TRILL OAM
If use of GENAPP is not approved, this will be changed to a Router Capabilities sub-TLV.

## Slide 3: OAM Layers
Router
Bridge
RBridge
RBridge
P = Ports and Fast Path Logic
ET = Ethernet stack possibly with 802.1ag OAM = Green
TR = TRILL protocol stack including TRILL OAM = Red
IP = IP protocol stack including Layer 3 OAM = Black
P
P
P
P
ET
IP
TR
TR
ET
Router
P
ET
IP
RBridge
P
TR
ET
ET
ET
ET
ET
ET

## Slide 4: Three Drafts
Channel Draft provides a communications path for inter-RBridge messages
BFD draft provides BFD Control and BFD Echo
RBridge OAM draft provides ICMP like facilities (ping, echo, error reporting)
1. RBridge Channel
3. RBridge OAM
2. BFD for TRILL

## Slide 5: An RBridge Channel
RBridge Channel Frames are TRILL Data Frames:
The Rbridge Channel Message Header & Payload:
Link Header
TRILL Header
Channel Header
Channel Data
Link Trailer
All-Egress- RBridges
Inner
MacSA
RBridge-Channel
Ethertype
Flags, Channel Protocol #
Channel Protocol Data

## Slide 6: An RBridge Channel Message
0 = Silent
1 = Multi-Hop
2 = Native
3 - 11 available
1 = RBridge Channel Error
2, 3 = BFD Control, Echo
3, 4 = TRILL Echo, Error
5 – 4,094 available
12 bits of Channel Header Flags
12 bit Channel Protocol Number
4 bit Channel Version = 0
4 bit ERR Code
All-Egress- RBridges
Inner
MacSA
RBridge-Channel
Ethertype
Flags, Channel Protocol #
Channel Protocol Data

## Slide 7: Channel Protocols Supported APPsub-TLV
Format of proposed APPsub-TLV
  Support of RBridge Channel protocols is consider to be a vector of bits numbered 0 through 4,094, defaulting to zero where a 1 bit indicates support
APPsub-Type = 1
Length
Bit
Vectors
| 0 1 2 3 4 5 6 7| 8 9 10 11 12 13 14 15|
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| Bit Vector Length | Bit Vector Offset |
+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+--+
| bits
+--+--+--...

## Slide 8: Channel Protocols Supported APPsub-TLV
Low volatility
  Support of channel protocols probably changes only on software upgrade or the like
Expected size: < 12 bytes
  1 GENAPP Type
  1 GENAPP Length
  2 TRILL GENAPP ID
  7 Example value
    3 A bit vector encoding of one byte of bits
    4 A bit vector encoding of two bytes of bits

## Slide 9: END
Donald E. Eastlake, 3rd
Huawei Technologies (USA)
d3e3e3@gmail.com