## Slide 1: IS-IS Extensions to support OTV
Hasmit Grover
Ayan Banerjee
Dhananjaya Rao

## Slide 2: Overlay Transport Virtualization
OTV is a L2/L3 Virtualization Solution for Enterprise environments
Transparent L2 extension for enterprise sites
L2 and/or L3 connectivity for site devices
Multi-site multi-point connectivity
Extremely simple provisioning and management

## Slide 3: Overview
MAC Routing
  Uses control plane advertisements instead of data plane learning
  Remote site MACs learnt via control plane
  No unknown unicast flooding
Inter-site data sent as IP packets
  Routed to destination Edge Devices
  No pre-built tunnels
STP terminated at each site

## Slide 4: Overview
OTV forms an overlay network
  Auto-discovery
  Unicast/multicast route exchange
OTV functionality only in edge devices
  Transparent to core and site devices
Core transport agnostic

## Slide 5
Overlay Network
Core
Network
VPN B
Site 3
VPN B
Site 2
VPN B
Site 1
VPN A
Site 3
VPN A
Site 2
VPN A
Site 1
VPN
Overlay B
pUMRP
cUMRP
cUMRP
cUMRP
pSTP/Snoop
cSTP/Snoop(1)
cSTP/Snoop(2)
cSTP/Snoop(3)
oUMRP
In core:
- No flooding of site L2 data
- No coordinated site state for L2 or L3
- No coordination between core and site
On the overlay:
- oUMRP carries unicast/multicast MAC addresses
- Use IP multicast in core for control and data to all
sites of a given VPN
- Packets sent on overlay are encapsulated in IP
X
X
Edge Devices
X
Legend:
red: L2
green: L3
UMRP: Unicast/Multicast
Routing Protocol

## Slide 6: Data Forwarding
Unicast packets encapsulated and routed to overlay “next-hop”
  Load-balancing and ECMP across core and overlay
Multicast uses Delivery Groups across core
  Data sent within (DS,DG) by source Edge Devices
  Optimal multicast replication by core network
Broadcast data sent as IP multicast
  All Edge Devices join this core multicast tree

## Slide 7: Multi-homing
OTV provides loop-free multi-homing
Authoritative Edge Device (AED) per site
  Edge Devices in the site elect AED
Only AEDs forward traffic on overlay
  Avoids loops and duplicates
Traffic load-balanced among Edge Devices
  Per-VLAN AED

## Slide 8: Overlay Routing Protocol
IS-IS used as oUMRP
  Edge Devices run IS-IS at L2 on overlay
  Provides auto-discovery and authentication
  Carries both unicast and multicast routes
Easily extensible
Leverage existing Layer-2 IS-IS extensions
Operational benefits of using one protocol

## Slide 9: IS-IS extensions
Protocol packet extensions
  TLVs, sub-TLVs, PDUs
No major changes to protocol behavior
IS-IS on overlay uses LAN procedures

## Slide 10: IIH extensions
Multi-Topology aware Port Capability defined in RFC 6165
Define new sub-TLVs
  Site Capability
  Site Group IPv4
  Site Group IPv6
  Adjacency Server IPv4
  Adjacency Server IPv6

## Slide 11: LSP Extensions
Group Address TLV defined in RFC 6326
Define new sub-TLVs
  Group IPv4 Address
  Group IPv6 Address
Group Membership Active Source TLV (new)
Define Sub-TLVs
  Group MAC Source
  Group IPv4 Source
  Group IPv6 Source

## Slide 12: MGroup PDU
Multicast Group PDU
  Carries multicast specific information
  MGroup CSNP
  MGroup PSNP

## Slide 13: I-Ds
Overlay Transport Virtualization
  http://www.ietf.org/id/draft-hasmit-otv-03
IS-IS Extensions to support OTV
  http://tools.ietf.org/html/draft-drao-isis-otv-00

## Slide 14: Next Step
Authors would like to solicit comments and feedback