## Slide 1: draft-ram-l2vpn-ldp-vpls-etree-2pw-02
IETF 81 Jul 2011
Rafi Ram (rafir@orckit.com)
Daniel Cohn (danielc@orckit.com)
Raymond Key (raymond.key@team.telstra.com)
Puneet Agarwal (pagarwal@broadcom.com)

## Slide 2: Background
This draft addresses the E-Tree requirement for leaf-to-leaf communication restriction
To comply with this requirement, the draft proposes using a pair of PWs (root and leaf) to interconnect core VPLS PEs
  Traffic originated in root AC is forwarded over root PW
  Traffic originated in leaf AC is forwarded over leaf PW

## Slide 3: Updates (1)
Instead of defining new VSI types to identify root and leaf PWs (-00), a new PW interface parameter called VSI E-Tree Type is defined
  To identify root and leaf PWs in the same logical VSI interface (identified by FEC in -00), a new PW interface parameter called VSI E-tree Identifier is defined

## Slide 4: Updates (2)
New parameters are encoded as interface parameters sub-TLVs (section 5.5. of RFC 4447), as follows:
VSI E-tree Type can take the following values:
  0: E-Tree Root VSI
  1: E-Tree Leaf VSI
VSI E-tree Identifier is a 32-bit number that is used to identify a pair of root and leaf PW as part of the same logical VSI interface, in the context of a pair of VPLS PEs.

## Slide 5: Next Steps
Incorporate input into new revision
Attempt to harmonize with other proposals

## Slide 6: Thank You
Questions ? Comments ?