## Slide 1: Node redundancy provisioning for VPLS Inter-domain
draft-liu-l2vpn-vpls-inter-domain-redundancy-00
Zhihua Liu, China Telecom
Lizhong Jin, ZTE
Ran Chen, ZTE
<number>
L2VPN IETF81
Notes: <number>

## Slide 2: Motivation
Current: Inter-AS VPLS redundancy could be provided by MC-LAG:
  VSI-to-VSI connections at the ASBR;
  The interconnected link between the two providers should be Ethernet link.
Why Inter-AS VPLS redundancy should be provided by PW redundancy?
  The interconnected link is POS (Packet over Sonet/SDH) link.
  Control bandwidth, QoS, MAC address and Broadcast/Multicast traffic.
<number>

## Slide 3: Introduction
Informational draft
Draft includes:
  Recommended deployment scenario of inter-domain VPLS redundancy
  Specific MAC withdraw procedure
  Load balancing
<number>

## Slide 4: Deployment scenario
From the operator's point of view, one operator will not highly rely on the other operator's technical choice for inter-domain VPLS node redundancy.
Why ICCP, instead of STP on ASBRs to avoid loop?
  Fast convergence
  Easy to control active/standby PW, so as to deploy load balance.
<number>
ASBR1
ASRB2
ASBR3
ASBR4
VSI
VSI
VSI
VSI
PE2
VSI
PE1
VSI
Active PW
Standby PW

## Slide 5: Deployment Recommendation
Recommended deployment scenario
  ICCP deployment option: ICCP is deployed on VPLS edge nodes (on ASBR in the figure) in both domain;
  PW redundancy mode: independent only.
Before deploying, the operator MUST negotiate to configure same PW priority at two PW end-points.
  To ensure the same active/standby negotiated state at two PW end-points.
<number>

## Slide 6: MAC Withdraw procedure
That means PE SHOULD not advertise MAC Address Withdraw message from one domain to the other.
  If not, the MAC address withdraw message with empty list originated from one domain would lead to a VPLS in another domain, to flush all MAC addresses which is not necessary, and bring potential network instability.
<number>

## Slide 7: Load Balancing
Load balancing among VPLS instance:
  Configure different PW priority values for different VPLS instance;
  The active PW of different VPLS will be running on different PEs, to provide load balancing between the two PEs in one domain.
<number>

## Slide 8: Next steps
Need comments from work group
Thank you
<number>