## Slide 1: VPLS PE Model with E-Tree Support
<number>
81th IETF - Quebec
Yuanlong Jiang (yljiang@huawei.com)
Lucy Yong (lucyyong@huawei.com)
Manuel Paul (manuel.paul@telekom.de)
Frederic Jounay (frederic.jounay@orange-ftgroup.com)
draft-jiang-l2vpn-vpls-etree-pe-04.txt
Notes: <number>

## Slide 2: Backgrounds
<number>
81th IETF - Quebec
E-Tree Requirements in multiple SDOs
  Service Definition: MEF 6.1, MEF 10.2
  Mobile backhaul: MEF 22
  Broadband Network Architecture: BBF WT-145
  MPLS in Carrier Ethernet: BBF WT-224
  MPLS in Mobile Backhaul: BBF WT-221
Lack of E-Tree support in VPLS standard
  Non-standard mechanism for single root topology
    Single VSI + extended split horizon mechanism
  No VPLS support for multi-roots topology
    Multiple nodes with root & leaf attached in a single domain
    Multiple roots and leaves located diversely across multiple domains
Notes: <number>

## Slide 3: E-Tree Solution in Ethernet
<number>
MEF E-Tree service model
  A UNI MUST be designated as Root or Leaf
  Forwarding rule at Root UNI and Leaf UNI are different
IEEE uses a pair of S-VLAN IDs - Trunk S-VLAN ID and Branch S-VLAN ID to support generic E-Tree, which is incorporated in the latest IEEE 802.1Q standard
UNI
Root
Leaf
Root
Leaf
MEN A
UNI
UNI
UNI
The green arrows show the forwarding of frames originated at a Leaf UNI
The red arrows show the forwarding of frames originated at a Root UNI
81th IETF - Quebec
Notes: <number>
http://www.ieee802.org/1/files/public/docs2010/liaison-rooted-multipath-vids-0310-v03.pdf
http://www.ieee802.org/1/files/public/docs2010/liaison-nfinn-split-horizon-vid-filtering-0710-v04.pdf
http://www.ieee802.org/1/files/private/aq-drafts/d4/802-1aq-D4-0.pdf

## Slide 4: VLAN Based E-Tree Solution in VPLS
<number>
81th IETF - Quebec
R
L
Bridge
Module
Root
PW
CE1
Root AC
PW
Leaf
Bridge
Module
PE1
PE2
Root
Leaf
L
R
2. Both VLANs connected
into a single VSI
PE3
CE2
CE3
CE4
CE5
NSP
VPLS
L
T-VSI
T-VSI
T-VSI
NSP: Native Service Processing
PW
1. Eth. frames tagged with Root or Leaf VLAN
Leaf AC
Root AC
Leaf AC
Leaf AC
3. Both VLANs carried
in the same PW
4. Egress filtering based on VLAN

## Slide 5: Global VLAN based provisioning
<number>
81th IETF - Quebec
R
L
Bridge
Module
Root
PW
CE1
PW
Leaf
Bridge
PE1
PE2
Root
Leaf
L
R
PE3
CE2
CE3
CE4
CE5
NSP
VPLS
L
T-VSI
T-VSI
T-VSI
PW
Global VLAN across VPLS
Global VLAN across VPLS

## Slide 6: Local VLAN based provisioning
<number>
81th IETF - Quebec
R
L
Bridge
Module
Root
PW1
CE1
PW2
Leaf
Bridge
PE1
PE2
Root
Leaf
L
R
PE3
CE2
CE3
CE4
CE5
NSP
VPLS
L
T-VSI
T-VSI
T-VSI
PW3
Auto-negotiation of
VLAN mapping
(i/f parameter from peer PE)
PE2 performs VLAN mapping on the frames from/to PW2
PE3 performs VLAN mapping on the frames from/to PW1 & PW3
Notes: All PEs capable of VLAN mapping
IP address: PE3 < PE2 < PE1

## Slide 7: Benefits
<number>
81th IETF - Quebec
Reusing E-Tree solution in Ethernet
  Data plane of bridge module is the same as in Ethernet
  Data plane of VSI is the same as in traditional VPLS
  No change in PW layer semantics
A single unified solution
  Applicable to both “VPLS only” and “VPLS-Ethernet interworking” scenarios
  Applicable to all known VPLS PE models
Scalability
  only a single VSI and a single suite of PWs needed
  Redundant PWs are avoided
Notes: <number>

## Slide 8: Changes in draft-04
<number>
81th IETF - Quebec
Data plane operation simplified
  Add or translate VLAN tag only once for each frame upon arrival
  Only one E-tree service per T-VSI, thus no need for (PW, VLAN) lookup in the reverse direction
VLAN manipulation simplified
  3 different ways described in version-03
  Now summarized into “Global VLAN based” and “Local VLAN based”
Tagged Mode as well as Raw Mode PW may be used to carry E-Tree service
Quite a few other improvements on texts and diagrams

## Slide 9: Questions
<number>
81th IETF - Quebec
Any other concerns unresolved?
Could this be accepted as WG draft?

## Slide 10
<number>
81th IETF - Quebec
Thank You
Notes: <number>