## Slide 1: draft-sajassi-l2vpn-pbb-evpn-02.txt
Ali Sajassi (Cisco), Nabil Bitar (Verizon), Aldrin Issac (Bloomberg), Samer Salam (Cisco), Sami Boutros (Cisco), Florin Balus (ALU), Wim Henderickx (ALU), Clarence Filsfils (Cisco), Dennis Cai (Cisco)
July 28th, 2011
IETF Quebec City

## Slide 2: Additional Requirements (PBB-EVPN)
MAC Advertisement Route Scalability
  To support millions of C-MAC addresses (million of VMs)
C-MAC Mobility with MAC sub-netting
  Support C-MAC address mobility while retaining the scalability benefits of MAC sub-netting
C-MAC Address Learning and Confinement
  MES nodes to maintain C-MAC addresses in their RIB & FIB for active flows ONLY

## Slide 3: Additional Requirements (PBB-EVPN)
Interworking with TRILL & 802.1aq/.1Qbp networks and C-MAC Transparency
  To avoid learning of C-MACs by DC WAN Edge PE
Per Site Policy
  To support connectivity policy rules at the granularity of a site (or segment)
Avoiding C-MAC flushing
    To avoid C-MAC flushing upon link, port, or node failure for multi-homed devices
Avoid transient loop for known unicast when doing egress MAC lookup

## Slide 4: Solution Overview
Advertise local B-MAC addresses in BGP to all other PEs that have at least one VPN in common just like E-VPN
Build a forwarding table from remote BGP advertisements just like E-VPN (e.g., association of B-MAC to MPLS labels)
PEs perform PBB functionality just like PBB-VPLS
  C-MAC learning for traffic received from ACs and C-MAC/B-MAC association for traffic received from core
PE2
PE1
PE3
LACP
CE1
CE2
MPLS
BE B
BE B
<- E-VPN |PBB ->
<- PBB|E-VPN ->
Single B-MAC to represent site ID
can derive the B-MAC automatically from system MAC address of LACP
B-MAC = Site ID

## Slide 5: Advantages
MAC Advertisement Route Scalability
  A single B-MAC represents a multi-homed site
  A single B-MAC can represent all single-homed sites
  A single C-MAC represents a single VM
  => several order of magnitude difference between C-MAC & B-MAC
C-MAC Mobility with MAC sub-netting
  Typically C-MACs are not managed and thus can not be sub-netted
  B-MACs on the other hand are always managed and can easily be sub-netted
  Even when C-MACs are sub-netted, VM mobility contradicts the effect of sub-netting

## Slide 6: Advantages – Cont.
C-MAC Address Learning and Confinement
  With C-MAC learning in control plane, C-MACs are always in RIBs and maybe also in FIBs
  With C-MAC learning in data plane, C-MACs are never in RIBs and they are only present in FIBs for active flow.
Interworking with TRILL & 802.1aq/.1bp networks and C-MAC Transparency
    PBB encapsulation enables end-to-end tunneling of C-MAC addresses for the access networks thus avoiding termination and learning by DC WAN Edge PE

## Slide 7: Advantages – Cont.
Per Site Policy
  Since B-MAC addresses are per site, BGP policy per MAC gives us very nice set of per-site policy
Avoiding C-MAC flushing
    Since B-MAC represent a site, a link, port, or node failure doesn’t change the B-MAC address – it only changes number of next hop for that B-MAC
Avoid transient loop for known unicast when doing egress MAC lookup
  Since B-MAC SA is always transmitted with every frame, checking of every frame against its source MAC SA for known unicast frame is already provided by PBB

## Slide 8: BGP Encoding
Ethernet A-D is not needed and it is not used
  Avoids different modes of operation associated with this route
  Simplifies operation and provisioning
MAC Mobility Extended Community (delta to rev 01)
  It is a transitive extended community
  When advertised with a B-MAC route, it signals all the C-MAC forwarding tables associated with the I-SIDs corresponding to the RTs should be flushed

## Slide 9: Network Multi-Homing: Active/Active Per VLAN Load-Balancing
Each MES advertises two MAC routes per Ethernet Segment: one with high Local Pref for active VLANs, and another with low Local Pref for standby VLANs.
  Use MES RD with LSBit reset (Standby) or set (Active) to differentiate the prefixes.
Remote MES installs the route with higher local pref into FIB for associated B-MAC.
MES1 MAC Routes:
  Route 1: RD11, B-MAC1, RT1, RT3, RT5, Local Pref = High
  Route 2: RD12, B-MAC1, RT2, RT4, RT6, Local Pref = Low
MES2 MAC Routes:
  Route 1: RD22, B-MAC1, RT1, RT3, RT5, Local Pref = Low
  Route 2: RD21, B-MAC1, RT2, RT4, RT6, Local Pref = High
MES1
MES2
VLAN 1,3,5
VLAN 2,4,6
ESI1, B-MAC1
MES3
VPN | B-MAC | NH | Pref
RT1 | B-MAC1 | MES1 | High
RT1 | B-MAC1 | MES2 | Low
RT2 | B-MAC1 | MES1 | Low
RT2 | B-MAC1 | MES2 | High
L2RIB
VPN | B-MAC | NH
RT1 | B-MAC1 | MES1
RT2 | B-MAC1 | MES2
L2FIB

## Slide 10: Future Considerations
ARP suppression
Anything else ?