## Slide 1: Update on LDP Extensions for Optimized MAC Address Withdrawal in H-VPLS draft-ietf-l2vpn-vpls-ldp-mac-opt-04
Geraldine Calvignac (geraldine.calvignac@orange-ftgroup.com)
Olen Stokes (ostokes@extremenetworks.com)
Pranjal Kumar Dutta (pranjal.dutta@alcatel-lucent.com)
Florin Balus (florin.balus@alcatel-lucent.com)

## Slide 2: Background - draft-ietf-l2vpn-vpls-ldp-mac-opt
Optimize, extend LDP MAC Flush to address existing LDP VPLS deployments, including PBB-VPLS use cases
Two components
  New “flush-all-from-me” procedure to minimize the MAC re-learning and unknown unicast flooding
  Required extensions for PBB VPLS
IETF-79 presentation proposed to consolidate some procedures
  Re-use MAC Flush TLV to address also the HVPLS use case (A/S PW access)
Notes: <number>

## Slide 3: Background - draft-ietf-l2vpn-vpls-ldp-mac-opt (cont.)
* PE-ID TLV procedure may result in PE-rs overloading and slower convergence due to additional LDP MAC Flush propagation in PE-rs
** PW Access – MTU multi-homed to VPLS PEs via A/S PWs
*** Ethernet Access multi-homed to VPLS PEs (Ethernet access multi-homing example - ICCP, MC-LAG, BGP MH, G.8032 rings)
Applicability | PW Access** | Ethernet Access*** | PBB-VPLS extensions
MAC Flush TLV |  |  | 
PE-ID TLV* |  |  | 
Notes: draft-ietf-l2vpn-vpls-ldp-mac-opt-02 – submitted for IETF-78
  Added draft-balus-l2vpn-pbb-ldp-ext-02 text as agreed in IETF-77
    PBB VPLS extensions – propagate CMAC flush transparently through the B-VPLS; avoid unnecessary BMAC flushing
  Existing enhancements apply also to PBB-VPLS
<number>

## Slide 4: Changes in version 04
Added a brief description of Ethernet access use case
Consolidated text in the solution section - PE-ID TLV procedure removed
Fixed wording throughout the document
Notes: draft-ietf-l2vpn-vpls-ldp-mac-opt-02 – submitted for IETF-78
  Added draft-balus-l2vpn-pbb-ldp-ext-02 text as agreed in IETF-77
    PBB VPLS extensions – propagate CMAC flush transparently through the B-VPLS; avoid unnecessary BMAC flushing
  Existing enhancements apply also to PBB-VPLS
<number>

## Slide 5: Next steps
Incorporate WG feedback on some of the wording for backwards compatibility/emulating RFC 4762 procedure
Draft ready for LC?
Notes: <number>

## Slide 6: MAC Optimization benefits
  Flush-all-from-me benefit: optimized MAC Flush, less flooding - flush only the MACs associated with PW13
M1
ALL other MACs in the FIB
  Flush-all-but-mine (RFC4762): flush all the MACs except the MACs learned from PE2
ALL other MACs in the FIB
M2
IP/MPLS
PE1
MTU/CE
PE2
PE3
NTU
VSI
VSI
VSI
Primary PW
Standby PW
1. PW failure
  X
PW12
PW23
PW13
M1
M2

## Slide 7: Old PE ID TLV based solution for “flush-all-from-me”
IP/MPLS
PE1
MTU
PE2
PE3
NTU
VSI
VSI
VSI
Primary PW
Standby PW
1. PW failure
4. Flush only MACs learned over PW13
  X
1. T-LDP MAC Withdraw with PE-ID1 TLV
PW12
PW23
PW13
3. T-LDP MAC Withdraw with PE-ID1 TLV
M1
Applicable only to HVPLS resiliency using (A/S) PW Access
2. Flush only MACs learned over PW12
M1

## Slide 8: Native Ethernet use case
IP/MPLS
PE1
MTU/CE
PE2
PE3
NTU
VSI
VSI
VSI
Primary
Standby
1. Link failure
  X
PW12
PW23
PW13
  Solution expanded to address the native Ethernet access
  Applicable to any non-STP based resiliency scheme – ICCP, MC-LAG, BGP MH, G.8032
Ethernet Access

## Slide 9: MAC TLV based solution for “flush-all-from-me”
IP/MPLS
PE1
MTU/CE
PE2
PE3
NTU
VSI
VSI
VSI
Primary
Standby
1. Link failure
2. Flush only MACs learned over PW13
  X
PW12
PW23
PW13
1. T-LDP MAC Withdraw (N=1)
1. T-LDP MAC Withdraw (N=1)
M1
2. Flush only MACs learned over PW12
M1
Use the N-Flag from MAC Flush parameters TLV: N=1 indicates “flush-all-from-me” is required – re-uses the method proposed before for PBB-VPLS
Same procedure for both Ethernet and PW Access