## Slide 1: Requirements and Framework of VPN-oriented Data Center Services http://datatracker.ietf.org/doc/draft-so-vdcs/
IETF 81 Quebec City
<number>
Ning So ning.so@verizonbusiness.com
Paul Unbehagen paul.unbehagen@alcatel-lucent.com
Linda Dunbar Linda.dunbar@huawei.com
Henry Yu Henry.yu@twtelecom.com
John M. Heinz john.m.heinz@centurylink.com
Norival Figueira nfigueir@brocade.com
Bhumip Khasnabish vumip1@gmail.com
Notes: <number>

## Slide 2: What Is VDCS
<number>
VPN-oriented Data Center Services (VDCS) are the extensions to the existing L2 and L3 VPN services into cloud data centers and to control the virtual resources sharing functions
  Strictly maintaining the secure, reliable, and logical isolation characteristics of VPN
  Making the data center resources as additional attributes to VPNs
  Allowing end-to-end VPN-based service management
  VPN having the control on how and what data center resources to be associated with the VPN
This draft describes the characteristics of those services, the service requirements, and the corresponding requirements to data center networks.

## Slide 3: VDCS Service Definition and Requirements
<number>
VPN-oriented DC computing services
  Virtual Machines (VMs) and/or physical servers in a virtualized carrier data center being attached to a customer VPN
  Requirements: auto-provisioning, VM and server instantiation and removal, VM migration policy control, VM monitoring
VPN-oriented DC storage services
  disk space, either virtual or actual blocks of hard drives in data centers, being added to a customer’s VPN
  Requirements: content replication control, storage space auto-provisioning, storage migration policy control, content life cycle management

## Slide 4: Other Requirements
<number>
Intra-DC Network Requirements
  Requirements when VPNs are extended into DC using VPN Gateway
    Traffic separation per VPN and per service
    DC virtual resource assignment control and reporting
    Dynamic configuration and provisioning control of DC virtual resources
    QoS support
Virtual Resources Management Requirements
  DC virtual resources include physical servers and VMs, disk spaces, memories, intra-DC network connections and bandwidth.
  Requirements include
    Resource partition and assignment
    Resource accessibility control and management

## Slide 5: Other Requirements
<number>
Security requirements
Auto-configuration requirements
OAM requirements
And etc.

## Slide 6: L3-VDCS Physical Framework – Virtual Machines attached to VPN
Data Center
LAN Switch
VM
User
Desktops
LAN
Switch
CE
Router
VPN Edge Router
User
Desktops
LAN
Switch
CE
Router
VPN Edge Router
User
Desktops
LAN
Switch
CE
Router
VPN Edge Router
User
Desktops
LAN
Switch
CE
Router
VPN Edge Router
IP/MPLS network
Data Center VPN GW Router
Data Center
10.1.x
10.2.x
10.3.x
10.4.x
10.1.200.x
10.2.40.x
10.3.20.x
10.4.100.x

## Slide 7: Logical View of Routing Table at L3VPN Edge Routers
VM
User
Desktops
VPN Edge Router
User
Desktops
VPN Edge Router
User
Desktops
VPN Edge Router
User
Desktops
VPN Edge Router
IP/MPLS network
DC VPN GW Router
Data Center
10.1.200.x
10.2.40.x
10.3.20.x
10.4.100.x
1
3
2
4
10.1.x
10.3.x
10.4.x
10.2.x
IP Address | Next Hop
10.1.200.x | DC VPN GW
10.1.x | VPN ER 1
10.2.20.x | DC VPN GW
10.2.x | VPN ER 2
10.3.20.x | DC VPN GW
10.3.x | VPN ER 3
10.4.100.x | DC VPN GW
10.4.x | VPN ER 4
<number>
IP Address | Next Hop
10.1.200.x | DC VPN GW
10.1.x | VPN ER 1
10.2.20.x | DC VPN GW
10.2.x | VPN ER 2
10.3.20.x | DC VPN GW
10.3.x | VPN ER 3
10.4.100.x | DC VPN GW
10.4.x | VPN ER 4
IP Address | Next Hop
10.1.200.x | DC VPN GW
10.1.x | VPN ER 1
10.2.20.x | DC VPN GW
10.2.x | VPN ER 2
10.3.20.x | DC VPN GW
10.3.x | VPN ER 3
10.4.100.x | DC VPN GW
10.4.x | VPN ER 4
IP Address | Next Hop
10.1.200.x | DC VPN GW
10.1.x | VPN ER 1
10.2.20.x | DC VPN GW
10.2.x | VPN ER 2
10.3.20.x | DC VPN GW
10.3.x | VPN ER 3
10.4.100.x | DC VPN GW
10.4.x | VPN ER 4
IP Address | Next Hop
10.1.200.x | DC VPN GW
10.1.x | VPN ER 1
10.2.20.x | DC VPN GW
10.2.x | VPN ER 2
10.3.20.x | DC VPN GW
10.3.x | VPN ER 3
10.4.100.x | DC VPN GW
10.4.x | VPN ER 4
IP Address | Next Hop
10.1.200.x | DC VPN GW
10.1.x | VPN ER 1
10.2.20.x | DC VPN GW
10.2.x | VPN ER 2
10.3.20.x | DC VPN GW
10.3.x | VPN ER 3
10.4.100.x | DC VPN GW
10.4.x | VPN ER 4
IP Address | Next Hop
10.1.200.x | DC VPN GW
10.1.x | VPN ER 1
10.2.20.x | DC VPN GW
10.2.x | VPN ER 2
10.3.20.x | DC VPN GW
10.3.x | VPN ER 3
10.4.100.x | DC VPN GW
10.4.x | VPN ER 4
IP Address | Next Hop
10.1.200.x | DC VPN GW
10.1.x | VPN ER 1
10.2.20.x | DC VPN GW
10.2.x | VPN ER 2
10.3.20.x | DC VPN GW
10.3.x | VPN ER 3
10.4.100.x | DC VPN GW
10.4.x | VPN ER 4

## Slide 8: L3VDCS Logical View – Virtual Machines attached to VPN
For end users of a VPN client, they see the VMs in data center as if they are co-located with them.
User
Desktops
VPN Edge Router
User
Desktops
VPN Edge Router
User
Desktops
VPN Edge Router
User
Desktops
VPN Edge Router
IP/MPLS network
DC VPN GW Router
1
3
2
4
10.1.x
10.3.x
10.4.x
10.2.x

## Slide 9: Next Steps
<number>
As this drafts gets longer, it may need to be broken into two separate drafts: requirements draft and framework draft
Welcome feedbacks and solution development cooperation
Still looking for a WG for the progression of the work of this draft, and the solution drafts